## Slide 1
Jung-Ah Choi, Cheon Lee, and Yo-Sung Ho
October 13th, 2012
Gwangju Institute of Science and Technology
Throughput Improvement on CABAC for Depth Videos with Modified Level Coding
ISO/IEC JTC1/SC29/WG11
JCT3V-B0123

## Slide 2: Throughput Issue
Key issue of CABAC decoding
  Other processes can be parallelized
  The serial nature of entropy coders
    Bottleneck for overall codec performance
CABAC gives a good coding efficiency, but its throughput remains a challenge
  CABAC: ~ 1 bin/cycle
  CAVLC: at least one codeword/cycle

## Slide 3: Two Coding Modes in CABAC
Regular coding mode (≡ context-coded bin)
  LPS value and LPS probability of each bin are estimated by a predetermined context model
  Each bin is encoded by binary arithmetic coding based on LPS probability
Bypass coding mode (≡ bypass bin)
  Less complexity than the resular coding mode
  To encode a symbol having equal probability
    LPS value and LPS probability are fixed
  Estimation is skipped

## Slide 4: Main Reason of Limited Throughput
Serial dependencies in CABAC
Data dependencies for context model selection
  Often the context model selection for a bin depends on the value of a previously encoded/decoded bin
  This dependency makes parallelism difficult
Context-coded bins → bypass bins

## Slide 5: Background
Level coding in CABAC
  Three context coded bins for one coefficient
  coeff_sign_flag and coeff_abs_ remaining are bypass bins
Not all the context-coded bins are beneficial for compression efficiency while exaggerating the throughput
  Code up to 8 coeff_abs_level_greater1_flag for the non-zero coefficients in a subset of 16 coefficients
  Code up to 1 coeff_abs_level_greater2_flag a subset of 16 coefficients
  Early switch to Golomb-Rice bypass code
significant_coeff_flag
coeff_abs_level_greater1_flag
coeff_abs_level_greater2_flag
coeff_sign_flag
coeff_abs_remaining

## Slide 6: Background
Example of level coding
 | 0 | 1 | -1 | 0 | 2 | 4 | -1 | -4 | 4 | 2 | -6 | 4 | 7 | 6 | -12 | 18
(a) | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
(b) |  | 0 | 0 |  | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  |  |  | 
(c) |  |  |  |  | 0 |  |  |  |  |  |  |  |  |  |  | 
(d) |  | 0 | 1 |  | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
(e) |  |  |  |  |  | 2 |  | 2 | 2 | 0 | 5 | 3 | 6 | 5 | 10 | 17
Coding order
(a) significant_coeff_flag
(b) coeff_abs_level_greater1_flag
(c) coeff_abs_level_greater2_flag
(d) coeff_sign_flag
(e) coeff_abs_remaining
18 | 6 | -6 | -1
-12 | 4 | -4 | 0
7 | 4 | 2 | 1
2 | 4 | -1 | 0

## Slide 7: Motivation
Level coding in the current HTM is originally designed for texture
It can be observed that “often” a given texture TU has a lot of quantized transform coefficients than its collocated depth TU

## Slide 8: Proposal
Code up to 4 coeff_abs_level_greater1_flag for the non-zero coefficients in a subset of 16 coefficients in depth coding
(a) significant_coeff_flag
(b) coeff_abs_level_greater1_flag
(c) coeff_abs_level_greater2_flag
(d) coeff_sign_flag
(e) coeff_abs_remaining
 | 0 | 1 | -1 | 0 | 2 | 4 | -1 | -4 | 4 | 2 | -6 | 4 | 7 | 6 | -12 | 18
(a) | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
(b) |  | 0 | 0 |  | 1 | 1 |  |  |  |  |  |  |  |  |  | 
(c) |  |  |  |  | 0 |  |  |  |  |  |  |  |  |  |  | 
(d) |  | 0 | 1 |  | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
(e) |  |  |  |  |  | 2 |  | 3 | 3 | 1 | 5 | 3 | 6 | 5 | 10 | 17
Coding order
18 | 6 | -6 | -1
-12 | 4 | -4 | 0
7 | 4 | 2 | 1
2 | 4 | -1 | 0

## Slide 9: Throughput Efficiency
Maximum number of context coded bins between HTM 4.0.1 and proposed method in worst-case scenario
  Reduces the maximum numbers of context bins from 25 to 21
  16% of context-coded bins are reduced in worst-case scenario
 | HTM 4.0.1 | Proposed Method
significant_coeff_flag | 16 | 16
coeff_abs_level_greater1_flag | 8 | 4
coeff_abs_level_greater2_flag | 1 | 1
Total | 25 | 21

## Slide 10: Simulation Results (1)
3 view test cases
  In most cases, no coding efficiency loss
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.5% | 97.6% | 100.5%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.8% | 99.8% | 100.7%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.5% | 99.8% | 96.9%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.8% | 98.6% | 99.2%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.0% | 100.2% | 100.4%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 97.6% | 100.2%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 98.9% | 98.5%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.9% | 99.0% | 99.3%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 98.8% | 99.6%
Average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.5% | 98.9% | 99.5%

## Slide 11: Simulation Results (2)
2 view test case (extracted from 3 view data)
  In most cases, no coding efficiency loss
 | video 0 | video 1 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
Kendo | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 12: Summary
Simple change of current CABAC to restrict the number of context-coded bins to improve throughput
  Modified level coding for keeping coding performance
16% of context-coded bins of CABAC level coding in depth coding is reduced
  No significant coding efficiency loss on average
  No encoding/decoding/rendering time increases
It seems worth reducing context-coded bins of CABAC considering characteristics of depth videos
  Processes of current CABAC are kept unchanged
  No additional module is needed