## Slide 1
Results on Weighted Prediction in 3D Video Coding (JCT3V-B0134)
10. 13. 2012
Jiwook Jung, Hongbin Liu, Jaewon Sung , Jie Jia, Sehoon Yea (LG)

## Slide 2
Weighted Prediction (WP)
  Noticeable coding gains for fade in/out sequences (in HEVC)
  No consideration of weighted prediction in 3D-HEVC so far
  This contribution proposes to
    - Disable weighted prediction for inter-view prediction
  - Inherit weighted prediction parameters for dependent
  views from the base view
Introduction

## Slide 3
1. Disable weighted prediction for inter-view prediction
Weighted prediction applied on each view independently
2. Inherit WP parameters for dependent views
Weighted prediction parameters on dependent views inherited from the base view
Proposal
V0 Reference Picture
V1 Reference Picture
V2 Reference Picture
V1 Current Picture
V0 Current Picture
V2 Current Picture
WP Table
Estimation
WP Table Inheritance
WP Table Inheritance
Independent view
Dependent view
Dependent view

## Slide 4
Suggested Syntax Change
slice_header( ) { | Descriptor
first_slice_in_pic_flag | u(1)
… | 
if( !entropy_slice_flag ) { | 
… | …
if( ( weighted_pred_flag && slice_type = = P) ¦ ¦ ( weighted_bipred_flag = = 1 && slice_type = = B ) ) { | 
if( !base_view && !is_depth ) { | 
base_pred_weight_table_flag | u(1)
if( base_pred_weight_table_flag == 0 ) | 
pred_weight_table( ) | 
} | 
… | 
} | 

## Slide 5
Test Sequences
Fading sequences
  The fading tool used in HEVC (JCTVC-E041) applied to 3DV Sequences
  A linear fade in/out on each of the Y, U, V components
  First 2-seconds of texture videos
  : linear fade-out for 0 ~ 1 sec interval
  : linear fade-in for 1~2 sec interval
  : fading in/out strength [0.25,1]

## Slide 6
Objective result – Test1
Anchor : HTM-4.01 WP Off
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | -36.0% | -19.5% | -17.7% | -29.6% | 156.7% | 100.0%
Kendo | -18.6% | -4.9% | -3.1% | -13.5% | 192.4% | 101.6%
Newspapercc | -33.0% | -22.4% | -24.1% | -29.4% | 139.5% | 94.2%
GhostTownFly | -29.6% | -3.2% | -3.4% | -24.8% | 162.1% | 104.9%
PoznanHall2 | -32.1% | -10.8% | -15.5% | -24.9% | 166.4% | 99.4%
PoznanStreet | -27.5% | -15.6% | -14.9% | -24.5% | 136.2% | 102.0%
UndoDancer | -37.2% | -20.0% | -24.1% | -33.3% | 155.9% | 102.4%
1024x768 | -29.2% | -15.6% | -15.0% | -24.2% | 161.4% | 98.5%
1920x1088 | -31.6% | -12.4% | -14.5% | -26.9% | 154.7% | 102.2%
average | -30.6% | -13.8% | -14.7% | -25.7% | 157.5% | 100.6%

## Slide 7
Objective result – Test2
Anchor : HTM-4.01 WP Off
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | -36.0% | -26.3% | -25.1% | -32.0% | 160.8% | 99.7%
Kendo | -18.6% | -12.9% | -11.9% | -16.4% | 193.2% | 101.0%
Newspapercc | -33.0% | -28.2% | -29.2% | -31.3% | 143.1% | 93.4%
GhostTownFly | -29.6% | -11.6% | -12.2% | -26.2% | 163.4% | 104.3%
PoznanHall2 | -32.1% | -18.6% | -19.9% | -27.0% | 168.0% | 98.4%
PoznanStreet | -27.5% | -19.1% | -19.4% | -25.5% | 141.2% | 101.2%
UndoDancer | -37.2% | -23.8% | -26.7% | -33.9% | 158.0% | 102.1%
1024x768 | -29.2% | -22.5% | -22.1% | -26.6% | 164.4% | 98.0%
1920x1088 | -31.6% | -18.3% | -19.6% | -28.2% | 157.3% | 101.5%
average | -30.6% | -20.1% | -20.7% | -27.5% | 160.3% | 100.0%

## Slide 8
Conclusion
Proposed to enable weighted prediction for coding fading in/out 3D sequences
Showed benefits of WP parameter inheritance in terms of coding efficiency
Recommend to adopt the proposal