## Slide 1: JCT3V-E0163 AHG 15: Camera parameter signaling and depth reference selection
Yu-Lin Chang, Yi-Wen Chen, Jian-Liang Lin, Yu-Pao Tsai, Shawmin Lei
Presented by Yu-Lin Chang
JCT on 3D Video Coding Extension Development
Jul., 2013

## Slide 2: Overall Summary
When the macro for flexible coding order (FCO) is activated, compilation errors appear in HTM-7.0r1
  FCO bug-fixes without normative changes are provided.
Depth inherits the camera parameters from the texture of the same view, so view synthesis prediction (VSP) and depth oriented neighbor block disparity vector (DoNBDV) cannot work properly for depth-first coding
  Propose to explicitly signal the camera parameters for the depth when VSP or DoNBDV is enabled.
VSP and DoNBDV currently always use the depth of a reference view
  When depth-first coding is used, use the collocated depth of the current view, instead of using the depth of a reference view (e.g., base view), for deriving disparity vectors.
Notes:     Problem and proposeVSP off, finding inter-view reference without warping

## Slide 3: Bug-fixes for FCO about CU-level NBDV
CU based (NBDV) is adopted in the 4th JCT-3V meeting
  The original DoNBDV with flexible coding order should have been modified to fit into the CU-based NBDV scheme
  Compilation error occurs for current HTM-7.0r1 if enabling flexible coding order
Propose non-normative changes to use FCO with CU-based NBDV for DoNBDV

## Slide 4: Introduction to Camera Parameter
Camera parameter in the current HTM-7.0r1 works differently under different coding order
  Inconsistent cam-param signaling scheme might increase the parsing througput
  Signal camera parameters when they are really in use
Coding order | Cam-param of texture layer | Cam-param of depth layer
Texture first | Always sent in SPS | Always derived from texture picture of the same view
Depth first | Always sent in SPS | Always sent in SPS

## Slide 5: Proposed Changes in VPS for Camera Parameter
First align the WD with current HTM software 7.0r1
  Follow the HTM for its higher flexibility to control DoNBDV and VSP
vps_extension2( ) { | Descriptor
while( !byte_aligned( ) ) | 
vps_extension_byte_alignment_reserved_one_bit | u(1)
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
layerId = layer_id_in_nuh[ i ] | 
view_id[ layerId ] | u(8)
if ( layerId ! = 0 ) { | 
if ( !VpsDepthFlag[ layerId ] ) { | 
iv_mv_pred_flag[ layerId ] | u(1)
iv_res_pred_flag[ layerId ] | u(1)
depth_refinement_flag[ layerId ] | u(1)
view_synthesis_pred_flag[ layerId ] | u(1)
} else { | 
…. | u(1)
} | 
} | 
depth_refinement_flag[ layerId ] | u(1)
view_synthesis_pred_flag[ layerId ] | u(1)
} | 
} | 
iv_mv_scaling_flag | u(1)
} | 

## Slide 6: Proposed Changes in SPS for Camera Parameter
Propose to send camera parameter according to depth_refinement_flag and view_synthesis_pred_flag
  Transmit the camera parameters as long as they will be used in a certain layer
sps_extension2( ) { | Descriptor
if( !VpsDepthFlag[ nuh_layer_id ] ¦¦ ( depth_refinement_flag[ nuh_layer_id ] ¦¦ view_synthesis_pred_flag[ nuh_layer_id ] ) ) { | 
cp_precision | ue(v)
cp_in_slice_header_flag | u(1)
if( !cp_in_slice_header_flag ) { | 
for ( i = 0; i < ViewId[ nuh_layer_id ]; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
} | 
} | 
} | 
} | 

## Slide 7: Proposed Changes in Slice Header for Camera Parameter
Transmit camera parameter in slice header as long as they will be used in a certain layer
slice_header_extension( ) { | Descriptor
if( cp_in_slice_header_flag ¦¦ ( depth_refinement_flag[ nuh_layer_id ] ¦¦ view_synthesis_pred_flag[ nuh_layer_id ] ) ) { | 
for ( i = 0; i < ViewIdx; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
} | 
} | 
} | 

## Slide 8: Introduction to Depth Reference
In current 3D-HEVC, DoNBDV and BVSP all use the depth picture in base view as the depth reference because texture-first coding order is used
The depth picture in the same view provides better accuracy and less memory buffer to store the depth map
CB
T1
Coded D0
Associated depth
Estimated disparity vector
Virtual depth
CB
T1
Coded D0
Collocated depth
Depth availability under texture first coding order
Depth availability under depth first coding order
Coded D1

## Slide 9: Proposed Adaptive Depth Reference for DoNBDV and VSP
Propose to use the depth picture in the same view for BVSP while view_synthesis_pred_flag = 1
Propose to use the depth picture in the same view for DoNBDV while depth_refinement_flag = 1
 | view_synthesis_pred_flag=0 | view_synthesis_pred_flag=1
Depth first | BVSP off | VSP from collocated depth of the current view
Texture first | BVSP off | VSP from associated depth of a reference view
 | depth_refinement_flag=0 | depth_refinement_flag=1
Depth first | From neighbor block disparity vector | From collocated depth of the current view
Texture first | From neighbor block disparity vector | From associated depth of a reference view

## Slide 10: Experiment Results – HTM 7.0r1 FCO
Anchor: HTM 7.0r1 CTC
Test: HTM 7.0r1 with flexible coding order enabled
Crosschecked by JCT3V-E0297, Thanks to NTT

## Slide 11: Experiment Results – Proposed Adaptive Depth Reference vs HTM 7.0r1 FCO
Anchor: HTM-7.0r1 with flexible coding order enabled
Test: Proposed adaptive depth reference
Crosschecked by JCT3V-E0297, Thanks to NTT

## Slide 12: Conclusions
Bug-fixes on CU-based NBDV for FCO is proposed without normative change
The camera parameters are proposed to be signaled in a normative way for both texture-first coding and depth-first coding
  Explicit flag is proposed to enable the transmitting of camera parameters
Adaptations on BVSP and DoNBDV are proposed to utilize proper depth reference under different coding order
  Depth buffer can be reduced
  Provide some coding efficiency gain on synthesized view over total bitrate against HTM 7.0r1 FCO

## Slide 13: Thanks for your attention!
www.mediatek.com