## Slide 1: JCT3V-E0183 3D-CE3.h related: An additional texture merging candidate in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
Background
  JCT3V-D0109 proposes an additional inter-view merging candidate in texture coding.
    Inherit motion parameters from the right bottom position of the collocated PU in the reference view picture
Proposed
  An additional texture merging candidate
    Inherit motion parameters from the right bottom position of the collocated PU in the reference texture picture
Results
  Achieve 0.1% BD-rate saving for the synthesized views

## Slide 3: Background
In current 3D-HEVC, an inter-view merging candidate is adopted into the merging candidate list at position 0 in texture coding
  Inherit motion parameters from the center position of the collocated PU in the reference inter-view picture
Similarly, a texture merging candidate is adopted into the merging candidate list at position 0 in depth coding
  Inherits motion parameters from the center position of the collocated PU in the reference texture picture

## Slide 4: Background (Cont.)
JCT3V-D0109 proposes an additional inter-view merging candidate in texture coding
  Inherits motion parameters from the right bottom position of the collocated PU in the reference view picture.
  The additional candidate is inserted into the merging candidate list before TMVP if it is not pruned.

## Slide 5: Proposed
  Similarly, this contribution proposes an additional texture merging candidate in depth coding
    Inherits motion parameters from the right bottom position of the collocated PU in the reference texture picture
    The proposed additional texture merging candidate is also inserted into the merging candidate list before TMVP, if it is not identical to the merging candidate at position 0.

## Slide 6: Results
Achieve 0.1% BD-rate saving for the synthesized views
CTC

## Slide 7: Conclusion
An additional texture merging candidate is proposed for depth coding.
0.1% BD-rate saving for the synthesized views
Suggest to be adopted

## Slide 8: Thank you for your attention!