## Slide 1
CE1 related : The unification of sub-PU process for MPI blocks
Sunmi Yoo, Junghak Nam, Sehoon Yea
LG Electronics

## Slide 2: Introduction
The motion parameter inheritance (MPI)
  For depth coding, the motion parameters can be derived from the collocated texture block.
  Currently, the texture motion parameters can be derived at sub-PU level.
Sub-PU level motion vector prediction
  Motion holes (i.e. sub-PU blocks without motion vectors) appearing during the Sub-PU level IvMC are filled with CMP (Center Motion Parameters) of the corresponding blocks.
Currently, MPI motion holes are filled with the latest motion parameters, not CMP.

## Slide 3: Proposed method
It is proposed to fill the motion holes in MPI block with CMP, not the latest motions.
  To align the hole filling process
  It can reduce the complexity to store and update the latest motions.
Texture
Depth
(a)
Texture
Depth
(b)
Figure 1. The current motion hole filling process (a) and the proposed method (b)

## Slide 4: Experimental result
It is shown that the proposed method does not have any coding loss for the synthesized view.

## Slide 5: Conclusion
Current status
  MPI blocks derive the motion parameters from the collocated texture blocks at sub-PU level.
  The motion hole filling methods between IvMC and MPI is different.
MPI motion hole filling with CMP
  To align with the Sub-PU IvMC hole filling process
  No need to update the default MV