## Slide 1: Simplification of VSP candidate derivation (JCT3V-I0130)
ETRI* and KHU
*Gun Bang, Min Seong Lee, Young Su Heo, Gwang Hoon Park, *Gwang Soon Lee, *Nam Ho Hur

## Slide 2: Introduction
In the current HTM, the inherited VSP candidates are derived from all of the spatial neighboring blocks
The current NBDV process derives DV from the first available block between left and above block
However, all of these candidates have the same DV with the current CU
There is no benefit to use multiple inherited VSP candidates

## Slide 3: Proposal
Skipping for derivation process for default VSP merging candidate
  If one or more of the inherited VSP candidate is available derivation process for default VSP merging candidate will be skipped
Constraint position of inherited VSP candidates
  5 blocks → 2 blocks (Left, Above)
  The first available block is selected as the inherited VSP candidates, and skip derivation process for default VSP candidate
  If available inherited VSP candidate does not exist, then default VSP candidate derivation process is performed

## Slide 4: Proposal

## Slide 5: Proposal
By proposed simplification, MCL could have only one VSP merging candidate with no redundancy

## Slide 6: Result
Default VSP Derivation Skip

## Slide 7: Result
Limit inheritance VSP cand. Position + default VSP skip

## Slide 8: Conclusion
This contribution proposes to skip derivation process of VSP merging candidate when at lease one inherited VSP candidates is available.
The position of inherited VSP candidate is constrained to two (A1, B1) block
  the first available one is used among the inherited and default VSP candidate.
By the proposed method, redundant ones between VSP and the inherited VSP candidates are removed from MCL construction without coding loss.