## Slide 1: Centralized Color-Depth Packing (CCDP) SEI Message Syntax (A Revision of JCT-S0031)
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University

## Slide 2: Outlooks of CCDPs (color 3/4, 7/8, 15/16)
1H
3/4H
1/8H
1/8H
1H
Color-3/4 CCDP
1H
15/16H
1/32H
1/32H
Color-15/16 CCDP
1H
7/8H
1/16H
1/16H
Color-7/8 CCDP
Original Color
Original Depth

## Slide 3: CCDP SEI Syntax
centralized_color-depth_packing( payloadSize ) { | Descriptor
centralized_color-depth_packing_id | ue(v)
centralized_color-depth_packing_cancel_flag | u(1)
if( ! centralized_color-depth_packing_cancel_flag) { | 
centralized_color-depth_packing_type | u(7)
centralized_color-depth_packing_content_interpretation_type | u(6)
depth_spatial_flipping_flag | u(1)
depth_subpixel_arrangement_type | u(4)
color_samping_type | u(8)
depth_samping_type | u(8)
centralized_color-depth_packing_reserved_byte | u(8)
centralized_color-depth_packing_persistence_flag | u(1)
} | 
} | 

## Slide 4: centralized_color-depth_packing_id
centralized_color-depth_packing_id contains an identifying number that may be used to identify the usage of the centralized color-depth packing SEI message. The value of centralized_color-depth_packing_id shall be in the range of 0 to 232 − 2, inclusive
Values of centralized_color-depth_packing_id from 0 to 255 and from 512 to 231 − 1 may be used as determined by the application. Values of centralized_color-depth_packing_id from 256 to 511 and from 231 to 232 − 2 are reserved for future use by ITU-T | ISO/IEC. Decoders shall ignore all centralized color-depth packing arrangement SEI messages containing a value of centralized_color-depth_packing_id in the range of 256 to 511, inclusive, or in the range of 231 to 232 − 2, inclusive, and bitstreams shall not contain such values.

## Slide 5: centralized_color-depth_packing_cancel_flag
centralized_color-depth_packing_cancel_flag equal to 1 indicates that the centralized color-depth packing arrangement SEI message cancels the persistence of any previous the centralized color-depth packing in output order. centralized_color-depth_packing_cancel_flag equal to 0 indicates that indicates that centralized color-depth packing follows.

## Slide 6: centralized_color-depth_packing_type
Value | Interpretation
4 | Color and depth plane of the decoded frames contains a color-3/4 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x1.
6 | Color and depth plane of the decoded frames contains a color-5/6 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x2.
8 | Color and depth plane of the decoded frames contains a color-7/8 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x3.
12 | Color and depth plane of the decoded frames contains a color-11/12 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x4.
16 | Color and depth plane of the decoded frames contains a color-15/16 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x5.

## Slide 7: centralized_color-depth_packing_content_interpretation_type
Value | Interpretation
0 | Unspecified relationship between the centralized color-depth packed constituent frames
1 | Indicates that the packed frame is arranged in order of reduced_depth_1, resized_color, and reduced_depth_2 from top to bottom
2 | Indicates that the packed frame is arranged in order of reduced_depth_1, resized_color, and reduced_depth_2 from left to right
NOTE 1: When value is 1 or 2 in centralized_color-depth_packing_content_interpretation_type, and
centralized_color_depth_packing_type should be equal to 4, 6, 8, 12, or 16.
1H
1W
centralized_color-depth_packing_content_interpretation_type=1
centralized_color-depth_packing_content_interpretation_type =2

## Slide 8: depth_spatial_flipping_flag
depth_spatial_flipping_flag equal to 1, when centralized_color-depth_packing_arrangement_type is equal to 4, 6, 8, 12 or 16 and centralized_color-depth_packing_content_interpretation_type equal 1 or 2, indicates that depth frame is spatially flipped relative to its intended orientation for display or other such purposes.
When centralized_color-depth_packing_type is equal to 4, 6, 8, 12, or 16, centralized_color-depth_packing_content_interpretation_type equal 1 or 2, and depth_spatial_flipping_flag is equal to 1, the type of spatial flipping that is indicated is as follows:
  If centralized_color-depth_packing_content_interpretation_type is equal to 1, the indicated depth spatial flipping is vertical flipping.
  If centralized_color-depth_packing_content_interpretation_type is equal to 2, the indicated depth spatial flipping is horizontal flipping.
  Otherwise (depth_spatial_flipping_flag is equal to 0), the indicated spatial flipping is not necessary.
1H
1H
depth_spatial_flipping_flag=1
depth_spatial_flipping_flag=0

## Slide 9: depth_subpixel_rotation_flag
depth_subpixel_rotation_flag equal to 1 indicates that embedding the 3 depth values into R, G and B channels to the colored-depth frame is used the rotation method. depth_subpixel_arrangement_flag equal to 0 indicates that embedding the 3 depth values into R, G, and B channels in the colored-depth frame is used the sequence order.
(Y11, Y21, Y31) (Y22, Y32, Y12) (Y33, Y13, Y23), …
….
depth_subpixel_rotation_flag=1
(Y11, Y21, Y31) (Y12, Y22, Y32) (Y13, Y23, Y33), …
….
depth_subpixel_rotation_flag=0
Y11 Y12 Y13…
Y21 Y22 Y23…
Y31 Y32 Y33…
…
Colored depth in subpixels (R, G, B)
Depth map
Colored depth in subpixels (R, G, B)

## Slide 10: color_samping_type
color_samping_type indicates that the method of the color sampling is used by an encoder to indicate to a decoder as specified in Table D‑13.
Value | Interpretation
0 | Encoder using bilinear method to downscale the vertical or horizontal resolution of color frame
Values of color_samping_type that do not appear in Table D.13 are reserved for future specification by ITU-T |ISO/IEC and shall not be present in bitstreams conforming to this version of this Specification. Decoders shall ignore centralized color-depth packing arrangement SEI messages that contain reserved values of color_sampling_type.
NOTE 2– When centralized_color-depth_packing_content_interpretation_type equal to 1, the value 0 for color_sampling_type, the color frame is down scale the vertical resolution by using bilinear method. When centralized_color-depth_packing_content_interpretation_type equal to 2, the value 0 for color_sampling_type, the color frame is down scaled in the horizontal resolution by using bilinear method.

## Slide 11: depth_samping_type
depth_samping_type indicates that the method of the depth sampling is used by an encoder to indicate to a decoder as specified in Table D‑14.
Value | Interpretation
0 | Encoder using bilinear method to downscale the vertical or horizontal resolution of depth frame
Values of depth_samping_type that do not appear in Table D.14 are reserved for future specification by ITU-T |ISO/IEC and shall not be present in bitstreams conforming to this version of this Specification. Decoders shall ignore centralized color-depth packing arrangement SEI messages that contain reserved values of depth_samping_type .
NOTE 3–When centralized_color-depth_packing_content_interpretation_type equal to 1, the value 0 for depth_samping_type, the depth frame is down scale the vertical resolution by using bilinear method. When centralized_color-depth_packing_content_interpretation_type equal to 2, the value 0 for depth_samping_type, the depth frame is down scale the horizontal resolution by using bilinear method.

## Slide 12: centralized_color-depth_packing_reserved_byte
centralized_color-depth_packing_reserved_byte is reserved for future use by ITU-T | ISO/IEC. It is a requirement of bitstreams conformance that the value of centralized_color-depth_packing_reserved_byte shall be equal to 0. All other values of centralized_color-depth_packing_reserved_byte are reserved for future use by ITU-T | ISO/IEC. Decoders shall ignore the value of centralized_color-depth_packing_reserved_byte.

## Slide 13: centralized_color-depth_packing_persistence_flag
centralized_color_depth_packing_persistence_flag specifies the persistence of the centralized color-depth packing arrangement SEI message.
centralized_color-depth_packing_persistence_flag equal to 0 specifies that the centralized color-depth packing arrangement SEI message applies to the current decoded frame only.
centralized_color-depth_packing_persistence_flag equal to 1 specifies that the centralized color-depth packing arrangement SEI message persists in output order until any of the following conditions are true:
  – A new CVS begins.
  – The bitstream ends.
  – A frame in an access unit containing a centralized color-depth packing SEI message with the same value of centralized_color-depth_packing_id is output having PicOrderCntVal greater than PicOrderCnt( CurrPic ).

## Slide 14: Conclusions
In this contribution, the objective measurements of the proposed color-3/4, color-7/8 and color-15/16 CCDP methods are comparing to that of the frame compatible color-and-depth (SbS) packing format.
To include the color-3/4, color-5/6, color-7/8, color-11/12, and color-15/16 CCDP formats and their settings in the AVC and HEVC standards, we propose a new CCDP SEI message syntax.
The proposed CCDP format attains better image quality in the receiving side compared to the frame compatible color-and-depth (SbS) packing format for both 2D-TV and 3D-TV displays.

## Slide 15
Thanks for your kind attention
Q&A