## Slide 1
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University, Taiwan
Centralized Texture-Depth Packing
SEI Message for HEVC
(Revisions of JCT3V-M0022)

## Slide 2: Contents
Centralized Texture-Depth Packing (CTDP) SEI Message Syntax
Experimental Results: Depth Enhancement and Temporal DIBR
Experimental Results: Upsampling and Downsampling Filters
CTDP Adoption Plans in Taiwan
Conclusions

## Slide 3: Centralized Texture-Depth Packing (CTDP) SEI Message Syntax
Remove the syntax of depth_sampling_factor and packed_depth_sampling_type as suggested in the previous meeting
Add the syntax quarter_reduced_depth_line_number for defining the sizes of depth and texture

## Slide 4: CTDP SEI Syntax
centralized_texture-depth_packing( payloadSize ) { | Descriptor
centralized_texture-depth_packing_cancel_flag | u(1)
if( ! centralized_texture-depth_packing_cancel_flag ) { | 
depth_sampling_factor | u(3)
packed_depth_size_factor | u(2)
centralized_texture-depth_packing_content_interpretation_type | u(3)
quarter_reduced_depth_line_number | u(10)
depth_spatial_flipping_flag | u(1)
depth_chroma_sampling_type | u(3)
depth_subpixel_arrangement_type | u(2)
depth_representation_type | ue(v)
baseline_dist_flag | u(1)
focal_length_flag | u(1)
z_near_flag | u(1)
z_far_flag | u(1)
d_min_flag | u(1)
d_max_flag | u(1)
if( baseline_dist_flag ) | 
view_syn_rep_info_element( BdistanceSign, BdistanceExp, BdistanceMantissa, BdistanceManLen ) | 
if( focal_length_pixel_flag ) | 
view_syn_rep_info_element( FlengthSign, FlengthExp, FlengthMantissa, FlengthManLen ) | 
if( z_near_flag ) | 
view_syn_rep_info_element( ZNearSign, ZNearExp, ZNearMantissa, ZNearManLen ) | 
if( z_far_flag ) | 
view_syn_rep_info_element ( ZFarSign, ZFarExp, ZFarMantissa, ZFarManLen ) | 
if( d_min_flag ) | 
view_syn_rep_info_element ( DMinSign, DMinExp, DMinMantissa, DMinManLen ) | 
if( d_max_flag ) | 
view_syn_rep_info_element ( DMaxSign, DMaxExp, DMaxMantissa, DMaxManLen ) | 
if( depth_representation_type = = 3 ) { | 
depth_nonlinear_representation_num_minus1 | ue(v)
for( i = 1; i <= depth_nonlinear_representation_num_minus1 + 1; i++ ) | 
depth_nonlinear_representation_model[ i ] | 
centralized_texture-depth_packing_persistence_flag | u(1)
} | 
} | 
removed
added

## Slide 5: centralized_texture-depth_packing_content_interpretation_type
Value | Interpretation
0 | Indicates the CTDP-1TB type that the CTDP packed frame, which provides one texture-plus-depth view, is arranged in the order of reduced_depth_top (RDT), resized_texture (RT), and reduced_depth_bottom (RDB) regions from top to bottom as illustrated in Figure D‑X1.
1 | Indicates the CTDP-1LR type that the CTDP packed frame is arranged in the order of reduced_depth_left (RDL), resized_texture (RT), and reduced_depth_right (RDR) regions from left to right as illustrated in Figure D‑X2.
2 | Indicates the CTDP-2TB type that the CTDP packed frame, which provides two texture-plus-depth views, is arranged in the order of reduced_depth_leftview_top (RDLT), resized_texture_leftview (RTL), and reduced_depth_leftview_bottom (RDLB) regions in the left-half frame and reduced_depth_rightview_top (RDRT), resized_texture_rightview (RTR), and reduced_depth_rightview_bottom (RDRB) regions in the right-half frame from top to bottom as illustrated in Figure D‑X3.
3 | Indicates the CTDP-2LR type that the CTDP packed frame, which provides two texture-plus-depth views, is arranged in the order of reduced_depth_topview_left (RDTL), resized_texture_topview (RTT), and reduced_depth_topview_right (RDTR) regions in the top-half frame and reduced_depth_bottomview_left (RDBL), resized_texture_bottomview (RTB), and reduced_depth_bottomview_right (RDBR) regions in the bottom-frame from left to right as illustrated in Figure D‑X4.
CTDP-1TB
CTDP-1LR
CTDP-2TB
CTDP-2LR

## Slide 6
centralized_texture-depth_packing_content_interpretation_type =0
CTDP-TB
HHD = 2*quarter_reduced_depth_line_number

## Slide 7
centralized_texture-depth_packing_content_interpretation_type =1
CTDP-LR
WHD = 2*quarter_reduced_depth_line_number

## Slide 8
centralized_texture-depth_packing_content_interpretation_type =2
CTDP-2TB
HHD = 2*quarter_reduced_depth_line_number

## Slide 9
centralized_texture-depth_packing_content_interpretation_type =3
CTDP-2LR
WHD = 2*quarter_reduced_depth_line_number

## Slide 10: quarter_reduced_depth_line_number
quarter_reduced_depth_line_number indicates the half number of horizontal lines of the reduced depth top and reduced depth bottom regions if centralized_texture-depth_packing_content_interpretation_type is equal to 0 or 2.
Guidelines for selecting quarter_reduced_depth_line_number for CTDP-1TB and CTDP-2TB:
  to be a divisible factor of H such that it will result in simple downsample and upsampling VLSI implementations;
  to be less than H/16 such that the downsampling factor of texture frame is less than that of depth map to achieve good packing quality.
Video Formats | quarter_reduced_ depth_ line_ number | HHD | HRT | Texture Vertical Downsampling factor | Depth Vertical Downsampling factor
UHD (H=2160) | 90 | 180 | 1800 | 5:6 | 1:2
 | 60 | 120 | 1920 | 8:9 | 1:3
 | 45 | 90 | 1980 | 11:12 | 1:4
HD (H=1080) | 45 | 90 | 900 | 5:6 | 1:2
 | 30 | 60 | 960 | 8:9 | 1:3
Possible Selections for UHD and HD video formats:

## Slide 11: quarter_reduced_depth_line_number
quarter_reduced_depth_line_number indicates the half number of horizontal lines of the reduced depth top and reduced depth bottom regions if centralized_texture-depth_packing_content_interpretation_type is equal to 1 or 3.
Guidelines for selecting quarter_reduced_depth_line_number for CTDP-1LR and CTDP-LR:
  to be a divisible factor of W such that it will result in simple downsample and upsampling VLSI implementations;
  to be less than W/16 such that the downsampling factor of texture frame is less than that of depth map to achieve good packing quality.
Possible Selections for UHD and HD video formats:
Video Formats | quarter_reduced_ depth_ line_ number | WHD | WRT | Texture Horizontal Downsampling factor | Depth Horizontal Downsampling factor
UHD (W=3840) | 160 | 320 | 3200 | 5:6 | 1:2
 | 120 | 240 | 3360 | 8:9 | 1:3
 | 80 | 160 | 3520 | 11:12 | 1:4
HD (W=1920) | 80 | 160 | 1600 | 5:6 | 1:2
 | 60 | 120 | 1680 | 8:9 | 1:3
 | 40 | 80 | 1760 | 11:12 | 1:4

## Slide 12: depth_spatial_flipping_flag
depth_spatial_flipping_flag indicates that the reduced depth region are spatially flipped relative to its intended orientation for display or other such purposes
Value | Interpretation
0 | No flipping
1 | Flipping
HRD
HRD
w
w
HRD
HRD
w
w
No flipping
Flipping

## Slide 13
depth-chroma_sampling_type indicates that the depth chroma sampling method from 444 to 422 or 420 format is used by the CTDP packer as specified in Table D-X2.
depth_chroma_sampling_type
Value | Interpretation
1 | CTDP depacker is informed that the direct sample is used to convert the chroma sample from 444 to 422 or 420 format according to marked chroma sample location.
2 | CTDP depacker is informed that the mean of two (four) samples is used to convert the chroma sample from 444 to 422 (420) format.

## Slide 14: depth_subpixel_arrangement_type = 0

## Slide 15: depth_subpixel_arrangement_type = 1

## Slide 16: depth_representation_type
Value | Interpretation
0 | Each decoded luma sample value of an auxiliary picture represents an inverse of Z value that is uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the luma sample value equal to 0 represents the inverse of ZFar (specified below). When z_near_flag is equal to 1, the luma sample value equal to maxVal represents the inverse of ZNear (specified below).
1 | Each decoded luma sample value of an auxiliary picture represents disparity that is uniformly quantized into the range of 0 to maxVal, inclusive. When d_min_flag is equal to 1, the luma sample value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the luma sample value equal to maxVal represents DMax (specified below).
2 | Each decoded luma sample value of an auxiliary picture represents a Z value uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the luma sample value equal to 0 corresponds to ZFar (specified below). When z_near_flag is equal to 1, the luma sample value equal to maxVal represents ZNear (specified below).
3 | Each decoded luma sample value of an auxiliary picture represents a nonlinearly mapped disparity, normalized in range from 0 to maxVal, as specified by depth_nonlinear_representation_num_minus1 and depth_nonlinear_representation_model[i].When d_min_flag is equal to 1, the luma sample value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the luma sample value equal to maxVal represents DMax (specified below).
Other values | Reserved for future use
The variable maxVal is set equal to ( 1 << ( 8 + bit_depth_luma_minus8 ) ) − 1, where bit_depth_luma_minus8 is the value included in or inferred for the active SPS of the layer with nuh_layer_id equal to targetLayerId.
depth_representation_type specifies the representation definition of decoded luma samples of auxiliary pictures. In the table, disparity specifies the horizontal displacement between two texture views and Z value specifies the distance from a camera.

## Slide 17: Depth Parameter Related Flags
baseline_dist_flag equal to 0 specifies that the syntax elements specifying the baseline distance are not present in the syntax structure. baseline_dist_flag equal to 1 specifies that the syntax elements specifying the baseline distance value are present in the syntax structure.
focal_length_flag equal to 0 specifies that the syntax elements specifying the focal length are not present in the syntax structure. focal_length_pixel_flag equal to 1 specifies that the syntax elements specifying the focal length value are present in the syntax structure.
z_near_flag equal to 0 specifies that the syntax elements specifying the nearest depth value are not present in the syntax structure. z_near_flag equal to 1 specifies that the syntax elements specifying the nearest depth value are present in the syntax structure.
z_far_flag equal to 0 specifies that the syntax elements specifying the farthest depth value are not present in the syntax structure. z_far_flag equal to 1 specifies that the syntax elements specifying the farthest depth value are present in the syntax structure.
d_min_flag equal to 0 specifies that the syntax elements specifying the minimum disparity value are not present in the syntax structure. d_min_flag equal to 1 specifies that the syntax elements specifying the minimum disparity value are present in the syntax structure.
d_max_flag equal to 0 specifies that the syntax elements specifying the maximum disparity value are not present in the syntax structure. d_max_flag equal to 1 specifies that the syntax elements specifying the maximum disparity value are present in the syntax structure.

## Slide 18: View synthesis representation information element syntax
The syntax structure specifies the value of an element in the view synthesis representation information SEI message.
The syntax structure sets the values of the OutSign, OutExp, OutMantissa and OutManLen variables that represent a floating-point value. When the syntax structure is included in another syntax structure, the variable names OutSign, OutExp, OutMantissa and OutManLen are to be interpreted as being replaced by the variable names used when the syntax structure is included.
da_sign_flag equal to 0 indicates that the sign of the floating-point value is positive. da_sign_flag equal to 1 indicates that the sign is negative. The variable OutSign is set equal to da_sign_flag.
da_exponent specifies the exponent of the floating-point value. The value of da_exponent shall be in the range of 0 to 27 − 2, inclusive. The value 27 − 1 is reserved for future use by ITU-T | ISO/IEC. Decoders shall treat the value 27 − 1 as indicating an unspecified value. The variable OutExp is set equal to da_exponent.
da_mantissa_len_minus1 plus 1 specifies the number of bits in the da_mantissa syntax element. The value of da_mantissa_len_minus1 shall be in the range of 0 to 31, inclusive. The variable OutManLen is set equal to da_mantissa_len_minus1 + 1.
da_mantissa specifies the mantissa of the floating-point value. The variable OutMantissa is set equal to da_mantissa.
view_syn_rep_info_element( OutSign, OutExp, OutMantissa, OutManLen ) { | Descriptor
da_sign_flag | u(1)
da_exponent | u(7)
da_mantissa_len_minus1 | u(5)
da_mantissa | u(v)
} | 

## Slide 19: Association between depth parameter variables and syntax elements
x | s | e | n | v
Bdistance | BdistanceSign | BdistanceExp | BdistanceMantissa | BdistanceManLen
Flength | FlengthSign | FlengthExp | FlengthMantissa | FlengthManLen
ZNear | ZNearSign | ZNearExp | ZNearMantissa | ZNearManLen
ZFar | ZFarSign | ZFarExp | ZFarMantissa | ZFarManLen
DMax | DMaxSign | DMaxExp | DMaxMantissa | DMaxManLen
DMin | DMinSign | DMinExp | DMinMantissa | DMinManLen
The variables in the x column of table are derived from the respective variables in the s, e, n and v columns as follows:
– If the value of e is in the range of 0 to 127, exclusive, x is set equal to ( −1 )s* 2e - 31 * ( 1 + n ÷ 2v ).
– Otherwise (e is equal to 0), x is set equal to ( −1 )s * 2−( 30 + v ) * n.
The DMin and DMax values, when present, are specified in units of a luma sample width of the coded picture.
The units for the ZNear and ZFar, when present, are identical but unspecified.
When depth_representation_type is equal to 0 or 2, the disparity D can further be obtained from the value of Z, Bdistance, and Flength, where D = Bdistance × Flength ÷ Z

## Slide 20: Other Syntax Elements
depth_nonlinear_representation_num_minus1 plus 2 specifies the number of piecewise linear segments for mapping of depth values to a scale that is uniformly quantized in terms of disparity.
depth_nonlinear_representation_model[ i ] for i ranging from 0 to depth_nonlinear_representation_num_minus1 + 2, inclusive, specify the piecewise linear segments for mapping of decoded luma sample values of an auxiliary picture to a scale that is uniformly quantized in terms of disparity. The values of depth_nonlinear_representation_model[0] and depth_nonlinear_representation_model[ depth_nonlinear_representation_num_minus1 + 2 ] are both inferred to be equal to 0.
centralized_texture_depth_packing_persistence_flag specifies the persistence of the centralized texture-depth packing arrangement SEI message.
centralized_texture-depth_packing_persistence_flag equal to 0 specifies that the centralized texture-depth packing arrangement SEI message applies to the current decoded frame only.
centralized_texture-depth_packing_persistence_flag equal to 1 specifies that the centralized texture-depth packing arrangement SEI message persists in output order until any of the following conditions are true:
– A new CVS begins.
– The bitstream ends.
– A frame in an access unit containing a centralized texture-depth packing SEI message with the same

## Slide 21: Experimental Results
Environment Settings
Coding performance in HEVC HM 13.0 (CTDP)
Coding performance in 3D-HEVC HTM 8.0

## Slide 22
Sequences | Clipped Resolution | Frames | Coded View | Coded 2 Views | Synthesized View
Undo Dancer | 1920×1080 | 250 | 3 | 3, 5 | 4
Ghost Town Fly | 1920×1080 | 250 | 3 | 3, 5 | 4
Shark | 1920×1080 | 300 | 5 | 5, 9 | 7
Test Sequences (CG)
PS: Since Ghost Town Fly does not provide camera parameters, we do not include it for performance comparisons

## Slide 23: Experimental Settings
Encoding Mode: All Intra, Low delay, Random access
QP: 27,32,37,42
depth_sampling_factor: 5/6, 8/9
CTDP_content_interpretation_type: CTDP-1TB and CTDP-2TB
image resizing: bicubic and Lancos 4
  depth resizing: bicubic
  depth spatial flipping: flipped
  depth subpixel arrangement: sequential order
  depth_chorma_sampling: direct sample

## Slide 24: Adaptive Bilateral Depth Enhancement
With the YCbCr calibration [2], the depth enhancement in [2] is revised by using jointly adaptive texture and depth filtering as
with
where Y(x, y) and D(x, y) represents the luminance channel of depacked texture image and the depacked depth map at position (x, y), respectively. The adaptive parameters include weight control parameters a and b and threshold parameters s and x. If the variance of the texture or depth pixels in 9x9 windows is smaller than the threshold, a larger support region WA (9x9) will be used, otherwise, a smaller support regions WB (3x3) is suggested, where the limited variances, VA(x, y) = max(min(varA(Y(x, y), LA), UA) and VB(x, y) = max(min(varB(Y(x, y), LB), UB) and the variances varA(Y(x, y), and varB(Y(x, y)) are computed in the corresponding support regions WA and WB accordingly.

## Slide 25: Adaptive Temporal View Synthesis
The ATVS system adopts spatial Gaussian and temporal smooth filtering for depth maps to increase the temporal consistency of synthesized view. The Gaussian smooth filter can help to reduce the artifact after hole-filling process and the temporal filtering can avoid the jumping effect in the synthesized video. The concept of temporal filtering is to maintain similar depth value when the difference of pixel values in current and previous frames is smaller. The modified depth value at (x, y) can be obtained by
where
and
As for the hole-filling process, we simply use the background extension to make a suitable trade-off between quality and computation.

## Slide 26
DIBR
CTDP
Depacking
YCbCr Calib.
Bilateral
Depth Enhancement
ATVS
Depacked
Texture
(WxH)
D1
D2
D3
Depacked Depth
without YCbCr
calibration (WxH)
Depacked Depth
with YCbCr
calibration (WxH)
YCbCr Direct
Enhanced
Depth
(WxH)
Synthesized
VSRS View
(WxH)
VSRS
Synthesized
ATVS View
(WxH)
Depacked Depth Enhancements

## Slide 27: CTDP-2TB Packing (for 2-View 2 Depth)
CTDP-2TB

## Slide 28: Texture and Depth Performance Comparisons
Original frame
Tested frame
Texture PSNR &
Bitrate
Depth PSNR &
Bitrate
3840
3840
1080
3840
3840
1088

## Slide 29: Virtual View Performance Comparisons
1920
1080
1920
1080
Virtual View PSNR & Bitrate
from 3D HEVC
Virtual view from 3D HEVC decoded texture and depth frames
Virtual view from uncompressed texture and depth frames
Virtual view from uncompressed texture and depth frames
1920
1080
1920
1080
Virtual View PSNR
& Bitrate
from HEVC-CTDP
Virtual view from HEVC
CTDP depacked texture and depth frames

## Slide 30
Experimental Results (1-View 1-Depth) HEVC + 5/6 CTDP-1TB with respect to 3D-HEVC
BDBR |  |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View | 
 | Texture | Depth |  |  | VSRS | ATVS
 | 5/6_1TB | 5/6_1TB_D1 | 5/6_1TB_D2 | 5/6_1TB_D3 | 5/6_1TB | 5/6_1TB
ra | 19.1613 | -40.6867 | -40.9320 | -48.4200 | 45.0708 | 38.9570
ldp | 13.6528 | -57.0321 | -56.8624 | -61.5932 | 29.8237 | 19.1906
ai | 11.6244 | -15.1046 | -16.5193 | -28.0788 | 54.2097 | 50.6141
ave | 14.8128 | -37.6078 | -38.1045 | -46.0307 | 43.0347 | 36.2539
BDPSNR |  |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View | 
 | Texture | Depth |  |  | VSRS | ATVS
 | 5/6_1TB | 5/6_1TB_D1 | 5/6_1TB_D2 | 5/6_1TB_D3 | 5/6_1TB | 5/6_1TB
ra | -0.5741 | 1.8158 | 1.8827 | 2.4889 | -1.0416 | -0.8495
ldp | -0.4308 | 3.6340 | 3.7121 | 4.3047 | -0.7667 | -0.5183
ai | -0.4129 | 0.4578 | 0.6219 | 1.2294 | -1.3641 | -1.1630
ave | -0.4726 | 1.9692 | 2.0722 | 2.6743 | -1.0575 | -0.8436
Bicubic Up and Down Sampling for Both Texture and Depth

## Slide 31
Experimental Results (1-View 1-Depth) HEVC + 8/9 CTDP-1TB with respect to 3D-HEVC
BDBR |  |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View | 
 | Texture | Depth |  |  | VSRS | ATVS
 | 5/6_1TB | 5/6_1TB_D1 | 5/6_1TB_D2 | 5/6_1TB_D3 | 5/6_1TB | 5/6_1TB
ra | 15.6515 | -20.4062 | -21.0416 | -30.4340 | 53.2643 | 54.4600
ldp | 10.3883 | -46.7615 | -46.6968 | -52.0132 | 36.3050 | 29.4947
ai | 8.3173 | 7.7358 | 6.3711 | -8.0741 | 62.7299 | 68.1486
ave | 11.4523 | -19.8106 | -20.4558 | -30.1738 | 50.7664 | 50.7011
BDPSNR |  |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View | 
 | Texture | Depth |  |  | VSRS | ATVS
 | 5/6_1TB | 5/6_1TB_D1 | 5/6_1TB_D2 | 5/6_1TB_D3 | 5/6_1TB | 5/6_1TB
ra | -0.4186 | 0.6767 | 0.7462 | 1.2684 | -1.1861 | -1.0743
ldp | -0.2996 | 2.6069 | 2.6873 | 3.2358 | -0.8902 | -0.6921
ai | -0.1949 | -0.7220 | -0.5610 | 0.1314 | -1.5130 | -1.4087
ave | -0.3043 | 0.8539 | 0.9575 | 1.5452 | -1.1964 | -1.0584
Bicubic Up and Down Sampling for Both Texture and Depth

## Slide 32
View1
View2
Depth1
Depth2
Bicubic SbS
dowm-sample
Bicubic
up-sample
CTDP
packing
CTDP
depacking
Wrong Packing Procedure (2V+2D)
SbS
packing
SbS
Depacking

## Slide 33
Experimental Results (2-View 2-Depth) HEVC + 5/6 CTDP-2TB with respect to 3D-HEVC
BDBR |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View
 | Texture | Depth |  |  | VSRS
 | 5/6_2TB | 5/6_2TB_D1 | 5/6_2TB_D2 | 5/6_2TB_D3 | 5/6_2TB
ra | 1283.9177 | -9.3105 | -9.3525 | -19.4928 | 690.0581
ldp | 654.7494 | -41.2514 | -41.0887 | -47.1645 | 390.4533
ai | 595.2655 | -34.0683 | -34.1806 | -43.6932 | 464.8886
ave | 844.6442 | -28.2100 | -28.2073 | -36.7835 | 515.1333
BDPSNR |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View
 | Texture | Depth |  |  | VSRS
 | 5/6_1TB | 5/6_1TB_D1 | 5/6_1TB_D2 | 5/6_1TB_D3 | 5/6_1TB
ra | -3.9810 | -0.1143 | -0.0966 | 0.2896 | -3.7034
ldp | -3.6308 | 1.4910 | 1.5108 | 1.9282 | -3.3098
ai | -2.5472 | 0.7856 | 0.8457 | 1.4330 | -2.7448
ave | -3.3863 | 0.7208 | 0.7533 | 1.2169 | -3.2526

## Slide 34
View1
View2
Depth1
Depth2
SbS
Packing
CTDP
packing
Corrected Packing Procedure (2V+2D)
Down
Sampling
SbS
Depacking
CTDP
depacking
Up
Sampling

## Slide 35
Experimental Results (1-View 1-Depth) HEVC + 5/6 CTDP-1TB with respect to 3D-HEVC
BDBR |  |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View | 
 | Texture | Depth |  |  | VSRS | ATVS
 | 5/6_1TB | 5/6_1TB_D1 | 5/6_1TB_D2 | 5/6_1TB_D3 | 5/6_1TB | 5/6_1TB
ra | 16.5230 | -42.7322 | -42.9519 | -49.2434 | 40.1037 | 32.6021
ldp | 11.2823 | -59.8105 | -59.7042 | -63.1895 | 27.6951 | 16.4208
ai | 8.5414 | -25.1800 | -26.2376 | -36.0964 | 47.7336 | 41.1882
ave | 12.1156 | -42.5742 | -42.9645 | -49.5098 | 38.5108 | 30.0704
BDPSNR |  |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View | 
 | Texture | Depth |  |  | VSRS | ATVS
 | 5/6_1TB | 5/6_1TB_D1 | 5/6_1TB_D2 | 5/6_1TB_D3 | 5/6_1TB | 5/6_1TB
ra | -0.5067 | 1.9765 | 2.0415 | 2.6139 | -0.9598 | -0.7446
ldp | -0.3627 | 4.0170 | 4.0984 | 4.7465 | -0.7069 | -0.4351
ai | -0.3117 | 0.9744 | 1.1391 | 1.8881 | -1.2425 | -1.0104
ave | -0.3937 | 2.3226 | 2.4263 | 3.0828 | -0.9697 | -0.7300
Lancoz4 Up and Down Sampling for Texture and Bicubic for Depth

## Slide 36
Experimental Results (1-View 1-Depth) HEVC + 8/9 CTDP-1TB with respect to 3D-HEVC
BDBR |  |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View | 
 | Texture | Depth |  |  | VSRS | ATVS
 | 8/9_1TB | 8/9_1TB_D1 | 8/9_1TB_D2 | 8/9_1TB_D3 | 8/9_1TB | 8/9_1TB
ra | 12.0555 | -19.3112 | -20.0301 | -29.6826 | 48.5718 | 48.1107
ldp | 6.2928 | -49.4961 | -49.5887 | -54.4696 | 32.3082 | 24.5316
ai | 5.9415 | 2.5363 | 1.5019 | -12.3999 | 58.8312 | 60.1661
ave | 8.0966 | -22.0903 | -22.7056 | -32.1840 | 46.5704 | 44.2694
BDPSNR |  |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View | 
 | Texture | Depth |  |  | VSRS | ATVS
 | 8/9_1TB | 8/9_1TB_D1 | 8/9_1TB_D2 | 8/9_1TB_D3 | 8/9_1TB | 8/9_1TB
ra | -0.3743 | 0.6502 | 0.7217 | 1.2627 | -1.1153 | -0.9874
ldp | -0.2096 | 2.9462 | 3.0288 | 3.5925 | -0.8094 | -0.5972
ai | -0.2183 | -0.5635 | -0.4037 | 0.3132 | -1.4564 | -1.3097
ave | -0.2674 | 1.0110 | 1.1156 | 1.7228 | -1.1270 | -0.9647
Lancoz4 Up and Down Sampling for Texture and Bicubic for Depth

## Slide 37
Experimental Results (2-View 2-Depth) HEVC + 5/6 CTDP-2TB with respect to 3D-HEVC
BDBR |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View
 | Texture | Depth |  |  | VSRS
 | 5/6_2TB | 5/6_2TB_D1 | 5/6_2TB_D2 | 5/6_2TB_D3 | 5/6_2TB
ra | 281.0796 | -14.3619 | -14.3901 | -23.1498 | 226.3722
ldp | 212.6822 | -46.3458 | -46.2310 | -51.1193 | 166.7185
ai | 120.6750 | -40.1254 | -40.2415 | -46.5875 | 133.9196
ave | 204.8122 | -33.6110 | -33.6209 | -40.2855 | 175.6701
BDPSNR |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View
 | Texture | Depth |  |  | VSRS
 | 5/6_2TB | 5/6_2TB_D1 | 5/6_2TB_D2 | 5/6_2TB_D3 | 5/6_2TB
ra | -3.4523 | 0.2035 | 0.2203 | 0.6046 | -3.1486
ldp | -3.1293 | 2.0161 | 2.0384 | 2.4799 | -2.7743
ai | -2.1034 | 1.2915 | 1.3636 | 1.8502 | -2.3456
ave | -2.8950 | 1.1703 | 1.2074 | 1.6449 | -2.7562
Lancoz4 Up and Down Sampling for Texture and Bicubic for Depth

## Slide 38
Experimental Results (2-View 2-Depth) HEVC + 8/9 CTDP-2TB with respect to 3D-HEVC
BDBR |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View
 | Texture | Depth |  |  | VSRS
 | 8/9_2TB | 8/9_2TB_D1 | 8/9_2TB_D2 | 8/9_2TB_D3 | 8/9_2TB
ra | 275.0123 | 7.6578 | 7.5698 | -6.2878 | 230.8110
ldp | 209.0862 | -34.4792 | -34.2503 | -40.7517 | 171.1121
ai | 117.8838 | -25.0388 | -24.7130 | -33.3960 | 137.6251
ave | 200.6608 | -17.2867 | -17.1312 | -26.8118 | 179.8494
BDPSNR |  |  |  |  | 
 | Recovered Texture and Depth |  |  |  | Synthesized Virtual View
 | Texture | Depth |  |  | VSRS
 | 8/9_2TB | 8/9_2TB_D1 | 8/9_2TB_D2 | 8/9_2TB_D3 | 8/9_2TB
ra | -3.4115 | -0.5479 | -0.5174 | -0.0245 | -3.1663
ldp | -3.1054 | 1.2126 | 1.2409 | 1.6748 | -2.8149
ai | -2.1073 | 0.2496 | 0.3348 | 0.8719 | -2.4196
ave | -2.8747 | 0.3047 | 0.3528 | 0.8407 | -2.8003
Lancoz4 Up and Down Sampling for Texture and Bicubic for Depth

## Slide 39: 3D_HEVC (1-view 1-depth,ra, Qp=27, view:4, bitrate : 3149.811 Kbps)

## Slide 40: CTDP-1TB (ra, Qp=27, view:4, bitrate : 2661.774 Kbps)

## Slide 41: 3D_HEVC (1-view 1-depth,ra, Qp=27, view:7, bitrate : 3408.615 Kbps)

## Slide 42: CTDP-1TB (ra, Qp=27, view:7, bitrate : 3237.252 Kbps)

## Slide 43: 3D_HEVC (2-view 2-depth,ra, Qp=27, view:4, bitrate : 3710.741 Kbps)

## Slide 44: CTDP-2TB (ra, Qp=27, view:4, bitrate : 3984.372 Kbps)

## Slide 45: 3D_HEVC (2-view 2-depth,ra, Qp=27, view:7, bitrate : 3980.025 Kbps)

## Slide 46: CTDP-2TB (ra, Qp=27, view:7, bitrate : 4660.701 Kbps)

## Slide 47: 3D_HEVC (ra, Qp=27, L view:5, R view:5.5 bitrate : 767kpbs) Kbps)
Video Demos

## Slide 48: CTDP-2LR (ra, Qp=27, L view:5, R view=5.5, bitrate : 738 Kbps)
Video Demos

## Slide 49: CTDP-2LR_DE (ra, Qp=27, R view:5, L view: 5.5, bitrate : 738 Kbps)
Video Demos

## Slide 50: CTDP Adoption Plans in Taiwan

## Slide 51: ChungHwa Telecom’s Adoption Plan
Chunghwa Telecom (CHT) Company with about 1.4 million MOD users has signed an agreement to adopt CTDP format as the following:
1. 04/01/2016: Propose and confirm the test and adoption detailed plan
2. 07/01/2016: Test of downloaded 3D CTDP services with computer clients
(Internal test in CHT and TOUCH Center only)
3. 02/01/2017: Services of 3D MOD services for computer clients
(Charge and open to the public and final CTDP format selection)
4. 02/01/2018: Test of 3D MOD services through Set-top-Boxes with separated CTDP depacking module (Open for selected users)
5. 02/01/2019：Test of 3D MOD services through Set-top-Boxes with Integrated
CTDP depacking module (charged 3D services)

## Slide 52: Hsin Yeong An’s Adoption Plan
Hsin Yeong An (HYA) Cable TV Company with about 145 thousand users is a local cable company near the National Cheng Kung University. The test and adoption plan with time lines are designed as the following:
1. 04/01/2016: Propose and confirm the test and adoption detailed plan
2. 07/01/2016: Test of downloaded 3D CTDP services with computer clients
(Internal test in HYA and TOUCH Center only)
3. 02/01/2017: Services of 3D CATV services for computer clients
(Charge and open to the public and final CTDP format selection)
4. 02/01/2018: Test of 3D CATV services through Set-top-Boxes with separated CTDP depacking module (Open for selected users)
5. 02/01/2019：Test of 3D CATV services through Set-top-Boxes with Integrated CTDP depacking module (charged 3D services)

## Slide 53
2nd
stage
Standard Adoption for 3D TV Services
Naked-eye
3DTV
H.264/AVC
Glasses
3DTV
2D
Videos
CTDP
Packer
5/6-CTDP
(1V+1D)
Videos
CTDP Depacker
with DIBR Engine
RB Glasses
2DTV
H.265/HEVC
8/9- CTDP
(1V+1D)
Videos
8/9- CTDP
(2V+2D)
Videos
3D-HEVC
1V+1D
Viewable
2DTV
DIBR Engine
Multi-view
Multi-depth
Videos
2D
Videos
All 3DTV
1st
stage
3rd
stage
1.5st
stage

## Slide 54: First Stage of 3D Service Delivery in Taiwan
2D
TV
Naked-eye
3D TV
CTDP
Depacker
Exiting
STB
DIBR
Engine
New
Glasses
3D TV
RB-glasses
3D Services
2D TV
SBS
Packing
Old
3D TV
3D Effect Control
Multi-view
Two-View
SbS 3D Video
Mixed 2-View to RB 3D
CTDP
3D
Programs
HDMI
HDMI
HDMI
HDMI
HDMI

## Slide 55: Conclusions
This contribution proposes modified CTDP SEI Message which is an update of the prior contribution JCT3V-M0022 by adding quarter_reduced_depth_line_number, which can precisely specify the downsampling factors of depth and texture, is replaced of all the unprecise syntax terms.
The adaptive depth enhancement method and Lanczos4 resizing filter can be used to further improve the CTDP performances.
Once CTDP SEI Message is accepted by MPEG, ChungHwa Telecom MOD System and Hsin-Yeong An Cable TV Company will adopt CTDP formats for their 3D video services in Taiwan.
Not limited to HEVC, the CTDP formats can be applied to all video coders, such as MPEG-2, H.264/AVC..

## Slide 56
Thanks for your kind attention
Q&A

## Slide 57: 3D_HEVC (1-view 1-depth,ra, Qp=42, view:4, bitrate : 300.6064 Kbps)

## Slide 58: CTDP-1TB (ra, Qp=42, view:4, bitrate : 284.7752 Kbps)

## Slide 59: 3D_HEVC (1-view 1-depth,ra, Qp=42, view:7, bitrate : 375.3256 Kbps)

## Slide 60: CTDP-1TB (ra, Qp=42, view:7, bitrate : 366.288 Kbps)

## Slide 61: 3D_HEVC (2-view 2-depth,ra, Qp=42, view:4, bitrate : 356.1464 Kbps)

## Slide 62: CTDP-2TB (ra, Qp=42, view:4, bitrate : 373.648 Kbps)

## Slide 63: 3D_HEVC (2-view 2-depth,ra, Qp=42, view:7, bitrate : 438.0792 Kbps)

## Slide 64: CTDP-2TB (ra, Qp=42, view:7, bitrate : 420.688 Kbps)