## Slide 1
JCTVC-I0295: Non-CE
On positive/negative sign
for Category 1,4 Edge Offset in SAO
Hak-Sop Song, Chanyul Kim, Joeng-Bum Choi, Jae-Hwan Joo,
Kyo-Hyuk Lee, Jae-Hyun Kim
Samsung Electronics Co., KOREA

## Slide 2
pixel index
x-1
x
x+1
pixel level
category 1
pixel index
x-1
x
x+1
pixel level
category 2
pixel index
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 3
pixel index
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 4
Positive edge offset
Negative edge offset
Edge offset categorization in HM6.0
Positive sign offset for category 1 and 2
Negative sign offset for category 3 and 4
Loss of sharpness and coding gain for special contents

## Slide 3
Proposed method (1/3)
pixel index
x-1
x
x+1
pixel level
category 1
pixel index
x-1
x
x+1
pixel level
category 2
pixel index
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 3
pixel index
x-1
x
x+1
pixel level
pixel index
x-1
x
x+1
pixel level
category 4
Positive/
Negative
Edge offset
Positive/
Negative
Edge offset
Allow positive/negative sign of edge offset for category 1 and 4
Provide coding gain and recover sharpness

## Slide 4
Min_Th(75)
Max_Th(160)
Visibility threshold
Pixel
value
Sensitive
region
Non-sensitive
region
Proposed method (2/3)
Background-luminance dependent function [3]

## Slide 5
if ((category 1 && offset < 0) || (category 4 && offset > 0))
{
if (Min_Th (75) < avgPix < Max_Th (160) && QP>=37) offset = 0;
}
else if (category 2 && offset < 0) offset = 0;
else (offset > 0) offset = 0; // when category 3
Proposed method (3/3)
Offset restriction method using background-luminance dependent function
avgPix : average level of pixels included in each category
Min_Th : Minimum threshold (=75)
Max_TH : Maximum threshold (=160)
QP : Quantization parameter in Slice (=37)

## Slide 6
Objective quality
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.1% | 0.0% | 0.0% | -0.2% | 0.1%
Class C | 0.0% | 0.2% | -0.1% | 0.0% | 0.1% | 0.1%
Class D | 0.1% | 0.1% | 0.4% | 0.0% | 0.0% | -0.3%
Class E | -0.4% | -0.2% | 0.5% | -0.4% | -0.2% | 0.1%
Class F | 0.0% | 0.1% | 0.0% | 0.0% | 0.2% | -0.2%
Overall | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.1%
Enc Time[%] | 98% |  |  | 101% |  | 
Dec Time[%] | 98% |  |  | 102% |  | 
Average coding gain : 0.4% LB-main/LB-HE10 for class E.
Johnny sequence coding gain : 1.1% LB-main, 1.0% LB-HE10.

## Slide 7
Subjective quality (1/8)
BasketballDrive AI_HE10 QP37 Frame 286
HM6.0
Proposed

## Slide 8
Subjective quality (2/8)
BQMall LB_HE10 QP37 Frame 29
HM6.0
Proposed

## Slide 9
Subjective quality (3/8)
BQMall LB_HE10 QP37 Frame 102
HM6.0
Proposed

## Slide 10
Subjective quality (4/8)
BasketballDrive LB_HE10 QP37 Frame 146
HM6.0
Proposed

## Slide 11
Subjective quality (5/8)
BasketballDrive LB_HE10 QP37 Frame 423
HM6.0
Proposed

## Slide 12
Subjective quality (6/8)
BasketballDrillText LB_HE10 QP37 Frame 351
HM6.0
Proposed

## Slide 13
Subjective quality (7/8)
BQTerace AI_HE10 QP37 Frame 194
HM6.0
Proposed

## Slide 14
Subjective quality (8/8)
ChinaSpeed AI_HE10 QP37 Frame 499
HM6.0
Proposed

## Slide 15
Conclusion
Recommend the proposed method to be adapted
  Average coding gain : 0.4% LB-main/LB-HE10 for class E.
  Johnny coding gain : 1.1% LB-main, 1.0% LB-HE10.
Subjective quality is similar to HM6.0

## Slide 16
Reference
[1] B. Bross, W.-J. Han, J.-R. Ohm, G. J. Sullivan, T. Wiegand, “High efficiency video coding (HEVC) text specification draft 6,” ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, Document JCTVC-H1003, Feb. 2012.
[2] W.-S. Kim, D.-K Kwon, “CE8 subset c: Necessity of Sign Bits for SAO Offsets,’’ ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, Document JCTVC-H0434, Feb. 2012.
[3] C.-H. Chou and Y.-C. Li, “A perceptually tuned subband image coder based on the measure of just noticeable distortion profile”, IEEE Trans. on CSVT, vol.5, no. 6, Dec. 1995.
[4] F. Bossen, “Common test conditions,” ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, Document JCTVC-H1100, Feb. 2012.

## Slide 17
WD Text Changes (adds marked in yellow)
sao_offset_vlc( rx, ry, cIdx ) { | Descriptor
sao_type_idx[ cIdx ][ rx ][ ry ] | ue(v)
if( sao_type_idx[ cIdx ][ rx ][ ry ] = =5 ) { | 
sao_band_position[ cIdx ][ rx ][ ry ] | u(5)
for( i = 0; i < 4; i++ ) | 
sao_offset[ cIdx ][ rx][ ry ][ i ] | se(v)
} else if( sao_type_idx[ cIdx ][ rx ][ ry ] != 0 ) | 
for( i = 0; i < 4; i++ ){ | 
if(i == 0 ¦¦ i==3) | 
Sao_offset[ cIdx ][ rx][ ry ][ i ] | se(v)
else | 
sao_offset[ cIdx ][ rx][ ry ][ i ] | ue(v)
} | 
7.2.2.8 Sample adaptive offset VLC syntax

## Slide 18
WD Text Changes (adds marked in yellow)
7.4.3.4 Sample adaptive offset VLC sementics
sao_offset[ cIdx ][ rx ][ ry ][ i ] indicates the offset value of i-th category of current coding treeblock at position rx and ry for the colour component cIdx.
The variable bitDepth is derived as follows.
If cIdx is equal to 0, bitDepth is set equal to BitDepthY..
Otherwise (cIdx is equal to1 or 2), bitDepth is set equal to BitDepthC.
The values of sao_offset[ cIdx ][ rx ][ ry ][ i ] shall be in the range of −( 1<< ( Min( bitDepth, 10 ) − 5 ) ) to ( 1<< ( Min( bitDepth, 10 ) −1.
When sao_offset[ cIdx ][ rx ][ ry ][ i ] is not present, it is inferred as follows.
If sao_merge_up_flag is equal to 1, sao_offset[ cIdx ][ rx ][ ry ][ i ] is set equal to sao_offset[ cIdx ][ rx ][ ry − 1 ][ i ].
Otherwise, sao_offset[ cIdx ][ rx ][ ry ][ i ] is set equal to sao_offset[ cIdx ][ rx − 1 ][ ry ][ i ].
The variable offsetSign is derived as follows.

## Slide 19
WD Text Changes (adds marked in yellow)
If sao_type_idx[ cIdx ][ rx ][ ry ] is less than 5 and i is larger than 1,offsetSign is set to −1.
Otherwise (sao_type_idx[ cIdx ][ rx ][ ry ] is equal to 5 or i is less than 2), offsetSign is set to 1.
If sao_type_idx[ cIdx ][ rx ][ ry ] is less than 5 and i is 2,offsetSign is set to −1.
Otherwise, offset is set to 1.
The array SaoOffsetVal is derived as follows.
SaoOffsetVal[ cIdx ][ rx ][ ry ][ 0 ] = 0 (7‑36)
SaoOffsetVal[ cIdx ][ rx ][ ry ][ i + 1 ] = offsetSign*sao_offset[ cIdx ][ rx ][ ry ][ i ] << ( bitDepth – Min( bitDepth, 10 ) ) (7‑37)
9.2.2.x Sample adaptive offset binarization process
Input to this process is sao_type_idx, SaoOffsetVal and category index i.
Output to this process is the Binarization of the syntax element.
if sao_type_index[cIdx][rx][ry] is not equal to 5 and category index is 0 and 3, the binarization type is unary.
Otherwise, the binarization type is signed unary.