## Slide 1: Tree syntax for field sequence SEI
Geneva
April 2012
JCTVC I-393 & I-062

## Slide 2: Section D.1.19 of HEVC CD
field_indication( payloadSize ) { | Descriptor
sequence_type_flag | u(1)
progressive_source_flag | u(1)
bottom_field_flag | u(1)
top_field_first_flag | u(1)
duplicate_flag | u(1)
reserved_zero_3bits /* equal to 0 */ | u(3)
} | 

## Slide 3: Problem: some combinations are not meaningful (indicated by “X”)
Use case | field_sequence | progressive_source | bottom_field | top_field_first
Interleaved fields, bottom field output first | 0 | 0 | X | 0
Interleaved fields, top field output first | 0 | 0 | X | 1
Progressive frame | 0 | 1 | X | X
Top field picture | 1 | 0 | 0 | X
Bottom field picture | 1 | 0 | 1 | X
Top field extracted from a progressive frame | 1 | 1 | 0 | X
Bottom field extracted from a progressive frame | 1 | 1 | 1 | X

## Slide 4: Meaningful use cases
sequence
frame seq
bottom
first
prog
frame
field seq
field picture
progressive_source_flag
bottom_field_flag
top_field_first_flag
top
first
inter-leaved
extracted field
Top
FieldSequenceFlag
Bottom
Top
Bottom
X
X
X
X
X

## Slide 5: Observations
top_field_first and bottom_field are mutually exclusive:
  bottom_field (field parity) always needed in field sequences; not meaningful in frame sequences.
  top_field_first only needs to be signalled in frame sequences containing interlaced content (“interlaced frames”) to know which field should be output first (field_sequence_flag == 0 && progressive_source_flag == 1 )
Neither top_field_first nor bottom_field needed in pure progressive frame sequences (field_sequence_flag == 0 && progressive_source_flag == 1 )
Possible solution: eliminate combinations that are not meaningful by making them impossible to signal via a conditional tree syntax.

## Slide 6: Tree version of syntax
field_sequence_flag
progressive_source_flag
duplicate_flag
top_field_first
bottom_field
SEI
field_sequence_flag?
0
1
0
1
Interleaved fields
progressive_source_flag?
reserved_zero_1bit
Frame sequences
Field sequences
Pure progressive
frames

## Slide 7: Pseudo-code tree syntax
field_indication(8 bits)
{
field_sequence_flag(1 bit) // 0: frame sequences
// 1: field sequences
progressive_source_flag(1 bit) // 0: interlaced content
// 1: progressive content
duplicate_flag(1 bit) // dummy picture?
if( field_sequence_flag == 1 )
{
bottom_field_flag(1 bit) // 0: top, 1: bottom
}
else if( progressive_source==0 )
{
top_field_first( 1 bit) // 0: bottom 1st, 1: top 1st
}
else
reserved_zero_1bit( 1 bit ) // pure progressive frames
reserved_zero_4bits // equal to 0
}