## Slide 1: Transform Selection for Inter-Layer Texture Prediction in Scalable Video Coding (JCTVC-K0321)
Liwei Guo, Marta Karczewicz, Joel Sole, Jianle Chen

## Slide 2: Introduction
Inter-layer texture prediction
  An popular tool in SVC proposals
    Intra BL mode, reconstructed BL as reference frame…
    Enhancement layer pixel values predicted using reconstructed base layer pixel values
  Residue characteristic can be different from that of single layer residue
    DCT Type-2 (transform in HEVC main profile) may not be efficient
Proposed:
  Additional two DCT/DST transforms for inter-layer texture prediction residues
  All 3 transforms share the current butterfly pipeline in HM

## Slide 3: Transform Selection
Multiple transform candidates
  Applied to luma component of inter-layer texture prediction residues
  The selected transform is signaled to the decoder
    Truncated unary codes
    Additional 8 contexts (# CU sizes X # bins)
  Chroma component only uses DCT-Type 2
transform_selection_index | Codes | Transform
0 | 0 | DST Type-3
1 | 10 | DCT Type-2 (HEVC transform)
2 | 11 | DCT Type-3

## Slide 4: Butterfly Implementation
Relations of DCT Type-3, DST Type-3 and DCT Type-2
  Let A, B and C be NxN DCT Type-2, DCT Type-3 and DST Type-3
    , for even i;
    , for odd i.
Implementation can reuse butterfly pipeline for DCT Type-2 in HM
  DCT Type-3
    Forward (inverse) transform uses inverse (forward) transform butterfly of DCT Type-2
  DST Type-3
    Similar approach to that of DCT Type-3
    Additional row flipping and sign inverting for odd columns of inputs

## Slide 5: Simulation-settings
Codebase: Qualcomm’s SVC response software K0035
Anchor: Only DCT Type-2 transform for Inter-layer texture prediction (Intra BL mode)
Settings: SVC CfP settings* without rate matching
Scalability | Base Layer QP | Enhancement Layer QP
Spatial 2X | 22, 26, 30, 34 | Baselayer QP -2, +0, +2, +4
Spatial 1.5X | 22, 26, 30, 34 | Baselayer QP -2, +0, +2, +4
*ISO/IEC JTC1/SC29/WG11 and ITU-T SG 16, “Joint Call for Proposals on Scalable Video Coding
Extensions of High Efficiency Video Coding (HEVC)”, ISO/IEC JTC 1/SC 29/WG 11 (MPEG)
Doc. N12957, Stockholm, Sweden, July 2012.

## Slide 6: Simulation-results
BD-rate calculated using both EL and BL rates
 | All Intra HEVC 2x |  |  | All Intra HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A+ | -1.69% | 1.17% | 1.16% |  |  | 
Class B | -1.42% | 0.99% | 0.97% | -1.27% | 1.49% | 1.50%
Overall | -1.55% | 1.08% | 1.07% | -1.27% | 1.49% | 1.50%

## Slide 7: Conclusions
Proposed transform selection for inter-layer texture prediction residue
  Additional 2 transforms for luma component
  All 3 transforms share current butterfly structure in HM software
Y BD-rate reduction
  AI-2X 1.55%;
  AI-1.5X 1.27%

## Slide 8
Thank you!