## Slide 1
On secondary transforms for Intra_BL
residue
JCTVC-M0033
Ankur Saxena and Felix Fernandes
Samsung Electronics, Co. Ltd.
Dallas R & D Research Center

## Slide 2: Motivation and Prior Work
DCT is not necessarily the optimal transform for Intra_BL residue
Prior Work :
L. Guo, M. Karczewicz, J. Sole, and J. Chen, JCTVC-K0321
L. Guo, M. Karczewicz, and J. Chen, JCTVC-L0330
  Full size 8x8, 16x16 and 32x32 additional transforms were proposed there.
  Gains of around 1.7% and 1.5% were obtained for AI 2x and AI 1.5x scenario.
Since additional transforms are expensive to implement at larger sizes, e.g., 32x32, we propose to use secondary transforms.

## Slide 3: Overview
Currently in SHM 1.0,
  For Luma Intra_BL 4x4 Residue: DST is used.
  For 8x8 and larger Luma Intra_BL residue, DCT is used
Proposal: Apply secondary transforms for Intra_BL residue at TU size 8x8 and larger (Luma only)
  No changes to Chroma and 4x4 Intra_BL TU’s
  Gains of 1.4 % and 0.9 % obtained for AI 2x and AI 1.5x scenarios.
Fast factorization/implementation of secondary transforms also proposed.
  Proposed Secondary Transform requires 22 mults and 58 adds
  Note : A full 8x8 transform implementation via matrix multiplication requires 64 mults and 56 adds.
  A low-complexity ROTation transform requiring only 20 mults and 12 adds is also presented.

## Slide 4: Improvements over secondary transforms proposed for HEVC
Fast implementation of secondary transforms
  Only 22 mults as compared to 64 mults for full 8x8 matrix multiplication.
  Low complexity secondary transform can even have 15 mults
In HEVC, the smaller blocks were providing more gains: e.g., 8x8.
In S-HEVC, in EL the larger blocks, e.g., 32x32 are providing larger gains
  So we can avoid applying secondary transform on 8x8 blocks (worst-case), and still get most of the gains.

## Slide 5: Different Tests
Case 1: At CU level, perform a R-D search to choose between:
(a) DCT
(b) DCT + Secondary Transform 1
Case 2: At CU level, perform a R-D search to choose between:
(a) DCT
(b) DCT + Secondary Transform 1
(c) DCT + Secondary Transform 2
Transmit a flag for transform choice per CU.

## Slide 6: Algorithm Description: Decoder
Trigger Conditions
Decoder Operations
Inverse DCT
Inverse Quantizer
Inverse Secondary Transform
TU >=8 ; Mode == Intra_BL ; Text_Luma;
and useSecTransFlag ==1
Inverse DCT
Inverse Quantizer

## Slide 7: Secondary Transform Matrices
[ 120 39 -20 -4 -9 -4 -4 -2
-33 114 37 -29 -1 -11 -2 -3
26 -26 116 22 -33 -2 -10 -1
-9 29 -14 119 4 -33 -2 -7
14 -6 27 -3 120 -15 -30 -3
-1 16 0 26 8 118 -33 -22
8 2 14 6 26 20 114 -45
4 9 7 13 14 27 36 118 ]
[ 120 -39 -20 4 -9 4 -4 2
33 114 -37 -29 1 -11 2 -3
26 26 116 -22 -33 2 -10 1
9 29 14 119 -4 -33 2 -7
14 6 27 3 120 15 -30 3
1 16 0 26 -8 118 33 -22
8 -2 14 -6 26 -20 114 45
-4 9 -7 13 -14 27 -36 118 ]
Secondary Transform matrices.
The two matrices differ in sign change for a few coefficients only.
Fast factorization with 22 mults and 58 adds as compared to 64 mults, and 56 adds for 8x8 matrix multiplication
1st Secondary Transform Matrix
2nd Secondary Transform Matrix

## Slide 8: Low-complexity Secondary Transform ROT Matrix
{ 87, -93, 12, 0, 0, 0, 0, 0,},
{ 91, 79, -44, 0, 0, 0, 0, 0,},
{ 25, 38, 120, 0, 0, 0, 0, 0,},
{ 0, 0, 0, 118, -50, -5, 0, 0,},
{ 0, 0, 0, -50, -118, -13, 0, 0,},
{ 0, 0, 0, 1, 14, -128, 0, 0,},
{ 0, 0, 0, 0, 0, 0, 128, 0,},
{ 0, 0, 0, 0, 0, 0, 0, 128,}
Sparse matrix. Implementation in 20 mults and 12 adds
The second secondary matrix is simply the transpose of ROT matrix above
Operations can be further reduced via lifting implementations (JCTVC-C096, JCTVC-G304) to 15 mults.

## Slide 9: Summary of Results
Test Number | # of secondary Transforms tested | Type of Secondary Transform | TU sizes on which secondary transform applied | AI 2x Y | AI 1.5x Y | Average Luma gain | Average Encoding Time | Average Decoding Time
1 | 1 | SecTrans | 8 to 32 | -1.0% | -0.6% | -0.8% | 112% | 103%
2 | 2 | SecTrans | 8 to 32 | -1.4% | -0.9% | -1.2% | 125% | 104%
3 | 1 | ROT | 8 to 32 | -0.8% | -0.4% | -0.6% | 111% | 101%
4 | 2 | ROT and Transpose | 8 to 32 | -1.1% | -0.6% | -0.9% | 124% | 102%
Notes: Additional encoding complexity (times) can be further reduced to half by using a fast search as in JCTVC-L0330.

## Slide 10: Complexity: Operation Counts
 |  |  |  |  | Worst Case | Worst Case | Average Case | Average Case
 |  | Operations for 2-d DCT | Proposed Sec Trans | Proposed ROT | % increase for Sec Trans | % increase for ROT | % increase for Sec Trans | % increase for ROT
TU Size |  | SHM 1.0 DCT |  |  |  |  |  | 
4x4 | Mults | 48 | N/A | N/A | N/A | N/A | N/A | N/A
 | Adds | 96 | N/A | N/A | N/A | N/A | N/A | N/A
8x8 | Mults | 352 | 352 | 320 | 100% | 91% | 50% | 45%
 | Adds | 576 | 928 | 192 | 161% | 33% | 81% | 17%
16x16 | Mults | 2752 | 352 | 320 | 13% | 12% | 6% | 6%
 | Adds | 3712 | 928 | 192 | 25% | 5% | 13% | 3%
32x32 | Mults | 21888 | 352 | 320 | 2% | 1% | 1% | 1%
 | Adds | 25856 | 928 | 192 | 4% | 1% | 2% | 0%

## Slide 11: Summary of Results (2)
Test Number | # of secondary Transforms tested | Type of Secondary Transform | TU sizes on which secondary transform applied | AI 2x Y | AI 1.5x Y | Average Luma gain | Average Encoding Time | Average Decoding Time
1 | 1 | SecTrans | 8 to 32 | -1.0% | -0.6% | -0.8% | 112% | 103%
2 | 2 | SecTrans | 8 to 32 | -1.4% | -0.9% | -1.2% | 125% | 104%
3 | 1 | ROT | 8 to 32 | -0.8% | -0.4% | -0.6% | 111% | 101%
4 | 2 | ROT and Transpose | 8 to 32 | -1.1% | -0.6% | -0.9% | 124% | 102%
5 | 2 | SecTrans | 16 and 32 | -0.9 | -0.5 | -0.7 | 123% | 103%
6 | 2 | ROT | 16 and 32 | -0.8 | -0.4 | -0.6 | 123% | 103%
Notes: Additional encoding complexity (times) can be further reduced to half by using a fast search as in JCTVC-L0330.

## Slide 12: Conclusions
Proposed secondary transform provides upto 1.4 % and 0.9 % gain for All Intra 2x and 1.5x cases respectively.
Presented fast factorization for secondary transforms.
Additional decoding complexity is marginal.
Recommend to adopt proposed secondary transform, or test in a Core Experiment for Transforms/Intra_BL residue.