## Slide 1: Adaptive bit allocation for R-λ model rate control in HM
University of Science and Technology of China

## Slide 2: Motivation
Adaptive bit allocation for rate control algorithm
  1.9%~2.9% performance improvement
  No significant impact on the running time
Four modifications
  Bug fix on the condition of parameter updating
  Picture level adaptive bit allocation
  Refined basic unit level bit allocation
  Rate control for intra coded pictures

## Slide 3: Condition on parameter updating
HM-10.0 rate control
  May not be able to update model parameters properly for very low delay case (e.g. Johnny LP-Main @ 98 kbps)
Fix this bug by removing about 19 lines

## Slide 4: Picture level adaptive bit allocation
HM-10.0 picture level bit allocation
  Allocate bits according to the predetermined weight
Proposed
  Allocate bits according to expected lambda ratio

## Slide 5: Picture level adaptive bit allocation (Cont.)
Lambda ratios are determined by analysis of HM reference software under CTC
Numerical method to solve the problem
  1.4%~2.2% performance gain
  By adding about 145 lines of code, mainly in TEncRateCtrl.cpp

## Slide 6: Refined basic unit level bit allocation
HM-10.0 basic unit level bit allocation
  By estimated prediction error
Refined bit allocation
  Similar to picture level bit allocation
  A net reduction of about 69 lines of code

## Slide 7: Rate control for intra coded pictures
Change one line to enable basic unit level rate control
Enlarge the clip range for parameter alpha
  Original [0.05, 20]
  Modified [0.05, 500]
Parameter updating
  Larger bpp for intra pictures, quicker updating
Basic unit level bit allocation (from JCTVC-M0036)
  All remaining LCUs smooth  next four LCUs smooth
  Helpful to improve coding efficiency
No pre-analysis process is introduced for normal intra coding structure

## Slide 8: Experimental results
Average Y BD-Rate (HM-10.0 as anchor)
 | HM-10.0 RC | Bug fix | BU level | picture level | All enabled
RA-Main | 5.3% | 5.2% | 4.7% | 3.1% | 2.4%
RA-Main10 | 5.2% | 5.2% | 4.5% | 3.0% | 2.3%
LB-Main | 3.8% | 3.8% | 3.9% | 2.1% | 1.9%
LB-Main10 | 3.9% | 3.9% | 3.8% | 2.2% | 1.9%
LP-Main | 3.1% | 3.1% | 3.0% | 1.6% | 1.4%
LP-Main10 | 3.0% | 3.0% | 2.7% | 1.6% | 1.2%

## Slide 9: Bitrate accuracy
 | HM-10.0 RC bitrate error |  | adaptive bit allocation enabled RC bitrate error | 
 | Average | Maximum | Average | Maximum
RA-Main | 0.25% | 3.01% | 0.22% | 2.70%
RA-Main10 | 0.27% | 2.82% | 0.23% | 2.44%
LB-Main | 0.12% | 1.40% | 0.09% | 0.83%
LB-Main10 | 0.17% | 1.53% | 0.13% | 0.91%
LP-Main | 0.14% | 1.44% | 0.10% | 0.82%
LP-Main10 | 0.16% | 1.48% | 0.12% | 1.01%

## Slide 10: Results with modifications for intra pictures
 | Y BD-Rate | average bitrate error | maximum bitrate error | Enc. Time | Dec. Time
AI-Main | 0.8% | 0.00% | 0.04% | 101% | 97%
AI-Main10 | 0.7% | 0.00% | 0.09% | 100% | 97%
RA-Main | 2.5% | 0.18% | 2.44% | 99% | 101%
RA-Main10 | 2.4% | 0.19% | 2.15% | 99% | 101%
LB-Main | 1.8% | 0.07% | 0.54% | 99% | 101%
LB-Main10 | 1.7% | 0.11% | 0.72% | 99% | 101%
LP-Main | 1.1% | 0.09% | 0.69% | 99% | 101%
LP-Main10 | 0.9% | 0.10% | 1.02% | 99% | 101%

## Slide 11: Picture by picture rate control
Constant number of bits is assigned to each picture
Have to estimated the complexity of the current picture is updating is not allowed
  Complexity C is estimated by 8x8 SATD (without DC)
  C is used to determine the model parameters
    alpha = 0.0071*power(C, 2.69)
    beta = -2.0

## Slide 12: Picture by picture result
 | AI-Main |  | AI-Main10 | 
 | average Y BD-Rate | average bitrate error | average Y BD-Rate | average bitrate error
w/o LCU RC, w/o updating | 0.0% | 15.1% | -0.1% | 15.1%
w LCU RC, w/o updating | 1.9% | 5.2% | 1.8% | 5.1%
w/o LCU RC, w updating | 0.3% | 2.1% | 0.3% | 2.1%
w LCU RC, w updating | 0.7% | 0.6% | 0.7% | 0.3%

## Slide 13: Conclusion
Suggest to include the bug fix, adaptive bit allocation, and the rate control for intra coded pictures in the next release of HM

## Slide 14
Thank you!