## Slide 1: <JCTVC-N0157/JCT3V-E0076> MV-HEVC/SHVC HLS: On signalling of sps_max_sub_layers_minus1
Jung Won Kang

## Slide 2: Problem Statement
In the SHVC draft text 2.0 and MV-HEVC draft text 4.0
  Parsing dependency between SPS and VPS
    For layer with nuh_layer_id >0, sps_max_sub_layers_minus1 is inferred to be vps_max_sub_layers_minus1
    DPB related parameters depend on sps_max_sub_layers_minus1
seq_parameter_set_rbsp( ) { | Descriptor
sps_video_parameter_set_id | u(4)
if( nuh_layer_id = = 0 ) { | 
sps_max_sub_layers_minus1 | u(3)
sps_temporal_id_nesting_flag | u(1)
profile_tier_level( 1, sps_max_sub_layers_minus1 ) | 
} | 
… | 
sps_sub_layer_ordering_info_present_flag | u(1)
for( i = ( sps_sub_layer_ordering_info_present_flag ? 0 : sps_max_sub_layers_minus1 ); i <= sps_max_sub_layers_minus1; i++ ) { | 
sps_max_dec_pic_buffering_minus1[ i ] | ue(v)
sps_max_num_reorder_pics[ i ] | ue(v)
sps_max_latency_increase_plus1[ i ] | ue(v)
} | 
} | 

## Slide 3: Problem Statement
In the SHVC draft text 2.0 and MV-HEVC draft text 4.0
  Singalling the maximum number of sub-layers for each layer
    vps_max_sub_layers_minus1 + 1: the max. num. of sub-layers in the bitstream
    Frame rate for each layers can be different in SHVC
     For layer with nuh_layer_id >0,
    sps_max_sub_layers_minus1 <= vps_max_sub_layers_minus1
seq_parameter_set_rbsp( ) { | Descriptor
sps_video_parameter_set_id | u(4)
if( nuh_layer_id = = 0 ) { | 
sps_max_sub_layers_minus1 | u(3)
sps_temporal_id_nesting_flag | u(1)
profile_tier_level( 1, sps_max_sub_layers_minus1 ) | 
} | 
… | 
sps_sub_layer_ordering_info_present_flag | u(1)
for( i = ( sps_sub_layer_ordering_info_present_flag ? 0 : sps_max_sub_layers_minus1 ); i <= sps_max_sub_layers_minus1; i++ ) { | 
sps_max_dec_pic_buffering_minus1[ i ] | ue(v)
sps_max_num_reorder_pics[ i ] | ue(v)
sps_max_latency_increase_plus1[ i ] | ue(v)
} | 
} | 
Notes: There is unnecessary signalling of DPB-related paramteres since sps_max_sub_layers_minus1 is inferred to be vps_max_sub_layers_minus1 for EL.

## Slide 4: Proposal
Signalling the maximum number of sub-layers for each layer in VPS extension
  When max_sub_layers_vps_prediction_flag[i]==1
   max_sub_layers_vps_minus1[i] = vps_max_sub_layers_minus1
vps_extension( ) { | Descriptor
… | 
for( i = 1; i <= vps_max_layers_minus1; i ++ ) { | 
max_sub_layers_vps_prediction_flag[i] | u(1)
if(!max_sub_layers_vps_prediction_flag[i]) | 
max_sub_layers_vps_minus1[i] | u(3)
} | 
… | 
} | 
Notes: The first proposal is to signal the maximum number of sub-layers for each layer in VPS extension

## Slide 5: Proposal
Signalling syntax elements which are DPB related parameters in VPS extension
  Assumption: each layer has a different DPB.
  For nuh_layer_id>0, max_dec_pic_buffering, max_num_reorder_pics, and max_latency_increase_plus1 are signalled in VPS extension for each sub-layer in each layer.
    Since the decoding process should depend on output layer set, max. DPB size for each layer in each output layer set is derived by max_dec_pic_buffering for each layer signalled in VPS extension.
vps_extension( ) { | Descriptor
… | 
for( i = 1; i <= vps_max_layers_minus1; i ++ ) { | 
if(max_sub_layers_vps_prediction_flag[i]) | 
sub_layer_ordering_info_vps_prediction_flag[i] | u(1)
if(!sub_layer_ordering_info_vps_prediction_flag[i]) | 
sub_layer_ordering_info_vps_present_flag[i] | u(1)
for( j = ( sub_layer_ordering_info_vps_present_flag[i] ? 0 : max_sub_layers_vps_minus1[i] ); j <= max_sub_layers_vps_minus1[i]; i++ ) { | 
max_dec_pic_buffering_minus1[ i ][ j ] | ue(v)
max_num_reorder_pics[ i ][ j ] | ue(v)
max_latency_increase_plus1[ i ][ j] | ue(v)
} | 
} | 
} | 
… | 
} | 
Notes: The second proposal is to signal syntax elements which are DPB related parameters in VPS extension
The assumption in this proposal is that each layer has a different DPB, and there is independent management of DPB for each layer

## Slide 6: Proposal
Signalling syntax elements which are DPB related parameters in VPS extension
  Max. DPB size of whose layer is an output layer should be different from max. DPB size whose layer is not an output layer.
    When a layer is an output layer, all pictures in the output layer is decoded.
    When a layer is not an output layer, a picture that is not used for inter-layer prediction in the output layer is not needed to be decoded.
Layer
N-1
Layer N
Tid
K-1
T-2
K-1
T-1
T-1
T
T
T
T
In the proposal
vps_max_sub_layers_minus1 = T
For Layer N, 0<= j <=T,
max_dec_pic_buffering[N][j]
max_num_reorder_pics[N][j] max_latency_increase_plus1[N][j]
For Layer N-1, 0<= j <= T-1,
max_dec_pic_buffering[N-1][j]
max_num_reorder_pics[N-1][j] max_latency_increase_plus1[N-1][j]
max_tid_il_ref_pics_plus1[N-1]=K
When layer N-1 is an output layer,
For Layer N-1, 0<=j <=T-1,
max_dec_pic_buffering[N-1][j]
max_num_reorder_pics[N-1][j] max_latency_increase_plus1[N-1][j]

## Slide 7: Proposal
Signalling syntax elements which are DPB related parameters in VPS extension
In the proposal
vps_max_sub_layers_minus1 = T
For Layer N, 0<= j <=T,
max_dec_pic_buffering[N][j]
max_num_reorder_pics[N][j] max_latency_increase_plus1[N][j]
For Layer N-1, 0<= j <= T-1,
max_dec_pic_buffering[N-1][j]
max_num_reorder_pics[N-1][j] max_latency_increase_plus1[N-1][j]
max_tid_il_ref_pics_plus1[N-1]=K
When layer N-1 is not an output layer,
For Layer N-1, 0<=j <=K-1,
max_dec_pic_buffering[N-1][j]
max_num_reorder_pics[N-1][j] max_latency_increase_plus1[N-1][j]
For Layer N-1, K <= j <=T
max_dec_pic_buffering[N-1][j] = max_dec_pic_buffering[N-1][K-1]
max_num_reorder_pics[N-1][j] = max_num_reorder_pics[N-1][K-1]
max_latency_increase_plus1[N-1][j] = max_latency_increase_plus1[N-1][K-1]
Layer
N-1
Layer N
Tid
K-1
T-2
K-1
T-1
T-1
T
T
T
T