## Slide 1: JCTVC-N0180 Color Mapping SEI message
P.Bordes
14th JCT-VC Meeting: Vienna, July 25- August 2nd, 2013

## Slide 2: Color Mapping SEI message
  Purpose
    Color mapping SEI message to support color mapping post-processing on reconstructed frames.
    The color mapping function is coded using a 3D Color LUT
  Context
    Several Color formats (primaries) supported (signalling) in HEVC syntax (VUI, SEI-Tone-mapping)
    Some end-devices may not support all formats because:
      Limited rendering capability
      New Color formats (ex: BT.2020)
      Historical obsolete or make no sense vs device/application
      Unspecified color format

## Slide 3: Color Mapping SEI message
new
future
historical
unspecified

## Slide 4: Color Mapping SEI message
  The Color LUT allows to map the reconstructed frames to supported color format
  Advantages
    To increase color adaptability (end-devices not supporting all color format)
    To preserve colorist intent when converting color graded content
    To provide color mapping function tailored to particular applications
    Color LUTs is a common and universal color mapping format

## Slide 5: Color Mapping SEI message syntax
nuh_layer_id identifies the layer of the reconstructed frames to which the 3D color lut should be applied.
color_map_id, color_map_cancel_flag, color_map_repetition_period semantic is same as tone_map_id, tone_map_cancel_flag and tone_map_repetition_period defined in SEI tone mapping.
color_primaries_input_id indicates the chromaticity coordinates of the source primaries as specified in Table 4 in terms of the CIE 1931 definition of x and y as specified by ISO 11664-1.
color_primaries_output_id indicates the chromaticity coordinates of the color mapped primaries as specified in Table 5 in terms of the CIE 1931 definition of x and y as specified by ISO 11664-1, once the 3D color lut is applied.
color_output_rgb equal to 1 specifies the output color samples are luma and chroma signals. Color_output_rgb equal to 0 specifies the output color samples are green, red, blue values.
lut_bit_depth_minus8 specifies the bit depth of the 3D lut samples.
color_mapping_info( payloadSize ) { | Descriptor
color_map_id | ue(v)
color_map_cancel_flag | u(1)
if( !color_map_cancel_flag ) { | 
color_map_repetition_period | ue(v)
color_description_present_flag | u(1)
If (colour_description_present_flag) { | 
color_primaries_input_id | u(8)
color_primaries_output_id | u(8)
} | 
color_ output_rgb | u(1)
lut_bit_depth_minus8 | u(4)
3D_ LUT_ color_data ( ) | 
} | 
} | 

## Slide 6: Color LUT coding syntax
Octree based coding using DPCM coding of YUV color vertices
  Unused (or less used) 3D color space regions are encoded with coarsely lattice size
  Each color component of a vertex is predicted with previously encoded color components of neighboring parent octant vertices
encoded_vertex_flag[i] indicates whether the residual components values (resY[i],resU[i], resV[i]) are encoded or all inferred to be zero.
split_octant_flag specifies whether an octant is split into octants with half horizontal and vertical size. The values (y,u,v) specify the location of the first vertex in the 3D LUT.
coding_octant ( layer_id, y,u,v) { | Descriptor
for( i = 0; i < 8 ; i++ ) { | 
encoded_vertex_flag[i] | u(1)
if ( encoded_vertex_flag[i] ) { | 
resY[i] | ue(v)
resU[i] | ue(v)
resV[i] | ue(v)
} | 
} | 
split_octant_flag | u(1)
if ( split_octant_flag ) { | 
for( i = 0; i < 8 ; i++ ) { | 
coding_octant ( layer_id+1, y+dy[i],u+du[i],v+dv[i]) | 
} | 
} | 
} |