## Slide 1
JCTVC-N0232
Non-RCE2: Rice parameter update method
Junghye Min, Sunil Lee, Chanyul Kim

## Slide 2: Summary
A rice parameter update method for transform skip and transform bypass block is proposed.
  One condition check is removed.
  Rice parameter is set as
    Method 1
      uiGoRiceParam = min<UInt>(uiGoRiceParam+ ((absCoeff[idx]+3)>>(uiGoRiceParam+3)), RICE_ MAX);
    Method 2
      uiGoRiceParam = min<UInt>(uiGoRiceParam+ ((absCoeff[idx]+4)>>(uiGoRiceParam+3)), RICE_ MAX);
Performance (AI, lossless )
 | Method 1 | Method 2
Class F | -1.4% | -1.4%
Class D | -0.7% | -0.3%
SC RGB 444 | -9.1 | -9.2%
SC YUV 444 | -4.0% | -4.1%
RangeExt | -0.5% | -0.9%

## Slide 3: Introductions
Current rice parameter update process was optimized for coefficient coding especially where absCoeffs (absolute value of coefficient level ) are increased as the coefficient position approaches the left top position in the transform units.
Rice parameter update process optimized for transform skip or transform by-pass is needed.

## Slide 4: Proposed method
Original method
  if(absCoeff[idx] > 3*(1<<uiGoRiceParam))
  {
  uiGoRiceParam = min<UInt>(uiGoRiceParam+ 1, 4);
  }
Proposed method 1)
  uiGoRiceParam = min<UInt>(uiGoRiceParam+ ((absCoeff[idx]+3)>>(uiGoRiceParam+3)), RICE_ MAX);
Proposed method 2)
  uiGoRiceParam = min<UInt>(uiGoRiceParam+ ((absCoeff[idx]+4)>>(uiGoRiceParam+3)), RICE_ MAX);
  RICE_MAX : 4,5, or 6

## Slide 5: Experimental results
(Lossless)
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.3 | -1.4% | 31.7 | 32.1 | -0.8% | 49.8 | 50.2 | -0.5%
Class B | 2.2 | 2.3 | -0.7% | 2.6 | 2.6 | -1.1% | 2.6 | 2.6 | -1.1%
SC RGB 444 | 10.1 | 10.9 | -6.9% | 100.4 | 109.2 | -5.6% | 381.6 | 420.4 | -5.3%
SC YUV 444 | 11.4 | 12.0 | -3.7% | 128.9 | 135.9 | -3.2% | 325.6 | 351.5 | -3.7%
RangeExt | 2.4 | 2.4 | -0.6% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 101% |  | 
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.3 | -1.4% | 31.7 | 32.1 | -0.8% | 49.8 | 50.1 | -0.5%
Class B | 2.2 | 2.3 | -0.7% | 2.6 | 2.6 | -1.1% | 2.6 | 2.6 | -1.1%
SC RGB 444 | 10.1 | 11.3 | -9.1% | 100.4 | 113.3 | -7.7% | 381.6 | 438.8 | -7.3%
SC YUV 444 | 11.4 | 12.0 | -4.0% | 128.9 | 136.7 | -3.6% | 325.6 | 354.9 | -4.0%
RangeExt | 2.4 | 2.4 | -0.5% | 2.5 | 2.5 | 0.0% | 2.5 | 2.5 | 0.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 101% |  |  | 99% |  | 
Method 1
RICE_ MAX=5
RICE_ MAX=6
MAX : cad-waveform
AI ,-15.1%
Performance gains are observed for all classes

## Slide 6: Experimental results
(Lossy)
RICE_ MAX=6
Proposed method applied for transform skip and transform bypass TU
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | 0.0% | 0.0% | 0.0% | -0.2% | -0.2% | -0.2% | -0.4% | -0.4% | -0.4%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.1% | 0.2% | 0.2% | -1.0% | -0.9% | -0.8% | -2.8% | -3.1% | -3.0%
SC YUV 444 | 0.1% | 0.0% | 0.1% | -0.1% | -0.1% | 0.0% | -0.6% | -0.6% | -0.6%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 98% |  |  | 98% |  |  | 98% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | 0.1% | 0.1% | 0.1% | -0.8% | -0.7% | -0.8% |  |  | 
SC YUV 444 | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 98% |  |  | 98% |  |  |  |  | 
Dec Time[%] | 97% |  |  | 96% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.2% | -0.4% | 0.0% | -0.2% | -0.3% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | 0.7% | 0.8% | 0.7% | -0.3% | -0.2% | -0.3% |  |  | 
SC YUV 444 | 0.5% | 0.5% | 0.4% | 0.3% | 0.3% | 0.3% |  |  | 
RangeExt | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 99% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 97% |  |  |  |  | 
Method 1

## Slide 7: Experimental results
(Lossless)
Method 2
RICE_ MAX=6
MAX : cad-waveform
AI ,-15.1%
Performance gains are observed for all classes and test conditions
 | All Intra Main |  |  | Random Access Main |  |  | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving | compression ratio |  | Bit-rate saving
 | Reference | Tested |  | Reference | Tested |  | Reference | Tested | 
Class F | 5.2 | 5.3 | -1.4% | 31.7 | 32.1 | -0.7% | 49.8 | 50.1 | -0.3%
Class B | 2.2 | 2.3 | -0.3% | 2.6 | 2.6 | -0.2% | 2.6 | 2.6 | -0.2%
SC RGB 444 | 10.1 | 11.3 | -9.2% | 100.4 | 113.3 | -7.7% | 381.6 | 439.1 | -7.3%
SC YUV 444 | 11.4 | 12.1 | -4.1% | 128.9 | 136.9 | -3.7% | 325.6 | 356.4 | -4.0%
RangeExt | 2.4 | 2.4 | -0.9% | 2.5 | 2.5 | -0.4% | 2.5 | 2.5 | -0.4%
Enc Time[%] | 102% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 106% |  |  | 107% |  |  | 107% |  | 

## Slide 8: Experimental results
(Lossy)
RICE_ MAX=6
Proposed method applied for transform skip and transform bypass TU
Method 2
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.1% | 0.0% | -0.1% | -0.2% | -0.2% | -0.2% | -0.5% | -0.5% | -0.5%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | 0.0% | 0.1% | 0.1% | -1.1% | -1.1% | -1.1% | -3.0% | -3.3% | -3.3%
SC YUV 444 | 0.0% | 0.0% | 0.0% | -0.2% | -0.2% | -0.1% | -0.8% | -0.8% | -0.8%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 101% |  | 
Dec Time[%] | 104% |  |  | 104% |  |  | 104% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.1% | -0.1% | -0.2% | -0.2% | -0.2% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -0.1% | 0.0% | 0.0% | -1.1% | -1.0% | -1.0% |  |  | 
SC YUV 444 | 0.0% | 0.0% | 0.1% | -0.1% | -0.1% | -0.1% |  |  | 
RangeExt | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! |  |  | 
Enc Time[%] | #VALUE! |  |  | #VALUE! |  |  |  |  | 
Dec Time[%] | #VALUE! |  |  | #VALUE! |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.3% | -0.1% | 0.9% | -0.1% | 0.0% | 0.1% |  |  | 
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
SC RGB 444 | -0.1% | -0.1% | -0.2% | -1.2% | -1.1% | -1.2% |  |  | 
SC YUV 444 | 0.2% | 0.3% | 0.2% | 0.0% | 0.1% | 0.1% |  |  | 
RangeExt | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! |  |  | 
Enc Time[%] | #VALUE! |  |  | #VALUE! |  |  |  |  | 
Dec Time[%] | #VALUE! |  |  | #VALUE! |  |  |  |  | 

## Slide 9: Conclusions
A rice parameter update method for transform skip and transform bypass block is proposed.
The proposed method provides performance gains up to -15.1% for lossless AI test conditions.
Performance gains are observed for all classes in lossless conditions.
We would like to thank qualcomm for the crosscheck of this proposal.

## Slide 10
Thank you !