## Slide 1: Restriction of CU sizes for Intra Block Copy (JCTVC-R0056)
Jonghyun Ma, Hyunho Jo, Ismail M, Yongjo Ahn, Woong Lim, and Donggyu Sim
Kwangwoon University (KWU)

## Slide 2: Contents
Introduction
Problems
Proposed method
Experimental results
Conclusion

## Slide 3: Introduction
Intra Block Copy (Intra BC) on/off flag is coded on each CU-level to indicate if its coding mode is intra block copying mode or not.
0
0
1
1
1
0
0
1
1
0
1
1
1
1
0
1
1
0
1
1
0
64x64 CTU
0
Intra BC off
1
Intra BC on

## Slide 4: Problems
Selected dominant block sizes for Intra BC may vary depending on different sequences.
  Some sequences are efficiently coded with only small Intra BC block sizes.
  On the contrary, some other sequences can be coded with large Intra BC block sizes.
Based on the fact, the intra block copying mode can be selectively performed on limited CU-levels, depending on sequences.
For SCM-1.0, the on/off flags for Intra BC are coded on all the CU-levels.

## Slide 5: Proposed method
Syntax flow and decoding process of the proposed algorithm
CU size >= min Intra BC size
Decoding an on/off flag for Intra BC in a CU
Perform the intra block copying mode
Intra BC flag == 1
Decoding prediction mode flag
CU size <= max Intra BC size
Y
N
Y
N
Y
N

## Slide 6: Experimental results (1/3)
The proposed method is integrated on SCM-1.0
For this evaluation, restricted CU sizes for Intra BC are set as below.
  Minimum Intra BC size: 88
  Maximum Intra BC size: 1616

## Slide 7: Experimental results (2/3)
Proposed vs The anchor (SCM-1.0 Lossy)

## Slide 8: Experimental results (3/3)
Proposed vs The anchor (SCM-1.0 Lossless)

## Slide 9: Conclusion
Restriction of CU sizes for Intra BC is proposed to reduce on/off flags for Intra BC, depending on sequences.
Minor coding gain is observed in the experimental results when the min and max Intra BC block sizes are given with 88 and 1616, respectively.
Coding performance of the proposed method can be improved by adaptively modifying the min/max Intra BC block sizes, depending on sequences.