## Slide 1: JCTVC-T0113: CE 3 Related MV and Run coding for Intra String Copy Feng Zou, Vadim Seregin, Ying Chen, Wei Pu, Marta Karczewicz

## Slide 2: JCTVC-T0113: MV and Run Coding
Current MV coding in CE 3 intra string copy software
  Greater than 0 flag + EG1
  Sign bit (bypass coded)
Proposed MV coding
  Greater than 0 flag, greater than 1 flag, plus EG5
  Two flags are context coded
  Sign bit (bypass coded)

## Slide 3: JCTVC-T0113: MV and Run Coding
Current run coding in CE 3 intra string copy software
  Region based fixed length code
Proposed Run coding
  Greater than 0 flag + EG0
  Greater than 0 flag is context coded
  Up to 5 bins of prefix of EG0 are context coded
  g_ucDictLen[6] = { 0, 1, 2, 3, 3, 4 } context assignment

## Slide 4: Simulation Results – MV coding
All Intra |  |  |  |  |  | 
 | 2CTU |  | 4CTU |  | Full Frame | 
 | CE 2CTU | MV 2CTU | CE 4CTU | MV 4CTU | CE Full frame | MV Full frame
RGB, text & graphics with motion, 1080p & 720p | -0.9% | -1.1% | -1.8% | -2.3% | -3.3% | -4.0%
RGB, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.3% | -0.4% | -0.9% | -1.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.8% | -1.0% | -1.5% | -1.9% | -2.9% | -3.5%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.2% | -0.3% | -0.8% | -1.0%
YUV, Animation, 720p | 0.1% | 0.1% | 0.0% | 0.0% | 0.1% | 0.1%
YUV, camera captured, 1080p | 0.1% | 0.1% | 0.0% | 0.0% | 0.1% | 0.1%
Enc Time[%] | 150% | 140% | 158% | 159% | 157% | 159%
Dec Time[%] | 104% | 100% | 102% | 100% | 99% | 100%

## Slide 5: Simulation Results – Run coding
All Intra |  |  |  |  |  | 
 | 2CTU |  | 4CTU |  | Full Frame | 
 | CE 2CTU | Run 2CTU | CE 4CTU | Run 4CTU | CE Full frame | Run Full frame
RGB, text & graphics with motion, 1080p & 720p | -0.9% | -1.1% | -1.8% | -2.1% | -3.3% | -3.6%
RGB, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.3% | -0.3% | -0.9% | -1.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.8% | -1.0% | -1.5% | -1.8% | -2.9% | -3.2%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.2% | -0.3% | -0.8% | -0.9%
YUV, Animation, 720p | 0.1% | 0.1% | 0.0% | 0.0% | 0.1% | 0.1%
YUV, camera captured, 1080p | 0.1% | 0.1% | 0.0% | 0.0% | 0.1% | 0.1%
Enc Time[%] | 150% | 143% | 158% | 141% | 157% | 160%
Dec Time[%] | 104% | 100% | 102% | 100% | 99% | 102%

## Slide 6: Simulation Results – Combo of MV and Run coding
All Intra |  |  |  |  |  | 
 | 2CTU |  | 4CTU |  | Full Frame | 
 | CE 2CTU | Com 2CTU | CE 4CTU | Com 4CTU | CE Full frame | Com Full frame
RGB, text & graphics with motion, 1080p & 720p | -0.9% | -1.3% | -1.8% | -2.6% | -3.3% | -4.4%
RGB, mixed content, 1440p & 1080p | -0.1% | -0.2% | -0.3% | -0.4% | -0.9% | -1.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.8% | -1.2% | -1.5% | -2.2% | -2.9% | -3.9%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.2% | -0.4% | -0.8% | -1.1%
YUV, Animation, 720p | 0.1% | 0.1% | 0.0% | 0.1% | 0.1% | 0.1%
YUV, camera captured, 1080p | 0.1% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
Enc Time[%] | 150% | 144% | 158% | 136% | 157% | 158%
Dec Time[%] | 104% | 100% | 102% | 95% | 99% | 99%

## Slide 7
Thanks