## Slide 1: JVET-C066: On coefficient Scaling
D. B. Sansli, D. Rusanovskyy, J. Sole, A. K. Ramasubramonian, M. Karczewicz (QUALCOMM)
28/05/2016

## Slide 2: Outline
Motivation
Luma Delta QP signaling
Residual Scaling
Our proposal
Summary

## Slide 3: Motivation
Recent HDR/WCG activity revealed that next generation containers, such as ST-2084, re-shape quantization noise as a function of brightness
  Brightness dependent spatially varying QP adaptation improves visual quality
JVET-B0054 includes an alternative residual scaling method to avoid delta QP signaling overhead
  Scale value is determined from average luma value of predicted block and DC value of residual
  Derived scale is applied to AC coefficients of current block
Some aspects of JVET-B0054 residual scaling design
  Using DC coefficient in derivation process prevents the scaling of luma DC coefficient
  Using DC coefficient for scale determination and placing the scaling after secondary inverse transform cause mismatch between encoder and decoder
  Current implementation has division at the decoder

## Slide 4: Delta QP solution
Encoder
Decoder

## Slide 5: EE-2.4 Residual Scaling

## Slide 6: Proposal
Remove DC from scale derivation process
Estimate average luma value from predicted samples
  Pro: Able to apply scaling on DC coefficient as well
  Con: Reduced accuracy of brightness estimation
Apply scaling at the quantization stage
  In decoder, scaling is applied directly on dequantized coefficients
  Secondary transform statistics is not changed
Avoid division at the decoder
  LUT is updated to move division to the encoder and multiplication to the decoder

## Slide 7: Proposal

## Slide 8: Results
Proposal is tested against delta QP signaling with 64x64 CTU, random access configuration and HDR sequences
Class | Sequences | tPSNR_Y | DE100 | PSNR Y | PSNR U | PSNR V
A | FireEaterClip4000r1 | 4.5% | 4.3% | 4.0% | 4.9% | 3.9%
 | Market3Clip4000r2 | 2.2% | -6.8% | 2.3% | -2.3% | -1.5%
 | SunRise | 2.7% | -6.8% | 2.8% | 3.2% | -1.8%
B | BikeSparklers cut 1 | -0.5% | -2.6% | -0.5% | 0.3% | -1.4%
 | BikeSparklers cut 2 | -0.4% | -2.4% | -0.4% | 0.0% | -3.7%
 | GarageExit | 1.1% | 1.2% | 1.2% | 2.3% | 2.3%
C | ShowGirl2Teaser | 0.5% | -3.4% | 0.5% | -0.6% | -0.2%
D | StEM_MagicHour cut 1 | 1.3% | 0.8% | 1.4% | 0.8% | 0.7%
 | StEM_MagicHour cut 2 | 0.9% | 0.7% | 0.9% | 1.8% | 1.9%
 | StEM_MagicHour cut 3 | 0.5% | 0.0% | 0.4% | 0.4% | 1.1%
 | StEM_WarmNight cut 1 | 1.2% | -2.0% | 1.1% | -1.5% | -1.0%
 | StEM_WarmNight cut 2 | 1.9% | -0.9% | 1.8% | 0.4% | 2.3%
G | BalloonFestival | 2.8% | -5.1% | 2.8% | 2.0% | 1.8%
H | EBU_04_Hurdles | 1.2% | -2.5% | 1.1% | 1.5% | 0.2%
 | EBU_06_Start | 0.9% | -5.0% | 1.0% | -1.1% | -1.2%
 | Overall | 1.2% | -2.5% | 1.2% | 0.5% | 0.0%

## Slide 9: Conclusion
Alternative residual scaling scheme is proposed:
  Removing DC coefficient from scale derivation process
  Placing scaling in the dequantizer stage
  Avoiding division at the decoder
It is proposed to establish EE on the proposed technique