## Slide 1
Vladyslav Zakharchenko
MPEG116
JVET 4
Suggested testing procedure for 360-degree video
D0027
October 17, 2016

## Slide 2: Suggested testing procedure for 360-degree video
AGENDA
360-degree video history and current problems
Video conversion process, common projection format
Suggested video quality evaluation pipeline
Conversion results discussion
Compression results discussion
Conclusions

## Slide 3: Suggested testing procedure for 360-degree video
Inter meeting activity for 360tools discussion
  50+ emails
  40 experts from the different companies on the mailing list
  Test sequences and testing procedure discussion
  Release announced on June 24th, first public release Aug 3rd
  Open source policies, BSD-3 license for donated software
Content donated by GoPro, Nokia, ETRI
  12 Test sequences in total with resolution of ~4K (3840x1920; 4096x2048; 4320x2160) in equirectangular projection format [JVET-C0021], [JVET-C0064],
Projections
  2 Specific projections adopted from proponents: TSP [JVET-D0071]; SSP [JVET-D0030]
Quality metrics
  Quality metrics discussed and accepted form proponents

## Slide 4: 360-degree VR content revisited
Where does the content comes from
There is a lot of history background in a VR video content as we see it now
  VR video
  360 video
  Omnidirectional content
All of these terms are representing one big concept:
A user has a freedom to observe any part of the surrounding space by directing his/hew view, pointer, or other control options The first concept for the proposed technology has appeared with an introduction of this device Oculus DK1. Being highly appreciated by technological society new technology quickly found adepts among game designers. Now it’s if not a museum piece it has definitely become a collector’s find
Gamedev driven architecture
Limited screen resolution
PC oriented market
All these factors has made a distinguishing impact on content creation procedure.

## Slide 5: Viewport rendering pipeline
Content storage and management has come from the gaming industry
Textures are based on complex meshes
Textures are computer generated, not natural images
Different approach to texture compression
texture
texture
texture
Build scene
Space model
Render viewport
Camera model

## Slide 6: VR content ecosystem
3D space models
Triangulated Cube Octahedron Icosahedron
sphere
Projections (Texture models)
Equirectangular Cubemap Octahedral Icosahedral

## Slide 7: Supported projections discussion
EPR
CPP
CMP RCMP
ISP RISP
SSP TSP
OHP ROHP

## Slide 8: Pipeline for 360-degree video content
Content representation
The main difference is that “What you see if what you get” rule is not working any more
Display, or a viewport, in general, is part of a 3D space model, with a corresponding texture attached to this model.
Thus resulting image quality depends on many factors
  3D space model complexity
  Projection quality
  Display hardware/driver dependent
Observed rendering problems
  Geometrical distortions, defined by model
  Discontinuities in stitched areas caused by compression
  Nonuniform spatial resolution across projection caused by projection

## Slide 9: Model-driven distortions
Model complexity driven (equirectangular format)
    ERP 18x12 mesh ERP 72x28 mesh
___
* Nonlinear coordinate system in projection may result in severe geometrical distortions

## Slide 10: Model-driven distortions
Edge area discontinuities for high QP values
    OHP QP22 OHP QP37
___
* Discontinuities in projection are resulting in prediction distortions

## Slide 11: 360tools: 360-degree video exploration software
/* The copyright in this software is being made available under the BSD
* License, included below. This software may be subject to other third party
* and contributor rights, including patent rights, and no such rights are
* granted under this license.
*
* Copyright (c) 2016, Samsung Electronics Co., Ltd.
* All rights reserved.
*
* Redistribution and use in source and binary forms, with or without
* modification, are permitted provided that the following conditions are met:
*
* * Redistributions of source code must retain the above copyright notice,
* this list of conditions and the following disclaimer.
* * Redistributions in binary form must reproduce the above copyright notice,
* this list of conditions and the following disclaimer in the documentation
* and/or other materials provided with the distribution.
* * Neither the name of Samsung Electronics Co., Ltd. nor the names of its
* contributors may be used to endorse or promote products derived from
* this software without specific prior written permission.
*
* THIS SOFTWARE IS PROVIDED BY THE COPYRIGHT HOLDERS AND CONTRIBUTORS "AS IS"
* AND ANY EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED TO, THE
* IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE
* ARE DISCLAIMED. IN NO EVENT SHALL THE COPYRIGHT HOLDER OR CONTRIBUTORS
* BE LIABLE FOR ANY DIRECT, INDIRECT, INCIDENTAL, SPECIAL, EXEMPLARY, OR
* CONSEQUENTIAL DAMAGES (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF
* SUBSTITUTE GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR BUSINESS
* INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF LIABILITY, WHETHER IN
* CONTRACT, STRICT LIABILITY, OR TORT (INCLUDING NEGLIGENCE OR OTHERWISE)
* ARISING IN ANY WAY OUT OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF
* THE POSSIBILITY OF SUCH DAMAGE.
*/
BSD
Clause 3
clear
>> git clone https://github.com/Samsung/360tools.git (available to public since Aug 3, 2016)

## Slide 12: 360tools: 360-degree video exploration software
360tools
Completely open and open source platform under BSD-3 license
Anyone is welcomed with a tech support and user-friendly interfaces. All the contributions from the mailing list have been integrated with a post processing support.
VR specific conversion pipeline is a motivation to have dedicated independent software capable to provide conversion and quality estimation for exploration experiments.
Suggested exploration pipeline
>> git clone https://github.com/Samsung/360tools.git (available to public since Aug 3, 2016)

## Slide 13: 360tools: 360-degree video exploration software
Craster Parabolic Projection (CPP)
Pixels duplication rate (projection anisotropy)
___
*Black area represents 1/w pixels density gray pixel density is uniform and equals 1

## Slide 14: 360tools: 360-degree video exploration software
Supported conversions
360 tools provides the following functionality:
variable bit-depth and different colorspaces
  Conversion in 10 bit’s internally provides better quality
various interpolation filters [JVET-D0125] exploration
  6 taps lanczos filter demonstrates the best quality among various compared filters
projection resolution scaling
  suggested within content management pipeline convert via common projection
packed projection support
  redundancy in unwrapped projections delivery method can be reduced by packing content, which results in a ~7-10% better compression. Consistent with [JVET-D0022] and [JVET-D0023] conclusions.
___
* V supported conversion
** QM conversion supported within quality metrics
 |  | Input format |  |  |  |  |  | 
 |  | CPP | ERP | ISP | CMP | OHP | TSP | SSP
Output format | CPP | V | V | QM | QM | QM | QM | QM
 | ERP | V | - | V | V | V | V | V
 | ISP | V | V | - | - | - | - | 
 | CMP | V | V | - | - | - | - | 
 | OHP | V | V | - | - | - | - | 
 | TSP | - | V |  |  |  |  | 
 | SSP | V | V | - | - | - | - | 

## Slide 15: 360tools: 360-degree video exploration software
Supported Quality metrics
Suggested quality metrics and testing methodology:
comparison within one projection WS-PSNR
  consistent analysis within the same projection for image, considering the distortions introduced by the projection process
comparison across projections CPP-PSNR
  provides equal condition for each projection with high fidelity for content display format
conversion and compression results demonstrate relevant results in exploration experiments
 |  | Projection format |  |  |  |  |  | 
 |  | CPP | ERP | ISP | CMP | OHP | TSP | SSP
Quality metrics | PSNR | - | V | V | V | V | V | V
 | S-PSNR | - | V | - | - | - | - | -
 | WS-PSNR | - | V | V | V | V | - | -
 | CPP-PSNR | V | V | V | V | V | V | V

## Slide 16: Conversion quality evaluation (without compression)
Following constrains had been considered for conversion
Number of points across compared projections must be equal or close
All the comparison candidates were converted via common projection (CPP)
___
*The results statistics deviations are significant and demonstrate consistency across different projections. Investigation showed that stitching and blending problems in original projection lead to low conversion quality results
 | ERPCPPCoding ProjectionrecERP (quality measured between ERP and recERP). |  |  |  |  |  | CPPCoding Projection (quality measured between CPP and Coding Projection). |  | 
 | S-PSNR |  |  |  | WS-PSNR |  |  | CPP-PSNR | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
ERP100 | 48.58 | 58.49 | 58.79 | 47.45 | 56.98 | 57.24 | 49.30 | 59.62 | 59.94
ISP75 | 46.70 | 56.23 | 56.39 | 48.03 | 57.91 | 58.12 | 49.05 | 59.34 | 59.48
ISP100 | 47.48 | 57.05 | 57.26 | 48.87 | 58.75 | 59.01 | 51.10 | 61.49 | 61.72
CMP75 | 46.40 | 55.96 | 56.08 | 47.74 | 57.63 | 57.80 | 48.58 | 58.96 | 59.09
CMP100 | 47.16 | 56.63 | 56.82 | 48.47 | 58.28 | 58.51 | 50.41 | 60.59 | 60.86
OHP75 | 46.83 | 56.29 | 56.56 | 48.22 | 58.01 | 58.32 | 49.21 | 59.46 | 59.71
OHP100 | 47.54 | 56.99 | 57.26 | 48.95 | 58.72 | 59.03 | 51.17 | 61.38 | 61.66
TSP25 | 33.60 | 47.23 | 47.13 | 33.82 | 47.73 | 47.62 | 33.68 | 47.67 | 47.59

## Slide 17: Conversion quality evaluation (without compression)
ERP->CPP->recERP conversion
ERP->CPP->CMP->recERP conversion
___
*Conversion error is lower than typical compression error
 | S-PSNR |  |  | WS-PSNR |  |  | CPP-PSNR |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
BearAttackLeft | 50.74 | 51.57 | 51.66 | 49.14 | 49.77 | 49.96 | 51.54 | 52.56 | 52.68
SheriffLeft | 49.45 | 55.81 | 56.39 | 47.41 | 53.51 | 54.09 | 50.66 | 58.73 | 59.78
LRRHLeft | 37.11 | 47.74 | 49.05 | 38.52 | 46.50 | 47.80 | 39.45 | 47.76 | 49.07
Paramotor | 45.51 | 56.36 | 59.64 | 44.35 | 55.16 | 58.27 | 45.38 | 57.10 | 60.84
Jump | 53.99 | 59.25 | 59.54 | 52.74 | 57.87 | 57.93 | 54.70 | 60.42 | 60.96
Building | 48.50 | 64.78 | 66.27 | 46.70 | 63.22 | 64.89 | 49.02 | 65.35 | 66.57
Boarding | 55.90 | 66.32 | 68.07 | 54.42 | 64.77 | 66.52 | 56.87 | 67.22 | 68.67
Bicyclist | 41.80 | 59.09 | 63.06 | 40.88 | 58.14 | 61.65 | 41.98 | 59.27 | 63.25
Glacier | 48.29 | 63.12 | 63.42 | 47.76 | 61.90 | 62.19 | 48.42 | 63.93 | 64.28
Shark | 43.72 | 57.54 | 49.27 | 42.93 | 56.44 | 48.25 | 43.46 | 57.76 | 49.08
Driving | 55.98 | 61.27 | 60.74 | 53.87 | 59.29 | 58.81 | 57.54 | 63.69 | 63.08
Dancing | 52.04 | 59.05 | 58.41 | 50.64 | 57.16 | 56.55 | 52.54 | 61.70 | 60.97
 | 48.58 | 58.49 | 58.79 | 47.45 | 56.98 | 57.24 | 49.30 | 59.62 | 59.94
 | S-PSNR |  |  | WS-PSNR |  |  | CPP-PSNR |  | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
BearAttackLeft | 47.94 | 48.76 | 49.04 | 49,26 | 65,35 | 65,73 | 50.54 | 51.76 | 51.98
SheriffLeft | 45.44 | 52.28 | 52.91 | 44,19 | 59,35 | 51,06 | 48.48 | 57.01 | 58.03
LRRHLeft | 38.33 | 46.66 | 47.94 | 61,55 | 66,34 | 65,40 | 39.58 | 48.73 | 50.01
Paramotor | 43.72 | 54.82 | 57.44 | 56,06 | 63,54 | 62,70 | 45.32 | 57.24 | 60.42
Jump | 51.32 | 56.68 | 56.34 | 49,73 | 51,00 | 51,30 | 53.47 | 59.52 | 59.57
Building | 44.41 | 60.69 | 62.46 | 47,54 | 56,14 | 57,14 | 46.84 | 63.47 | 64.77
Boarding | 53.13 | 62.68 | 64.28 | 39,19 | 48,24 | 49,55 | 56.16 | 65.60 | 66.87
Bicyclist | 40.61 | 57.78 | 59.47 | 44,72 | 56,73 | 59,85 | 42.13 | 59.77 | 61.44
Glacier | 47.56 | 61.13 | 61.49 | 52,71 | 58,91 | 58,84 | 48.69 | 63.61 | 63.95
Shark | 43.32 | 56.52 | 49.11 | 45,78 | 62,64 | 64,15 | 44.97 | 58.89 | 51.50
Driving | 50.99 | 57.50 | 57.11 | 55,22 | 64,74 | 66,00 | 54.06 | 61.76 | 61.22
Dancing | 49.98 | 56.00 | 55.38 | 41,68 | 59,36 | 60,56 | 52.70 | 60.12 | 59.36
 | 46.40 | 55.96 | 56.08 | 48,97 | 59,36 | 59,36 | 48.58 | 58.96 | 59.09

## Slide 18: Conversion quality evaluation (with compression)
Following constrains had been considered for conversion
Compression results have been obtained using HM16.11 sw and following test conditions equivalent (GOP size =16 in random access tests).
CPP-PSNR measured between reconstructed coded projection and common test projection
All coding projection candidates are compared against ERP
WS-PSNR calculation considers that reconstructed coding projection was converted to ERP (ERP vs recERP)
Compression efficiency for a given content shows results with a high deviation and in general is consistent across various projections (results are content dependent)
 |  | WS-psnr |  |  | CPP -psnr |  | 
 |  | Y | U | U | Y | U | U
ISP | 75 | 0.0% | 0.5% | -0.9% | -0.3% | 1.4% | -0.1%
ISP | 100 | 0.5% | -0.8% | -1.4% | -0.7% | 0.1% | -0.6%
CMP | 75 | 3.8% | 0.9% | 0.1% | -0.2% | -0.1% | -0.6%
CMP | 100 | 3.4% | -0.5% | -0.4% | 1.1% | 0.5% | 0.5%
OHP | 75 | 12.0% | 16.4% | 13.0% | 10.3% | 16.3% | 11.8%
OHP | 100 | 12.1% | 15.8% | 12.3% | 10.9% | 16.9% | 12.3%

## Slide 19: Conclusions
Donated software offers conversion compatibility for 6 different formats, both homebrew and adopted from a proponents
3 different 360-degree video specific quality metrics had been integrated into the software to provide quality estimation tools both within same projection and across different projections
We suggest using generalized common (Craster Parabolic) projection, corresponding to a spherical space as a reference to provide equal comparison conditions for every test candidate.
Visual test demo has been promoted and the experts are welcomed to attend and express their opinion.
The proposed contribution provides both subjective and objective quality evaluation.
Test content is provided in only one format, with a projection specific distortions leading to unequal conditions in quality evaluation.
Conversion results are content dependent. A strong correlation on the input content quality has been observed. Test sequences pruning is suggested.

## Slide 20
Annex 1
Full scale content

## Slide 21: ERP

## Slide 22: CPP

## Slide 23: CMP

## Slide 24: OHP

## Slide 25: ISP

## Slide 26: RCMP

## Slide 27: ROHP

## Slide 28: RISP

## Slide 29: TSP

## Slide 30: SSP

## Slide 32
Annex 2
Projection distortion measure

## Slide 33: 360tools: 360-degree video exploration software
Craster Parabolic Projection (CPP) vs Equal area projection (EAP) anisotropy
___
*Geometrical distortions discussed as Tissot’s indicatrics

## Slide 34
Annex 3
Suggestions
on test procedure

## Slide 35: Suggested test for tools evaluation
ERP
CMP
ISP
TSP
OHP
Enc/Dec
(for ex. HM)
recERP
recCMP
recISP
recTSP
recOHP
WS(AW)-PSNR
allows comparison across within the same projection and resolution
does not need interpolation
Viewport rendering
Implementation on Android platform viewable on HMD is provided (aligned with 360tools SW)
SSP
… …
recSSP
WS(AW)-PSNR
Test
materials
Method
TBD
Rendered
Viewport
REC
Rendered
Viewport
ORIG
Method
TBD
PSNR

## Slide 36: Suggested test for projections comparison
ERP
CMP
ISP
TSP
OHP
Enc/Dec
(for ex. HM)
recERP
recCMP
recISP
recTSP
recOHP
CPP-PSNR
CPP-PSNR
allows comparison across projections and resolutions
requires interpolation
WS(AW)-PSNR
allows comparison across within the same projection and resolution
does not need interpolation
SSP
… …
recSSP
WS(AW)-PSNR
Test materials
(for ex. ERP 8K)
Common projection
(for ex. CPP 8K)