## Slide 1
Sign Prediction
Felix Henry, Gordon Clare

## Slide 2
Principles
  Predict some luma EP signs and replace them with CABAC-coded sign residues
  Sign residues are transmitted, representing the difference between the sign predictors and the real signs
  Per-TU; Only when TU has left and top neighbors
  The top/left border pixels of the current block are reconstructed under all sign assumptions
  Signs are predicted by minimizing top/left border distortion of the current block against past pixels
  The sign residues are encoded using two CABAC contexts

## Slide 3
Choosing Signs to Predict
TU coefficients scanned in raster-scan order
Signs associated with dequantized amplitudes over a defined threshold are preferred
Maximum number of signs predicted per TU is limited by an encoder parameter (sweetspot at 4)

## Slide 4
Hypothesis Border Reconstructions
n signs predicted – there will be 2n border reconstructions
n+1 partial inverse transform operations
  n involve partial inverse transform of single coefficient
  1 partial inverse transform to start the process
n templates; one template per sign hidden
  Each template is the partial inverse transform of the single (absolute valued) coefficient having its sign predicted, other elements zero
The border reconstructions are approximations, not perfect reconstructions
Use subtraction of ‘templates’ to perform reconstructions, rather than a partial inverse transform operation per reconstruction
+2
-5
-1
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3

## Slide 5
Hypothesis Border Reconstructions
3-sign (8 hypothesis) case: 3 templates
… 8 hypotheses, each border costed:
+2
-5
-1
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
3 templates; inv xform of single abs coeff; labelled
T001
T010
T100

## Slide 6
Hypothesis Border Reconstructions
Costing: border distortion
hypothesis reconstruction
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
p-1,0
p-1,1
p-1,2
p-1,3
p-2,0
p-2,1
p-2,2
p-2,3
p0,-1
p1,-1
p2,-1
p3,-1
p0,-2
p1,-2
p2,-2
p3,-2
previously reconstructed neighbor pixels
linear prediction
hypothesis reconstruction

## Slide 7
Encoder/Decoder
Encoder
  hypothesis reconstructions during rdo: compares prediction to real sign, gets sign residue
  encode: writes sign residue
Decoder
  parsing: reads sign residue
  reconstruction: hypothesis reconstructions to get prediction – used with sign residue to get real sign

## Slide 8
Bitstream Changes
All signs in a TU moved to end of TU
  No longer signaled per CG
  Decoder needs coefficient values to determine which signs are predicted (and thus not EP signaled)
Includes chroma, even though chroma not predicted
  Single logic path

## Slide 9
Performance
 | All Intra Main10 |  |  |  | 
 | Over HM-16.6-JEM-3 (parallel encode, sequential decode) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.5% | -0.4% | -0.4% | 145% | 154%
Class A2 | -0.5% | -0.4% | -0.4% | 145% | 145%
Class B | -0.5% | -0.3% | -0.4% | 147% | 146%
Class C | -0.4% | -0.5% | -0.4% | 143% | 139%
Class D | -0.4% | -0.5% | -0.4% | 141% | 130%
Class E | -0.8% | -0.6% | -0.7% | 145% | 137%
Overall | -0.5% | -0.4% | -0.4% | 145% | 142%
Class F (optional) | -0.4% | -0.2% | -0.2% | 140% | 123%
 | Random Access Main 10 |  |  |  | 
 | Over HM-16.6-JEM-3 (parallel encode, sequential decode) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.6% | -0.4% | -0.5% | 131% | 107%
Class A2 | -0.6% | -0.4% | -0.4% | 123% | 102%
Class B | -0.6% | -0.2% | -0.6% | 123% | 103%
Class C | -0.6% | -0.3% | -0.4% | 121% | 102%
Class D | -0.4% | -0.1% | 0.1% | 117% | 101%
Class E |  |  |  |  | 
Overall (Ref) | -0.6% | -0.3% | -0.4% | 123% | 103%
Class F (optional) | -0.4% | -0.5% | -0.5% | 123% | 103%
 | Low delay B Main10 |  |  |  | 
 | Over HM-16.6-JEM-3 (parallel encode, sequential decode) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.5% | -0.2% | -0.3% | 126% | 107%
Class C | -0.5% | -0.2% | -0.4% | 116% | 106%
Class D | -0.5% | -0.4% | -1.2% | 111% | 104%
Class E | -0.6% | -0.7% | 0.1% | 114% | 103%
Overall (Ref) | -0.5% | -0.4% | -0.5% | 118% | 105%
Class F (optional) | -0.2% | -0.3% | 0.0% | 117% | 106%
 | Low delay P Main10 |  |  |  | 
 | Over HM-16.6-JEM-3 (parallel encode, sequential decode) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.5% | -0.2% | -0.2% | 132% | 111%
Class C | -0.6% | -0.4% | -0.2% | 124% | 110%
Class D | -0.4% | -0.3% | -0.2% | 118% | 106%
Class E | -0.7% | 0.4% | 0.5% | 120% | 107%
Overall (Ref) | -0.5% | -0.2% | -0.1% | 124% | 109%
Class F (optional) | -0.5% | -1.1% | -1.0% | 123% | 107%

## Slide 10
Conclusion
We propose to add this tool to the next version of the JEM.

## Slide 11
Thank you

## Slide 12
Interaction with Sign Data Hiding
Sign Prediction simply avoids using any sign hidden with SDH, and predicts using others
 | All Intra Main10 |  |  |  | 
 | Over HM-16.6-JEM-3 (parallel), SDH=0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class B | -0.5% | -0.3% | -0.3% | 124% | 126%
Class C | -0.4% | -0.4% | -0.4% | 136% | 140%
Class D | -0.4% | -0.3% | -0.3% | 135% | 137%
Class E | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Random Access Main 10 |  |  |  | 
 | Over HM-16.6-JEM-3 (parallel), SDH=0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class B | -0.6% | -0.4% | -0.5% | 119% | 102%
Class C | -0.6% | -0.3% | -0.4% | 143% | 130%
Class D | -0.5% | -0.3% | -0.1% | 246% | 211%
Class E |  |  |  |  | 
Overall (Ref) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Results with SDH turned off both in reference and SignPred=4.
(disregard timings)

## Slide 13
Qualcomm’s QTBT Encoder Patch
 | All Intra Main10 |  |  |  | 
 | Over r128+qualcommpatch, parallel |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class B | -0.5% | -0.4% | -0.3% | 149% | 149%
Class C | -0.4% | -0.4% | -0.4% | 146% | 135%
Class D | -0.4% | -0.5% | -0.3% | 142% | 121%
Class E | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Random Access Main 10 |  |  |  | 
 | Over r128+qualcommpatch, parallel |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class B | -0.6% | -0.6% | -0.6% | 122% | 104%
Class C | -0.5% | -0.6% | -0.2% | 119% | 104%
Class D | -0.4% | -0.4% | -0.4% | 115% | 102%
Class E |  |  |  |  | 
Overall (Ref) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  | 
 | Over r128+qualcommpatch, parallel |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.6% | 0.0% | -0.5% | 116% | 107%
Class C | -0.5% | -0.6% | -0.6% | 114% | 107%
Class D | -0.4% | 0.0% | 0.3% | 110% | 104%
Class E | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Overall (Ref) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay P Main10 |  |  |  | 
 | Over r128+qualcommpatch, parallel |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.5% | -0.5% | -0.8% | 125% | 111%
Class C | -0.6% | -0.4% | -0.4% | 123% | 110%
Class D | -0.4% | -0.5% | -0.2% | 116% | 105%
Class E | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Overall (Ref) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 14
Extra Results: hiding different numbers of signs.
RA only; class A,B,C,D,F; 17 frames.