## Slide 1: Enhanced Cross-component Linear Model Intra-prediction
JVET-D0110
Kai Zhang, Jianle Chen, Li Zhang, Marta Karczewicz

## Slide 2: Introduction
Cross-component Linear Model (CCLM) chroma intra prediction has been adopted in JEM
  Explores the neighboring reconstructed pixels by utilizing the linear regression approach to derive parameters of the linear model
  For 4:2:0 color format, reconstructed luma is downsampled to match size and phase of chroma signal

## Slide 3: Proposed
Three alternative methods are proposed to further improve the coding efficiency of CCLM
  Multi-model LM (MMLM) method
  Multi-filter LM (MFLM) method
  LM-Angular combined prediction (LAP) mode

## Slide 4: Multi-model LM (MMLM)
More than one linear models between the luma samples and chroma samples in a CU
Neighboring luma samples and neighboring chroma samples of the current block are classified into several groups
  When M = 2: A neighboring sample with Rec’L[x,y] <= Threshold is classified into group 1; otherwise it is classified into group 2.
  Each group is used as a training set to derive a specific linear model (α and β)
  The neighboring samples can be classified into M groups, where M is 2 or 3
Multiple models

## Slide 5: Multi-filter LM (MFLM) method
Four more additional LM modes named MFLM1, MFLM2, MFLM3 and MFLM4, with four different Luma down-sampling filters
  (a)
  (b)
  (c)
  (d)

## Slide 6: LM-Angular combined prediction (LAP) mode
Two prediction patterns named P1 and P2 are generated for the Chroma block first, and then they are combined together as
  One prediction pattern is generated with the normal intra mode (including angular, DC and Planar mode)
  The other prediction pattern is generated with MMLM2 mode

## Slide 7: Experimental Results
CTC, AI
CTC, RA
 | All Intra Main10 |  |  |  | 
 | Over JEM3.0rc1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.2% | -6.0% | -8.1% | 103% | 103%
Class A2 | -0.3% | -4.5% | -4.0% | 104% | 102%
Class B | -0.2% | -3.3% | -2.5% | 102% | 101%
Class C | -0.5% | -3.4% | -3.1% | 103% | 104%
Class D | -0.2% | -2.2% | -1.9% | 103% | 103%
Class E | 0.0% | -1.5% | -1.7% | 105% | 105%
Overall | -0.4% | -3.6% | -3.6% | 103% | 103%
Class F (optional) | -1.2% | -8.2% | -10.2% | 103% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over JEM3.0rc1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.9% | -4.5% | -6.5% | 103% | 100%
Class A2 | -0.2% | -4.1% | -3.2% | 102% | 102%
Class B | -0.1% | -3.4% | -2.3% | 102% | 100%
Class C | -0.2% | -1.9% | -1.9% | 103% | 101%
Class D | -0.1% | -1.6% | -1.3% | 102% | 95%
Class E |  |  |  |  | 
Overall (Ref) | -0.3% | -3.1% | -3.0% | 102% | 100%
Class F (optional) | -0.6% | -6.9% | -7.8% | 103% | 101%

## Slide 8: Summary
Three enhanced LM methods are proposed
  Multi-model LM (MMLM) method
  Multi-filter LM (MFLM) method
  LM-Angular combined prediction (LAP) mode
0.4%, 3.6% and 3.6% BD rate savings on Y, Cb and Cr components respectively for All Intra (AI) configuration with 103% encoding time
0.3%, 3.1%, 3.0% BD rate savings on Y, Cb and Cr components respectively for Random Access (RA) configuration with 102% encoding time

## Slide 9
Results of Multi-model LM (MMLM) method
 | All Intra Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.74% | -3.80% | -4.66% | 101% | 104%
Class A2 | -0.20% | -1.64% | -1.80% | 100% | 102%
Class B | -0.11% | -1.59% | -1.11% | 99% | 102%
Class C | -0.33% | -2.09% | -2.13% | 101% | 102%
Class D | -0.12% | -1.56% | -1.43% | 101% | 102%
Class E | -0.02% | -0.34% | -0.52% | 102% | 103%
Overall | -0.26% | -1.89% | -1.96% | 101% | 102%
Class F (optional) | -0.51% | -2.62% | -2.77% | 101% | 102%
Results of Multi-model LM (MMLM) and Multi-filter LM (MFLM)
 | All Intra Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.04% | -4.60% | -7.56% | 103% | 102%
Class A2 | -0.23% | -3.11% | -3.19% | 104% | 101%
Class B | -0.12% | -2.66% | -1.76% | 102% | 102%
Class C | -0.31% | -2.65% | -2.47% | 103% | 103%
Class D | -0.12% | -1.84% | -1.41% | 103% | 103%
Class E | -0.03% | -0.44% | -0.56% | 104% | 103%
Overall | -0.31% | -2.64% | -2.87% | 103% | 102%
Class F (optional) | -1.13% | -7.97% | -10.04% | 102% | 101%