## Slide 1: Peak Sample Adaptive Offset
JVET-D0133
Marta Karczewicz, Li Zhang, Jianle Chen, Wei-Jung Chien

## Slide 2: Summary
Peak SAO
  Each pixel may be modified by adding an offset
  Offset depends on both category index and pixel difference with its neighbors

## Slide 3: Proposed Peak SAO
Definitions of categories
  Depends on how many neighboring pixels are larger/smaller than current pixel
  For category 2, offset is always set to 0, i.e., pixels are unchanged.
Figure 2. Neighbouring samples.
Category | Condition
0 | 
1 | 
2 | None of the above
Category | Condition
0 | 
1 | 
2 | None of the above
lgr ( x ) = (x > 0) ? 1 : 0 | (1)
sml ( x ) = (x < 0) ? 1 : 0 | (2)

## Slide 4: Proposed Peak SAO
Offset selection
  average pixel value difference between the current pixel and its selected neighboring pixels (Cm)
  normalization factor NF
    M=3 or 4 for category 1 and 2, respectively
Signaling of side information
  Slice on/off control flag
  Offsets for each category and class index, NF, as well as maximum number of classes
 | (3)
 | (3)

## Slide 5: Experimental Results
CTC
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.06% | -0.08% | -0.03% | 100% | 113% | -0.02% | -0.26% | -0.09% | 99% | 104%
Class A2 | -0.15% | -0.05% | -0.04% | 103% | 114% | -0.18% | -0.06% | -0.02% | 99% | 103%
Class B | -0.12% | -0.02% | -0.02% | 100% | 113% | -0.34% | -0.02% | -0.18% | 99% | 102%
Class C | -0.32% | 0.01% | -0.02% | 100% | 109% | -0.33% | 0.17% | 0.05% | 100% | 101%
Class D | -0.15% | 0.03% | 0.04% | 99% | 105% | -0.30% | -0.05% | 0.17% | 100% | 101%
Class E | -0.21% | 0.00% | 0.00% | 100% | 112% |  |  |  |  | 
Overall (Ref) | -0.16% | -0.02% | -0.01% | 100% | 111% | -0.24% | -0.04% | -0.02% | 100% | 102%