## Slide 1
Adaptive NSST Kernel Size Selection (JVET-E0047)
Jan 2017
LG Electronics
Hyeongmoon Jang (hyeongmoon.jang@lge.com)

## Slide 2: Summary
  Efficient NSST kernel size between 4x4 and 8x8
    Select efficient NSST kernel size for over 8x8 block
    Flag signaling when the block is over 8x8 and NSST index is not 0
    Method1: Select kernel size 4x4 or 8x8 Luma and Chroma for I-slice, Luma for B-slice
    Method2: Select kernel size 4x4 or 8x8 for Luma only
Experimental results
Cross-checked by MediaTek(JVET-E0114)
All Intra main10 |  |  | 
 | Y | U | V
Method 1 | -0.16% | -0.48% | -0.54%
Method 2 | -0.18% | -0.24% | -0.34%
Random access main10 |  |  | 
 | Y | U | V
Method 1 | -0.07% | -0.50% | -0.59%
Method 2 | -0.08% | -0.35% | -0.50%

## Slide 3: Current status
JEM-4.0
  NSST index
    Signaled in Intra CU when the number of nonzero Coeff. > Threshold
    Signaled each Luma & Chroma in I-Slice and signaled only Luma in B-Slice
  NSST kernel
    35 x 3 NSST kernel for both 4x4 and 8x8
    Derived from NSST index and intra mode
  NSST kernel Size
    Fixed size of kernel is applied depend on block size
    NSST is applied on Top-left region under 8x8

## Slide 4: Proposal
Signal a flag for decide NSST kernel size
  Block size > 8x8 && NSST kernel index != 0

## Slide 5: Proposed method
Method 1 : Select efficient kernel size for Luma and Chroma
Method 2 : Select efficient kernel size for only Luma
Signal a flag to decide NSST kernel size
  Block size > 8x8 && NSST kernel index != 0
  Signaling
 | I-Slice |  | B-Slice | 
 | Luma | Chroma | Luma | Chroma
Method 1 | Signal | Signal | Signal | Derived from Luma
Method 2 | Signal | - | Signal | -

## Slide 6: Experimental results
 | Method 1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.19% | -0.43% | -0.67% | 152% | 101%
Class A2 | -0.17% | -1.13% | -1.11% | 157% | 101%
Class B | -0.14% | -0.43% | -0.48% | 149% | 103%
Class C | -0.24% | -0.26% | -0.20% | 146% | 98%
Class D | -0.12% | -0.17% | -0.28% | 151% | 99%
Class E | -0.11% | -0.46% | -0.52% | 157% | 98%
Overall | -0.16% | -0.48% | -0.54% | 152% | 100%
Class F (optional) | -0.17% | -0.12% | -0.12% | 140% | 100%
 | Method 2 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.22% | 0.01% | -0.37% | 151% | 103%
Class A2 | -0.22% | -0.65% | -0.73% | 155% | 101%
Class B | -0.15% | -0.27% | -0.29% | 148% | 100%
Class C | -0.24% | -0.18% | -0.29% | 139% | 105%
Class D | -0.13% | -0.07% | -0.18% | 145% | 104%
Class E | -0.10% | -0.27% | -0.15% | 158% | 103%
Overall | -0.18% | -0.24% | -0.34% | 149% | 102%
Class F (optional) | -0.17% | -0.07% | 0.05% | 148% | 102%
All intra main10

## Slide 7: Experimental results
 | Method 1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.15% | -0.23% | -0.69% | 115% | 100%
Class A2 | -0.02% | -0.94% | -1.12% | 109% | 101%
Class B | -0.04% | -0.41% | -0.62% | 110% | 102%
Class C | -0.13% | -0.45% | -0.44% | 110% | 102%
Class D | 0.00% | -0.49% | -0.08% | 108% | 102%
Class E |  |  |  |  | 
Overall | -0.07% | -0.50% | -0.59% | 110% | 101%
Class F (optional) | -0.04% | -0.18% | -0.25% | 115% | 105%
 | Method 2 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | -0.16% | -0.62% | 115% | 98%
Class A2 | -0.03% | -0.65% | -0.85% | 110% | 99%
Class B | -0.05% | -0.43% | -0.61% | 110% | 100%
Class C | -0.15% | -0.15% | -0.32% | 109% | 101%
Class D | -0.01% | -0.33% | -0.10% | 107% | 102%
Class E |  |  |  |  | 
Overall | -0.08% | -0.35% | -0.50% | 110% | 100%
Class F (optional) | -0.10% | -0.33% | -0.23% | 114% | 102%
Random access main10

## Slide 8
NSST kernel size portion in over 8x8 blocks
  4x4 NSST kernel is more efficient in some case over 8x8 blocks
Cactus (qp22 / All intra CTC.)

## Slide 9: Conclusion
Recommendation
  Study in EE for kernel size of NSST