## Slide 1: [JVET-F0027] JEM vs HM performance for 360-video content under CfE test condition
Anubhav Singh,
Chirag Pujara, Sri Nitchith Akula,
Amith Dsouza, Ramkumaar KK,
Raj Narayana Gadde, Vladyslav Zakharchenko,
Elena Alshina, Kwang Pyo Choi

## Slide 2: Table of content
Test Condition
HM vs JEM results
  Subjective
  Objective
Objective Result analysis
JEM results
Conclusion

## Slide 3: Test Condition
Tests are conducted according to CfE document JVET-E1002 and CTC document JVET-E1030
Input
  4 sequences in ERP format
  8K each
  Reconstructed sequences 4K
Target Bitrate
  Target bitrates are same for HM and JEM and are taken from JVET-E1002
 | Target bitrates [kbps] |  |  | 
Sequences | Rate 1 | Rate 2 | Rate 3 | Rate 4
SkateboardInLot | 2000 | 3300 | 6000 | 10000
Chairlift | 1500 | 2400 | 4000 | 7000
KiteFlite | 1500 | 2400 | 4000 | 7000
Harbor | 1200 | 2000 | 3300 | 6000

## Slide 4: Test Condition
JEM 5.0.1
360Lib 2.1
For comparison HM 16.15
PSNRS used
  E2E-SPSNR-NN, E2E-SPSNR-I, E2E-WSPSNR, E2E-CPPPSNR
    Compares Original High-Fidelity ERP with reconstructed High-Fidelity ERP
  CF-SPSNR-NN, CF-SPSNR-I, CF-CPPPSNR
    Compares original High-Fidelity ERP with reconstructed Low-Fidelity ERP
  DYN-VP-PSNR-0, DYN-VP-PSNR-1
    Considers 2 viewports and compares the PSNRs
  WS-PSNR
    Compares the Low fidelity ERP across encoder/decoder
  Encoder PSNR
    Compares the Low fidelity ERP across encoder/decoder

## Slide 5: JEM Results Summary
Sequence | Target Bitrate | QP Slice | QPIF | kbps | Diff to Target | E2E WS-PSNR Y | E2E WS-PSNR U | E2E WS-PSNR V
Skateboarding_in_lot | 10000 | 27 | 272 | 10062.7 | 0.6% | 39.20 | 47.98 | 49.27
 | 6000 | 29 | 16 | 5992.9 | -0.12% | 37.93 | 47.20 | 48.64
 | 3300 | 32 | 16 | 3355.9 | 1.7% | 36.58 | 46.56 | 48.12
 | 2000 | 35 | 112 | 2010.7 | 0.5% | 35.39 | 45.83 | 47.47
Chairlift | 7000 | 26 | 144 | 7130.7 | 1.9% | 40.47 | 47.63 | 48.88
 | 4000 | 30 | 272 | 3979.4 | -0.5% | 38.74 | 46.52 | 48.08
 | 2400 | 33 | 240 | 2423.9 | 1.0% | 37.28 | 45.82 | 47.56
 | 1500 | 36 | 272 | 1486.0 | -0.9% | 35.95 | 44.88 | 46.81
KiteFlite | 7000 | 29 | 176 | 7056.8 | 0.8% | 37.57 | 47.01 | 47.88
 | 4000 | 33 | 112 | 4026.4 | 0.7% | 35.28 | 45.80 | 46.90
 | 2400 | 37 | 208 | 2404.5 | 0.2% | 33.25 | 44.76 | 45.99
 | 1500 | 40 | 144 | 1509.8 | 0.7% | 31.53 | 43.99 | 45.29
Harbor | 6000 | 23 | 80 | 6067.1 | 1.1% | 42.72 | 51.47 | 50.82
 | 3300 | 27 | 48 | 3336.7 | 1.1% | 41.13 | 50.25 | 49.88
 | 2000 | 31 | 208 | 2013.5 | 0.7% | 39.59 | 49.16 | 48.99
 | 1200 | 34 | 80 | 1210.0 | 0.8% | 37.92 | 48.16 | 48.17

## Slide 6: HM Vs JEM : Subjective
As bitrate are same, visual quality comparison becomes easy
For the same bitrate JEM output is on an average ~1 dB better in terms of WS-PSNR E2E as compared to HM.
HM output seems to be more blurry and has more blockiness as compared to JEM output at the same bitrate.
There are seams visible in viewports covering the edges of ERP.
Subjective viewing session can provide better visualization of these.

## Slide 7: HM Vs JEM : Subjective
Chairlift _Original

## Slide 8: HM Vs JEM : Subjective
HM Viewport for Chairlift
JEM Viewport for Chairlift
Target bitrate : 2400 kbps Viewport : (-180,0) (frame boundary)

## Slide 9: HM Vs JEM : Objective
Test video | Target rate | HM based anchor |  |  |  | JEM based anchor |  |  | 
 |  | Actual rate | Diff to target | QP | QP switch frame | Actual rate | Diff to target | QP | QP switch frame
Skateboard-ing_in_lot | 10000 | 9858.0 | -1.4% | 27 | 64 | 10062.7 | 0.6% | 27 | 272
 | 6000 | 5924.9 | -1.3% | 30 | 144 | 5992.9 | -0.12% | 29 | 16
 | 3300 | 3269.8 | -0.9% | 33 | 64 | 3355.9 | 1.7% | 32 | 16
 | 2000 | 1975.0 | -1.3% | 36 | 96 | 2010.7 | 0.5% | 35 | 112
Chairlift | 7000 | 6997.2 | 0.0% | 27 | 64 | 7130.7 | 1.9% | 26 | 144
 | 4000 | 3962.7 | -0.9% | 31 | 208 | 3979.4 | -0.5% | 30 | 272
 | 2400 | 2372.6 | -1.1% | 34 | 176 | 2423.9 | 1.0% | 33 | 240
 | 1500 | 1479.3 | -1.4% | 37 | 272 | 1486.0 | -0.9% | 36 | 272
KiteFlite | 7000 | 6963.9 | -0.5% | 30 | 300 | 7056.8 | 0.8% | 29 | 176
 | 4000 | 3958.4 | -1.0% | 34 | 208 | 4026.4 | 0.7% | 33 | 112
 | 2400 | 2396.4 | -0.1% | 37 | 64 | 2404.5 | 0.2% | 37 | 208
 | 1500 | 1490.2 | -0.7% | 40 | 32 | 1509.8 | 0.7% | 40 | 144
Harbor | 6000 | 5973.1 | -0.4% | 24 | 208 | 6067.1 | 1.1% | 23 | 80
 | 3300 | 3265.1 | -1.1% | 28 | 176 | 3336.7 | 1.1% | 27 | 48
 | 2000 | 1972.9 | -1.4% | 31 | 32 | 2013.5 | 0.7% | 31 | 208
 | 1200 | 1189.0 | -0.9% | 35 | 240 | 1201.1 | 0.8% | 34 | 80

## Slide 10: HM Vs JEM : Objective
Quality Metric | BD-rate |  | 
 | Y | U | V
E2E SPSNR-NN | -23.5% | -49.6% | -51.7%
E2E SPSNR-I | -23.5% | -49.5% | -51.6%
E2E CPP-PSNR | -23.5% | -49.5% | -51.6%
E2E WS-PSNR | -23.5% | -49.6% | -51.7%
PSNR DYN-VP0 | -24.6% | -50.8% | -46.6%
PSNR DYN-VP1 | -26.3% | -50.5% | -46.4%
CF SPSNR-NN | -22.6% | -49.8% | -52.0%
CF SPSNR-I | -23.5% | -49.6% | -51.7%
CF CPP-PSNR | -23.5% | -49.7% | -51.8%
WS-PSNR | -23.7% | -51.1% | -52.8%
PSNR | -24.3% | -52.1% | -55.6%
The average BD rate gain is ~23% (for Luma)
CF-PSNRs and E2E PSNRS are almost equal as the coding format is same
as input format
Gain for KiteFlite is more than 30%, while Harbor and Chairlift is less than 20%

## Slide 11: HM Vs JEM : Objective

## Slide 12: HM Vs JEM : Objective
11 PSNRs are used for quality assessment.
Most of them require interpolation, causing inadequacy in representation.
It is desirable that majority of pixels should be considered for quality measure (in both input and output)
 | E2E SPSNR-NN | E2E SPSNR-I | E2E CPP-PSNR | E2E WS-PSNR | PSNR DYN-VP | CF SPSNR-NN | CF SPSNR-I | CF CPP-PSNR | WS-PSNR (Enc) | PSNR (Enc)
Interpolation steps (Orig/Rec) | (0/2) | (1/3) | (1/4) | (0/3) | (1/2) | (0/1) | (1/2) | (1/2) | (0/0) | (0/0)
Weighted MSE | N | N | N | Y | N | N | N | N | Y | N
Cross Format | Y | Y | Y | Y | Y | Y* | Y | Y | N | N
%-age of Active Pixels Considered (4K, Luma) | 8.8% | 90.7% | 98.4% | 100% | NA | NA | NA | NA | 100% | 100%

## Slide 13: HM Vs JEM : Observations
There are many quality metrics, which almost always confirm with each other, resulting in more testing time.
There are more conversion steps with interpolation in E2E metrics than CF metrics.
Metrics with integer rounding considerably reduce the number of pixels considered (almost by a factor of 10).
Integer rounding also results in comparison of samples with different locations in original and decompressed signal (which is inaccurate).

## Slide 14: Conclusion
JEM outperforms HM under CfE test conditions by 23% for 360-videos as compared to 33% in SDR videos.
The BD rate based on different metrics are same if there is no projection conversion.
Recommended to reduce number of PSNR metrics.
Recommended to reduce number of interpolation steps for quality assessment.
Nearest Integer Rounding PSNR methods have following problems:
  Inaccurate (compares different samples)
  Prone to errors (consider considerably less number of pixels (1/10x), hence could miss out on noise/error pixels)

## Slide 15: Thank You

## Slide 16: Addendum

## Slide 17: JEM PSNRs Comparison (Luma)

## Slide 18: HM PSNRs Comparison (Luma)