## Slide 1
JVET-F0072
Stretching ratio based adaptive quantization for 360 video
Yule Sun, Lu Yu,
Zhejiang University

## Slide 2: Summary
Introduction
Stretching ratio based adaptive quantization
Experimental results
Conclusion

## Slide 3: Introduction
Mapping from equirectangular to spherical surface
Content of 360 video is spherically uniform.
Sample interval on projection is not uniform.
Example: ERP (Coded with constant QP)
Distortion strength near the pole in ERP
is smaller than that in equator.
(Larger stretching ratio, less distortion)
Not correct for 360 video !

## Slide 4: Stretching ratio based adaptive quantization
To make distortion strength uniform in spherical space:
Implemented in CTU-level, so is the average stretching level for i-th CTU

## Slide 5: Stretching ratio based adaptive quantization
To make the rate close to the anchor: normalize

## Slide 6: Stretching ratio based adaptive quantization
For ERP(2a*a):
QP_offset in each CTU row
Ratio of MSE in each CTU row

## Slide 7: Experimental results
Proposed vs. ERP | SPSNR-NN (End to End) |  |  | SPSNR-I (End to End) |  | 
 | Y | U | V | Y | U | V
Trolley | 0.6% | 2.2% | 1.3% | 0.6% | 2.2% | 1.4%
GasLamp | 0.7% | 2.0% | 3.8% | 0.7% | 2.0% | 3.8%
Skateboarding_in_lot | -4.9% | -7.0% | -4.7% | -4.9% | -7.0% | -4.7%
Chairlift | -4.9% | -1.5% | -0.1% | -4.9% | -1.5% | -0.1%
KiteFlite | -1.2% | 1.1% | 0.5% | -1.2% | 1.1% | 0.5%
Harbor | 0.7% | 3.1% | 3.1% | 0.8% | 3.1% | 3.1%
PoleVault | -5.4% | -2.1% | -1.8% | -5.4% | -2.0% | -1.7%
AerialCity | -2.3% | 0.8% | 0.4% | -2.3% | 0.8% | 0.4%
DrivingInCity | 0.6% | 6.8% | 6.0% | 0.6% | 6.8% | 6.0%
DrivingInCountry | -5.5% | -4.4% | -3.9% | -5.4% | -4.5% | -4.0%
Overall | -2.2% | 0.1% | 0.5% | -2.2% | 0.1% | 0.5%
CPP-PSNR (End to End) |  |  | WS-PSNR (End to End) |  |  | WS-PSNR (codec) |  | 
Y | U | V | Y | U | V | Y | U | V
0.6% | 2.2% | 1.4% | 0.6% | 2.2% | 1.4% | 0.6% | 2.3% | 1.5%
0.7% | 2.0% | 3.8% | 0.7% | 2.0% | 3.8% | 0.6% | 2.0% | 3.8%
-4.9% | -7.0% | -4.8% | -4.9% | -6.9% | -4.8% | -5.2% | -6.8% | -4.7%
-4.8% | -1.4% | -0.1% | -4.8% | -1.4% | -0.1% | -5.0% | -1.3% | 0.0%
-1.3% | 1.0% | 0.4% | -1.3% | 1.0% | 0.5% | -1.3% | 1.1% | 0.5%
0.7% | 3.1% | 3.2% | 0.7% | 3.1% | 3.2% | 0.8% | 3.1% | 3.2%
-5.4% | -2.0% | -1.7% | -5.3% | -2.0% | -1.8% | -5.5% | -2.2% | -1.9%
-2.2% | 0.9% | 0.4% | -2.2% | 0.8% | 0.4% | -2.3% | 1.0% | 0.6%
0.6% | 6.8% | 6.0% | 0.6% | 6.8% | 6.0% | 0.6% | 6.8% | 6.1%
-5.5% | -4.6% | -4.0% | -5.5% | -4.4% | -3.9% | -5.6% | -4.4% | -3.9%
-2.2% | 0.1% | 0.5% | -2.1% | 0.1% | 0.5% | -2.2% | 0.2% | 0.5%

## Slide 8: Stretching ratio based adaptive quantization
 | constant QP | Adaptive QP | Realtionship | RD-Performance without weight | RD-Performance with weight
Blue area | D1, R1 | D2,R2 | D2>D1,R2<R1 | UNCHANGED | BETTER
Yellow area | D3,R3 | D4,R4 | D3=D4,R3=R4 | UNCHANGED | UNCHANGED
White area | D5,R5 | D6,R6 | D6<D6,R6>R5 | UNCHANGED | BETTER

## Slide 9: Conclusion
Stretching ratio based adaptive quantization for 360 video is proposed to make quality in spherical space uniform, which can improve coding efficiency too.
Other projection formats can also be applied to adjust quantization according to weight map derived in WS-PSNR.
Decoder side can derived the QPoffset according Pos
Consider the influence of stretching ratio in viewport-based subjective test .

## Slide 10
Thank you for your attention!