## Slide 1: JVET-J0077 “Deblocking Improvements for Large CUs”
W. Zhu, K. Misra, A. Segall (Sharp)

## Slide 2: Blocking artifacts in JEM7
Sometimes we see blocking artifact around large blocks
Sometimes we see artifact when using Local Illumination Compensation (LIC)
Observation at low bit rates

## Slide 3: Proposed modification
Use stronger filters for large blocks (on either side of the edge boundary)
Deblock larger number of samples for all sides of a large block
Deblock larger number of samples for all sides of a large LIC block when transform coefficients are zero (CBF=0)

## Slide 4: Example illustration of large block deblocking
64
16
64
Stronger filters
JEM7 filters
LUMA
64
16
64
CHROMA
Deblock 7 samples for large-block side
Deblock 3 samples when either side of boundary is large-block
Proposal uses current block size as well as adjacent block size in deblocking control

## Slide 5: Sample visual improvements
JEM7
JEM7+proposed modification

## Slide 6: Conclusion
We describe the following modifications of JEM7 deblocking:
  Use of stronger filters for large blocks
  Deblock larger number of samples for large blocks
  Deblock boundaries when LIC is used and CBF=0
The changes are asserted to show visual benefit
We propose studying the approach in a CE

## Slide 7
Thank You

## Slide 8
BACKUP SLIDES

## Slide 9: Luma deblocking flow chart

## Slide 10: Stronger filter for luma
Same as in JVET-J0028
p6′= (7*p7+2*p6+p5+p4+p3+p2+ p1+p0+q0+ 8) >> 4
p5′= (6*p7+p6+2*p5+p4+p3+p2+p1+p0+q0+q1+ 8) >> 4
p4′= (5*p7+p6+p5+2*p4+p3+p2+p1+p0+q0+q1+q2+ 8) >> 4
p3′= (4*p7+p6+p5+p4+2*p3+p2+p1+p0+q0+q1+q2+q3+ 8) >> 4
p2′= (3*p7+p6+p5+p4+p3+2*p2+p1+p0+q0+q1+q2+q3+q4+8) >> 4
p1′= (2*p7+p6+p5+p4+p3+p2+2*p1+p0+q0+q1+q2+q3+q4+q5+8) >> 4
p0′= (p7+p6+p5+p4+p3+p2+p1+2*p0+q0+q1+q2+q3+q4+q5+q6+8) >> 4

## Slide 11: Chroma deblocking flow chart

## Slide 12: Stronger filter for chroma
p0′= (p2 +2*p1+2*p0+2*q0+q1 +4) >> 3
p1′= (p2+p1+ p0+q0+2) >> 2
p2′= (p4+2*p3+3*p2+ p1+ p0+4) >> 3
q0′= (q2 +2*q1+2*q0+2*p0+p1 +4) >> 3
q1′= (q2+q1+ q0+p0+2) >> 2
q2′= (q4+2*q3+3*q2+ q1+ q0+4) >> 3