## Slide 1: CE1: Summary report on Partitioning

## Slide 2: General information for CE1
All participants submitted at least an initial software in time
CE coordinators have received most of the result in time
All SubCE test were cross checked by at least one other person from the participant list
Cross-checking information showed no significant mismatches in BD rates
Mismatches in timings were observed in tests

## Slide 3: Sub-categories in CE1
SubCE1: Picture boundary handling
SubCE2: Split constraints
SubCE3: Separate trees for luma and chroma

## Slide 4: Overall results
(For SubCE3-3.1.1 and SubCE3-3.1.2 there are updated results available in JVET-L0424 that harmonizes the timings.)
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SubCE1-1.1.1 | 0,00% | 0,01% | 0,02% | 99% | 98% | 0,02% | 0,08% | 0,01% | 99% | 98% | 0,03% | -0,10% | -0,24% | 98% | 98%
SubCE1-1.2.1 | 0,06% | 0,10% | 0,12% | 98% | 101% | 0,00% | 0,02% | 0,07% | 100% | 99% | -0,10% | -0,02% | -0,27% | 99% | 97%
SubCE1-1.2.2 | 0,07% | 0,09% | 0,11% | 100% | 100% | 0,12% | 0,17% | 0,18% | 100% | 100% | 0,20% | 0,10% | 0,07% | 99% | 96%
SubCE1-1.3.1 | 0,00% | 0,00% | 0,00% | 93% | 92% | -0,02% | -0,01% | -0,06% | 93% | 88% | -0,08% | -0,14% | -0,21% | 93% | 88%
SubCE2-2.1.1 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,26% | 0,35% | 0,25% | 95% | 104% | 0,30% | 0,23% | 0,20% | 98% | 101%
SubCE2-2.1.2 | 0,00% | 0,00% | 0,00% | 100% | 101% | 0,15% | 0,20% | 0,14% | 94% | 101% | 0,06% | 0,09% | -0,15% | 98% | 100%
SubCE2-2.1.3 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,35% | 0,43% | 0,27% | 87% | 101% | 0,22% | 0,21% | 0,13% | 91% | 101%
SubCE2-2.1.4 | 0,00% | 0,00% | 0,00% | 100% | 100% | 1,55% | 1,28% | 1,15% | 84% | 102% | 0,95% | 0,75% | 0,60% | 87% | 100%
SubCE3-3.1.1 | -0,01% | -0,07% | -0,06% | 111% | 111% | -0,13% | -2,32% | -1,87% | 122% | 101% | -0,03% | -0,55% | -0,63% | 115% | 102%
SubCE3-3.1.1-syn |  |  |  |  |  | -0,69% | -3,24% | -3,04% | 140% | 102% | -0.47% | -4.18% | -5.06% | 126% | 82%
SubCE3-3.1.2 | 0,02% | -0,05% | -0,05% | 89% | 90% | -0,11% | -2,25% | -1,89% | 129% | 104% | 0,00% | -0,66% | -0,89% | 110% | 97%
SubCE3-3.1.2-syn |  |  |  |  |  | -0,69% | -3,24% | -3,04% | 144% | 100% | -0.47% | -4.09% | -5.07% | 116% | 80%
SubCE3-3.2.1 | -0,01% | -0,07% | -0,06% | 85% | 92% | 0,01% | 0,01% | 0,02% | 94% | 95% | -0,04% | -0,06% | -0,08% | 82% | 89%
SubCE3-3.2.1-syn |  |  |  |  |  | 0.00% | 0.01% | 0.01% | 88% | 92% | 0.01% | 0.01% | 0.03% | 77% | 80%
SubCE3-3.2.2 | 0,02% | -0,05% | -0,05% | 85% | 91% | -0,11% | -2,24% | -1,87% | 106% | 90% | 0,04% | -0,43% | -0,78% | 92% | 89%
SubCE3-3.2.2-syn |  |  |  |  |  | -0.69% | -3.24% | -3.04% | 124% | 96% | -0.47% | -4.10% | -5.06% | 114% | 82%

## Slide 5: Overall results: Picture boundary
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SubCE1-1.1.1 | 0,00% | 0,01% | 0,02% | 99% | 98% | 0,02% | 0,08% | 0,01% | 99% | 98% | 0,03% | -0,10% | -0,24% | 98% | 98%
SubCE1-1.2.1 | 0,06% | 0,10% | 0,12% | 98% | 101% | 0,00% | 0,02% | 0,07% | 100% | 99% | -0,10% | -0,02% | -0,27% | 99% | 97%
SubCE1-1.2.2 | 0,07% | 0,09% | 0,11% | 100% | 100% | 0,12% | 0,17% | 0,18% | 100% | 100% | 0,20% | 0,10% | 0,07% | 99% | 96%
SubCE1-1.3.1 | 0,00% | 0,00% | 0,00% | 93% | 92% | -0,02% | -0,01% | -0,06% | 93% | 88% | -0,08% | -0,14% | -0,21% | 93% | 88%
SubCE2-2.1.1 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,26% | 0,35% | 0,25% | 95% | 104% | 0,30% | 0,23% | 0,20% | 98% | 101%
SubCE2-2.1.2 | 0,00% | 0,00% | 0,00% | 100% | 101% | 0,15% | 0,20% | 0,14% | 94% | 101% | 0,06% | 0,09% | -0,15% | 98% | 100%
SubCE2-2.1.3 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,35% | 0,43% | 0,27% | 87% | 101% | 0,22% | 0,21% | 0,13% | 91% | 101%
SubCE2-2.1.4 | 0,00% | 0,00% | 0,00% | 100% | 100% | 1,55% | 1,28% | 1,15% | 84% | 102% | 0,95% | 0,75% | 0,60% | 87% | 100%
SubCE3-3.1.1 | -0,01% | -0,07% | -0,06% | 111% | 111% | -0,13% | -2,32% | -1,87% | 122% | 101% | -0,03% | -0,55% | -0,63% | 115% | 102%
SubCE3-3.1.1-syn |  |  |  |  |  | -0,69% | -3,24% | -3,04% | 140% | 102% | -0.47% | -4.18% | -5.06% | 126% | 82%
SubCE3-3.1.2 | 0,02% | -0,05% | -0,05% | 89% | 90% | -0,11% | -2,25% | -1,89% | 129% | 104% | 0,00% | -0,66% | -0,89% | 110% | 97%
SubCE3-3.1.2-syn |  |  |  |  |  | -0,69% | -3,24% | -3,04% | 144% | 100% | -0.47% | -4.09% | -5.07% | 116% | 80%
SubCE3-3.2.1 | -0,01% | -0,07% | -0,06% | 85% | 92% | 0,01% | 0,01% | 0,02% | 94% | 95% | -0,04% | -0,06% | -0,08% | 82% | 89%
SubCE3-3.2.1-syn |  |  |  |  |  | 0.00% | 0.01% | 0.01% | 88% | 92% | 0.01% | 0.01% | 0.03% | 77% | 80%
SubCE3-3.2.2 | 0,02% | -0,05% | -0,05% | 85% | 91% | -0,11% | -2,24% | -1,87% | 106% | 90% | 0,04% | -0,43% | -0,78% | 92% | 89%
SubCE3-3.2.2-syn |  |  |  |  |  | -0.69% | -3.24% | -3.04% | 124% | 96% | -0.47% | -4.10% | -5.06% | 114% | 82%

## Slide 6: SubCE1-1.1.1 (JVET-L0080)
Ignore the QT-split restrictions at the picture boundary
Always infer a QT split if three corner points exceed the picture boundary
The additional BT depth counter at the boundary is removed to ensure the BT depth does not violate the specified maximum BT depth.
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,00% | 0,00% | 100% | 99% | 0,00% | 0,03% | 0,03% | 99% | 98% |  |  |  |  | 
Class A2 | 0,00% | 0,00% | 0,00% | 99% | 100% | 0,00% | 0,00% | -0,06% | 100% | 100% |  |  |  |  | 
Class B | 0,00% | 0,02% | 0,05% | 99% | 98% | 0,04% | 0,11% | -0,01% | 98% | 99% | 0,05% | 0,12% | 0,06% | 99% | 101%
Class C | 0,00% | 0,02% | 0,05% | 99% | 97% | 0,02% | 0,15% | 0,06% | 97% | 96% | 0,04% | -0,08% | -0,16% | 98% | 96%
Class E | 0,00% | -0,01% | 0,00% | 99% | 97% |  |  |  |  |  | -0,03% | -0,50% | -0,84% | 98% | 95%
Overall | 0,00% | 0,01% | 0,02% | 99% | 98% | 0,02% | 0,08% | 0,01% | 99% | 98% | 0,03% | -0,10% | -0,24% | 98% | 98%
Class D | 0,02% | 0,14% | -0,02% | 97% | 100% | 0,04% | 0,29% | 0,21% | 94% | 97% | 0,05% | 0,25% | -0,18% | 97% | 96%
Class F (optional) | 0,01% | 0,06% | 0,07% | 99% | 98% | 0,02% | 0,10% | 0,04% | 98% | 96% | 0,04% | 0,10% | -0,14% | 98% | 95%

## Slide 7: SubCE1-1.2.1 (JVET-L0268)
A Zero Unit (ZU) is a CU with width or height not being a power of 2
In current VTM a CU with non-power of 2 width or height is further split.
The cbf_flag for ZUs must be signaled to be 0 by an encoder restriction.
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,02% | 0,07% | 0,06% | 100% | 104% | -0,05% | -0,03% | -0,09% | 100% | 100% |  |  |  |  | 
Class A2 | 0,00% | 0,06% | 0,01% | 100% | 102% | -0,01% | 0,01% | -0,15% | 100% | 99% |  |  |  |  | 
Class B | 0,03% | 0,08% | 0,07% | 99% | 100% | -0,05% | -0,06% | 0,11% | 101% | 100% | -0,01% | -0,17% | -0,41% | 101% | 102%
Class C | 0,12% | 0,23% | 0,33% | 95% | 97% | 0,10% | 0,16% | 0,31% | 98% | 97% | 0,09% | 0,31% | 0,11% | 97% | 95%
Class E | 0,14% | 0,02% | 0,07% | 99% | 101% |  |  |  |  |  | -0,50% | -0,19% | -0,51% | 99% | 91%
Overall | 0,06% | 0,10% | 0,12% | 98% | 101% | 0,00% | 0,02% | 0,07% | 100% | 99% | -0,10% | -0,02% | -0,27% | 99% | 97%
Class D | 0,32% | 0,66% | 0,44% | 93% | 103% | 0,07% | 0,33% | 0,30% | 97% | 102% | 0,15% | 1,04% | 0,10% | 98% | 97%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8: SubCE1-1.2.2 (JVET-L0268)
A Zero Unit (ZU) is a CU with width or height not being a power of 2
In current VTM a CU with non-power of 2 width or height is further split.
ZUs must be further split by an encoder restriction .
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,04% | 0,08% | 0,00% | 102% | 105% | 0,11% | 0,14% | 0,09% | 100% | 100% |  |  |  |  | 
Class A2 | 0,02% | 0,06% | 0,03% | 100% | 100% | 0,07% | 0,14% | 0,00% | 101% | 99% |  |  |  |  | 
Class B | 0,06% | 0,05% | 0,06% | 100% | 100% | 0,13% | 0,15% | 0,22% | 100% | 99% | 0,16% | 0,08% | 0,10% | 100% | 100%
Class C | 0,12% | 0,23% | 0,33% | 96% | 98% | 0,14% | 0,23% | 0,34% | 98% | 100% | 0,15% | 0,02% | 0,01% | 97% | 94%
Class E | 0,14% | 0,02% | 0,07% | 100% | 98% |  |  |  |  |  | 0,33% | 0,27% | 0,13% | 99% | 94%
Overall | 0,07% | 0,09% | 0,11% | 100% | 100% | 0,12% | 0,17% | 0,18% | 100% | 100% | 0,20% | 0,10% | 0,07% | 99% | 96%
Class D | 0,33% | 0,63% | 0,46% | 93% | 99% | 0,41% | 0,64% | 0,67% | 96% | 102% | 0,46% | 1,45% | 1,08% | 97% | 101%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 9: SubCE1-1.3.1 (JVET-L0310)
A partial CU is a CU which contains areas inside and outside the picture.
The concept of a partial CU is only used for in non-intra slices.
Only the area inside the picture is further coded.
Only partial CUs are considered when the CU is coded as non-split and the part inside the picture boundaries has width or height non-power of 2.
The residual is not coded for a partial CU and the skip flag is inferred as true.
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,00% | 0,00% | 94% | 94% | -0,04% | 0,00% | -0,02% | 94% | 93% |  |  |  |  | 
Class A2 | 0,00% | 0,00% | 0,00% | 94% | 95% | -0,01% | -0,06% | -0,10% | 94% | 93% |  |  |  |  | 
Class B | 0,00% | 0,00% | 0,00% | 93% | 93% | -0,01% | 0,01% | -0,07% | 93% | 87% | -0,01% | 0,00% | 0,07% | 95% | 97%
Class C | 0,00% | 0,00% | 0,00% | 92% | 90% | 0,00% | -0,01% | -0,03% | 92% | 81% | 0,03% | -0,14% | -0,17% | 91% | 82%
Class E | 0,00% | 0,00% | 0,00% | 93% | 90% |  |  |  |  |  | -0,34% | -0,39% | -0,74% | 92% | 84%
Overall | 0,00% | 0,00% | 0,00% | 93% | 92% | -0,02% | -0,01% | -0,06% | 93% | 88% | -0,08% | -0,14% | -0,21% | 93% | 88%
Class D | 0,00% | 0,00% | 0,00% | 92% | 83% | -0,06% | -0,08% | -0,09% | 92% | 75% | 0,03% | 0,49% | 0,04% | 92% | 76%
Class F (optional) | 0,00% | 0,00% | 0,00% | 92% | 91% | -0,01% | -0,03% | -0,02% | 93% | 83% | -0,18% | 0,50% | 0,26% | 91% | 84%

## Slide 10: Overall results: Split constraints
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SubCE1-1.1.1 | 0,00% | 0,01% | 0,02% | 99% | 98% | 0,02% | 0,08% | 0,01% | 99% | 98% | 0,03% | -0,10% | -0,24% | 98% | 98%
SubCE1-1.2.1 | 0,06% | 0,10% | 0,12% | 98% | 101% | 0,00% | 0,02% | 0,07% | 100% | 99% | -0,10% | -0,02% | -0,27% | 99% | 97%
SubCE1-1.2.2 | 0,07% | 0,09% | 0,11% | 100% | 100% | 0,12% | 0,17% | 0,18% | 100% | 100% | 0,20% | 0,10% | 0,07% | 99% | 96%
SubCE1-1.3.1 | 0,00% | 0,00% | 0,00% | 93% | 92% | -0,02% | -0,01% | -0,06% | 93% | 88% | -0,08% | -0,14% | -0,21% | 93% | 88%
SubCE2-2.1.1 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,26% | 0,35% | 0,25% | 95% | 104% | 0,30% | 0,23% | 0,20% | 98% | 101%
SubCE2-2.1.2 | 0,00% | 0,00% | 0,00% | 100% | 101% | 0,15% | 0,20% | 0,14% | 94% | 101% | 0,06% | 0,09% | -0,15% | 98% | 100%
SubCE2-2.1.3 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,35% | 0,43% | 0,27% | 87% | 101% | 0,22% | 0,21% | 0,13% | 91% | 101%
SubCE2-2.1.4 | 0,00% | 0,00% | 0,00% | 100% | 100% | 1,55% | 1,28% | 1,15% | 84% | 102% | 0,95% | 0,75% | 0,60% | 87% | 100%
SubCE3-3.1.1 | -0,01% | -0,07% | -0,06% | 111% | 111% | -0,13% | -2,32% | -1,87% | 122% | 101% | -0,03% | -0,55% | -0,63% | 115% | 102%
SubCE3-3.1.1-syn |  |  |  |  |  | -0,69% | -3,24% | -3,04% | 140% | 102% | -0.47% | -4.18% | -5.06% | 126% | 82%
SubCE3-3.1.2 | 0,02% | -0,05% | -0,05% | 89% | 90% | -0,11% | -2,25% | -1,89% | 129% | 104% | 0,00% | -0,66% | -0,89% | 110% | 97%
SubCE3-3.1.2-syn |  |  |  |  |  | -0,69% | -3,24% | -3,04% | 144% | 100% | -0.47% | -4.09% | -5.07% | 116% | 80%
SubCE3-3.2.1 | -0,01% | -0,07% | -0,06% | 85% | 92% | 0,01% | 0,01% | 0,02% | 94% | 95% | -0,04% | -0,06% | -0,08% | 82% | 89%
SubCE3-3.2.1-syn |  |  |  |  |  | 0.00% | 0.01% | 0.01% | 88% | 92% | 0.01% | 0.01% | 0.03% | 77% | 80%
SubCE3-3.2.2 | 0,02% | -0,05% | -0,05% | 85% | 91% | -0,11% | -2,24% | -1,87% | 106% | 90% | 0,04% | -0,43% | -0,78% | 92% | 89%
SubCE3-3.2.2-syn |  |  |  |  |  | -0.69% | -3.24% | -3.04% | 124% | 96% | -0.47% | -4.10% | -5.06% | 114% | 82%

## Slide 11: SubCE1-2.1.1 (JVET-L0081)
If one of the following conditions is true, then a CU has to be further split:
  If the top-left position of the current CU is the top-left position of a VPDU and
    the width of the current CU is larger than 64 but not a multiple of 64 or
    the height of the current CU is larger than 64 but not a multiple of 64 or
    the VPDU to the left and the VPDU to the top of the current CU are not yet completely encoded
  If the current CU is not completely contained by a VPDU
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,41% | 0,60% | 0,48% | 90% | 105% |  |  |  |  | 
Class A2 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,52% | 0,48% | 0,38% | 95% | 107% |  |  |  |  | 
Class B | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,21% | 0,30% | 0,22% | 95% | 103% | 0,15% | 0,21% | 0,02% | 98% | 103%
Class C | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,03% | 0,14% | 0,03% | 98% | 101% | 0,06% | 0,08% | 0,03% | 99% | 100%
Class E | 0,00% | 0,00% | 0,00% | 100% | 100% |  |  |  |  |  | 0,85% | 0,45% | 0,74% | 96% | 100%
Overall | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,26% | 0,35% | 0,25% | 95% | 104% | 0,30% | 0,23% | 0,20% | 98% | 101%
Class D | 0,00% | 0,00% | 0,00% | 100% | 101% | 0,08% | 0,15% | 0,09% | 98% | 99% | 0,10% | 0,49% | -0,55% | 100% | 99%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 12: SubCE1-2.1.2 (JVET-L0081)
A 128x128 CTU cannot be split by a TT split
64x128 and 128x64 CUs cannot be partitioned by a TT split
128x64 CU cannot be partitioned using a horizontal BT split
64x128 CU cannot be partitioned using a vertical BT split
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,22% | 0,32% | 0,22% | 90% | 100% |  |  |  |  | 
Class A2 | 0,00% | 0,00% | 0,00% | 100% | 101% | 0,38% | 0,34% | 0,26% | 94% | 101% |  |  |  |  | 
Class B | 0,00% | 0,00% | 0,00% | 100% | 101% | 0,08% | 0,16% | 0,11% | 95% | 100% | 0,06% | 0,07% | -0,16% | 98% | 101%
Class C | 0,00% | 0,00% | 0,00% | 99% | 101% | 0,02% | 0,07% | 0,04% | 98% | 101% | 0,02% | 0,01% | -0,17% | 99% | 101%
Class E | 0,00% | 0,00% | 0,00% | 100% | 100% |  |  |  |  |  | 0,10% | 0,22% | -0,12% | 95% | 97%
Overall | 0,00% | 0,00% | 0,00% | 100% | 101% | 0,15% | 0,20% | 0,14% | 94% | 101% | 0,06% | 0,09% | -0,15% | 98% | 100%
Class D | 0,00% | 0,00% | 0,00% | 100% | 102% | 0,00% | -0,01% | 0,03% | 98% | 100% | 0,06% | 0,28% | 0,01% | 99% | 100%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 13: SubCE1-2.1.3 (JVET-L0081)
The maximum BT and TT sizes are set to 64.
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,69% | 0,88% | 0,63% | 78% | 101% |  |  |  |  | 
Class A2 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,67% | 0,64% | 0,45% | 86% | 102% |  |  |  |  | 
Class B | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,24% | 0,28% | 0,16% | 88% | 101% | 0,17% | 0,08% | 0,14% | 92% | 102%
Class C | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,01% | 0,11% | 0,01% | 95% | 100% | 0,05% | 0,07% | -0,21% | 98% | 101%
Class E | 0,00% | 0,00% | 0,00% | 100% | 100% |  |  |  |  |  | 0,51% | 0,60% | 0,55% | 81% | 100%
Overall | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,35% | 0,43% | 0,27% | 87% | 101% | 0,22% | 0,21% | 0,13% | 91% | 101%
Class D | 0,00% | 0,00% | 0,00% | 100% | 102% | 0,06% | 0,10% | 0,01% | 94% | 99% | 0,05% | 0,15% | 0,13% | 98% | 99%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 14: SubCE1-2.1.4 (JVET-L0081)
A 128x128 CTU is forced to be split into four 64x64 CUs
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,00% | 0,00% | 100% | 100% | 2,66% | 2,32% | 2,21% | 73% | 104% |  |  |  |  | 
Class A2 | 0,00% | 0,00% | 0,00% | 100% | 100% | 2,87% | 2,27% | 2,04% | 82% | 102% |  |  |  |  | 
Class B | 0,00% | 0,00% | 0,00% | 100% | 100% | 1,25% | 0,96% | 0,88% | 84% | 101% | 0,85% | 0,49% | 0,30% | 89% | 99%
Class C | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,10% | 0,14% | 0,04% | 94% | 100% | 0,10% | -0,13% | 0,11% | 97% | 99%
Class E | 0,00% | 0,00% | 0,00% | 100% | 100% |  |  |  |  |  | 2,26% | 2,35% | 1,78% | 73% | 100%
Overall | 0,00% | 0,00% | 0,00% | 100% | 100% | 1,55% | 1,28% | 1,15% | 84% | 102% | 0,95% | 0,75% | 0,60% | 87% | 100%
Class D | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,06% | 0,13% | -0,04% | 93% | 98% | 0,05% | 0,46% | -0,10% | 97% | 99%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 15: Overall results: Separate trees
(For SubCE3-3.1.1 and SubCE3-3.1.2 there are updated results available in JVET-L0424 that harmonizes the timings. For AI it is around (100%,100%).)
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
SubCE1-1.1.1 | 0,00% | 0,01% | 0,02% | 99% | 98% | 0,02% | 0,08% | 0,01% | 99% | 98% | 0,03% | -0,10% | -0,24% | 98% | 98%
SubCE1-1.2.1 | 0,06% | 0,10% | 0,12% | 98% | 101% | 0,00% | 0,02% | 0,07% | 100% | 99% | -0,10% | -0,02% | -0,27% | 99% | 97%
SubCE1-1.2.2 | 0,07% | 0,09% | 0,11% | 100% | 100% | 0,12% | 0,17% | 0,18% | 100% | 100% | 0,20% | 0,10% | 0,07% | 99% | 96%
SubCE1-1.3.1 | 0,00% | 0,00% | 0,00% | 93% | 92% | -0,02% | -0,01% | -0,06% | 93% | 88% | -0,08% | -0,14% | -0,21% | 93% | 88%
SubCE2-2.1.1 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,26% | 0,35% | 0,25% | 95% | 104% | 0,30% | 0,23% | 0,20% | 98% | 101%
SubCE2-2.1.2 | 0,00% | 0,00% | 0,00% | 100% | 101% | 0,15% | 0,20% | 0,14% | 94% | 101% | 0,06% | 0,09% | -0,15% | 98% | 100%
SubCE2-2.1.3 | 0,00% | 0,00% | 0,00% | 100% | 100% | 0,35% | 0,43% | 0,27% | 87% | 101% | 0,22% | 0,21% | 0,13% | 91% | 101%
SubCE2-2.1.4 | 0,00% | 0,00% | 0,00% | 100% | 100% | 1,55% | 1,28% | 1,15% | 84% | 102% | 0,95% | 0,75% | 0,60% | 87% | 100%
SubCE3-3.1.1 | -0,01% | -0,07% | -0,06% | 111% | 111% | -0,13% | -2,32% | -1,87% | 122% | 101% | -0,03% | -0,55% | -0,63% | 115% | 102%
SubCE3-3.1.1-syn |  |  |  |  |  | -0,69% | -3,24% | -3,04% | 140% | 102% | -0.47% | -4.18% | -5.06% | 126% | 82%
SubCE3-3.1.2 | 0,02% | -0,05% | -0,05% | 89% | 90% | -0,11% | -2,25% | -1,89% | 129% | 104% | 0,00% | -0,66% | -0,89% | 110% | 97%
SubCE3-3.1.2-syn |  |  |  |  |  | -0,69% | -3,24% | -3,04% | 144% | 100% | -0.47% | -4.09% | -5.07% | 116% | 80%
SubCE3-3.2.1 | -0,01% | -0,07% | -0,06% | 85% | 92% | 0,01% | 0,01% | 0,02% | 94% | 95% | -0,04% | -0,06% | -0,08% | 82% | 89%
SubCE3-3.2.1-syn |  |  |  |  |  | 0.00% | 0.01% | 0.01% | 88% | 92% | 0.01% | 0.01% | 0.03% | 77% | 80%
SubCE3-3.2.2 | 0,02% | -0,05% | -0,05% | 85% | 91% | -0,11% | -2,24% | -1,87% | 106% | 90% | 0,04% | -0,43% | -0,78% | 92% | 89%
SubCE3-3.2.2-syn |  |  |  |  |  | -0.69% | -3.24% | -3.04% | 124% | 96% | -0.47% | -4.10% | -5.06% | 114% | 82%

## Slide 16: SubCE1-3.1.1 (JVET-L0424)
Results are reported for CTC and for synthetic sequences that were also provided by the proponents.
The use of separate trees is dependent on a threshold signaled in the SPS.
If the number of luma samples exceeds the threshold, then separate trees are available.
If the number of samples is below the threshold, separate trees are not available.
In the remaining case there is a flag in the bit-stream that controls if separate trees are available or not.
Separate tree support at CU level for intra-coded CUs in inter slices is tested. No modifications for intra slices.
Updated timings in JVET-L0424: AI: (102%, 102%) RA: (122%, 102%) LP: (109%, 101%)
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,04% | -0,01% | 109% | 112% | -0,49% | -4,00% | -2,10% | 127% | 101% |  |  |  |  | 
Class A2 | -0,01% | -0,03% | -0,12% | 121% | 122% | -0,06% | -2,14% | -0,90% | 108% | 91% |  |  |  |  | 
Class B | 0,01% | 0,00% | 0,08% | 121% | 116% | -0,13% | -2,26% | -2,64% | 123% | 102% | 0,01% | -0,64% | -1,12% | 114% | 98%
Class C | -0,03% | -0,23% | -0,05% | 112% | 113% | 0,07% | -1,26% | -1,45% | 129% | 106% | 0,06% | -0,36% | -0,32% | 115% | 103%
Class E | -0,01% | -0,12% | -0,29% | 88% | 92% |  |  |  |  |  | -0,22% | -0,65% | -0,22% | 117% | 108%
Overall | -0,01% | -0,07% | -0,06% | 111% | 111% | -0,13% | -2,32% | -1,87% | 122% | 101% | -0,03% | -0,55% | -0,63% | 115% | 102%
Class D | 0,02% | 0,02% | -0,26% | 107% | 109% | 0,15% | -0,71% | -0,15% | 117% | 100% | 0,05% | -0,32% | -0,24% | 109% | 99%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 17: SubCE1-3.1.1-syn (JVET-L0424)
Results are reported for CTC and for synthetic sequences that were also provided by the proponents.
The use of separate trees is dependent on a threshold signaled in the SPS.
If the number of luma samples exceeds the threshold, then separate trees are available.
If the number of samples is below the threshold, separate trees are not available.
In the remaining case there is a flag in the bit-stream that controls if separate trees are available or not.
Separate tree support at CU level for intra-coded CUs in inter slices is tested. No modifications for intra slices.
Updated timings in JVET-L0424: RA: (144%, 105%) LP: (152%, 104%)
 | Random Access Main 10 (Synthetic) |  |  |  |  | Low delay B Main10 (Synthetic) |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0,81% | -2,92% | -1,55% | 143% | 107% |  |  |  |  | 
Class A2 | -0,49% | -1,91% | -1,00% | 147% | 102% |  |  |  |  | 
Class B | -0,75% | -4,24% | -5,16% | 134% | 100% | -0.47% | -4.18% | -5.06% | 126% | 82%
Class C |  |  |  |  |  |  |  |  |  | 
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0,69% | -3,24% | -3,04% | 140% | 102% | -0.47% | -4.18% | -5.06% | 126% | 82%
Class D |  |  |  |  |  |  |  |  |  | 
Class F (optional) |  |  |  |  |  |  |  |  |  | 

## Slide 18: SubCE1-3.1.2 (JVET-L0424)
Results are reported for CTC and for synthetic sequences that were also provided by the proponents.
The use of separate trees is dependent on a threshold signaled in the SPS.
If the number of luma samples exceeds the threshold, then separate trees are available.
If the number of samples is below the threshold, separate trees are not available.
In the remaining case there is a flag in the bit-stream that controls if separate trees are available or not.
CU level separate trees for intra-coded CUs in inter slices combined with support for both separate and shared trees in intra slices is tested, i.e. both slice types have separate tree signaling at CU level.
Updated timings in JVET-L0424: AI: (100%, 98%) RA: (122%, 102%) LP: (108%, 101%)
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,02% | 0,11% | 0,00% | 83% | 86% | -0,49% | -3,91% | -2,28% | 130% | 103% |  |  |  |  | 
Class A2 | 0,00% | -0,06% | -0,14% | 107% | 106% | -0,03% | -2,11% | -0,92% | 129% | 105% |  |  |  |  | 
Class B | 0,03% | 0,05% | 0,10% | 87% | 86% | -0,11% | -2,16% | -2,62% | 125% | 102% | 0,01% | -0,77% | -1,31% | 106% | 88%
Class C | 0,02% | -0,22% | -0,07% | 90% | 91% | 0,09% | -1,23% | -1,41% | 134% | 109% | 0,07% | -0,38% | -0,63% | 115% | 103%
Class E | 0,01% | -0,14% | -0,24% | 81% | 83% |  |  |  |  |  | -0,12% | -0,85% | -0,54% | 111% | 105%
Overall | 0,02% | -0,05% | -0,05% | 89% | 90% | -0,11% | -2,25% | -1,89% | 129% | 104% | 0,00% | -0,66% | -0,89% | 110% | 97%
Class D | 0,14% | 0,22% | -0,14% | 102% | 103% | 0,17% | -0,52% | -0,19% | 126% | 107% | 0,05% | 0,27% | -0,20% | 105% | 96%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 19: SubCE1-3.1.2-syn (JVET-L0424)
Results are reported for CTC and for synthetic sequences that were also provided by the proponents.
The use of separate trees is dependent on a threshold signaled in the SPS.
If the number of luma samples exceeds the threshold, then separate trees are available.
If the number of samples is below the threshold, separate trees are not available.
In the remaining case there is a flag in the bit-stream that controls if separate trees are available or not.
CU level separate trees for intra-coded CUs in inter slices combined with support for both separate and shared trees in intra slices is tested, i.e. both slice types have separate tree signaling at CU level.
Updated timings in JVET-L0424: RA: (144%, 103%) LP: (150%, 101%)
 | Random Access Main 10 (Synthetic) |  |  |  |  | Low delay B Main10 (Synthetic) |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0,81% | -2,89% | -1,54% | 140% | 103% |  |  |  |  | 
Class A2 | -0,49% | -1,89% | -1,00% | 157% | 104% |  |  |  |  | 
Class B | -0,75% | -4,27% | -5,17% | 139% | 96% | -0.47% | -4.09% | -5.07% | 116% | 80%
Class C |  |  |  |  |  |  |  |  |  | 
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0,69% | -3,24% | -3,04% | 144% | 100% | -0.47% | -4.09% | -5.07% | 116% | 80%
Class D |  |  |  |  |  |  |  |  |  | 
Class F (optional) |  |  |  |  |  |  |  |  |  | 

## Slide 20: SubCE1-3.2.1 (JVET-L0424)
Results are reported for CTC and for synthetic sequences that were also provided by the proponents.
The use of separate trees is dependent on a threshold signaled in the SPS.
If the number of luma samples exceeds the threshold, then separate trees are available.
If the number of samples is below the threshold, separate trees are not available.
In the remaining case there is a flag in the bit-stream that controls if separate trees are available or not.
Separate tree support at CTU level for intra-coded CTUs in inter slices. No modifications for intra slices.
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,04% | -0,01% | 79% | 91% | 0,00% | 0,09% | 0,00% | 92% | 92% |  |  |  |  | 
Class A2 | -0,01% | -0,03% | -0,12% | 97% | 103% | 0,02% | -0,12% | 0,03% | 91% | 91% |  |  |  |  | 
Class B | 0,01% | 0,00% | 0,08% | 89% | 95% | 0,01% | 0,03% | 0,07% | 88% | 92% | 0,00% | 0,02% | 0,14% | 79% | 87%
Class C | -0,03% | -0,23% | -0,05% | 86% | 91% | 0,02% | 0,03% | -0,03% | 107% | 106% | 0,00% | 0,03% | -0,14% | 85% | 90%
Class E | -0,01% | -0,12% | -0,29% | 75% | 82% |  |  |  |  |  | -0,17% | -0,32% | -0,37% | 84% | 89%
Overall | -0,01% | -0,07% | -0,06% | 85% | 92% | 0,01% | 0,01% | 0,02% | 94% | 95% | -0,04% | -0,06% | -0,08% | 82% | 89%
Class D | 0,02% | 0,02% | -0,26% | 83% | 88% | 0,02% | -0,26% | 0,04% | 97% | 98% | 0,02% | 0,00% | -0,73% | 86% | 88%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 21: SubCE1-3.2.1-syn (JVET-L0424)
Results are reported for CTC and for synthetic sequences that were also provided by the proponents.
The use of separate trees is dependent on a threshold signaled in the SPS.
If the number of luma samples exceeds the threshold, then separate trees are available.
If the number of samples is below the threshold, separate trees are not available.
In the remaining case there is a flag in the bit-stream that controls if separate trees are available or not.
Separate tree support at CTU level for intra-coded CTUs in inter slices. No modifications for intra slices.
 | Random Access Main 10 (Synthetic) |  |  |  |  | Low delay B Main10 (Synthetic) |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | -0.01% | 88% | 95% |  |  |  |  | 
Class A2 | 0.00% | 0.02% | 0.02% | 92% | 94% |  |  |  |  | 
Class B | -0.02% | -0.01% | 0.01% | 87% | 90% | 0.01% | 0.01% | 0.03% | 77% | 80%
Class C |  |  |  |  |  |  |  |  |  | 
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.00% | 0.01% | 0.01% | 88% | 92% | 0.01% | 0.01% | 0.03% | 77% | 80%
Class D |  |  |  |  |  |  |  |  |  | 
Class F (optional) |  |  |  |  |  |  |  |  |  | 

## Slide 22: SubCE1-3.2.2 (JVET-L0424)
Results are reported for CTC and for synthetic sequences that were also provided by the proponents.
The use of separate trees is dependent on a threshold signaled in the SPS.
If the number of luma samples exceeds the threshold, then separate trees are available.
If the number of samples is below the threshold, separate trees are not available.
In the remaining case there is a flag in the bit-stream that controls if separate trees are available or not.
For all slices a flag is sent at CTU level. If the flag is true, then the CTU is coded as intra CTU using separate trees. If the flag is false, then CU level separate trees are used at CU-level for intra-coded CUs in inter slices and for intra slices both, shared and separate trees are supported (cf. SubCE1-3.1.2).
 | All Intra Main10 |  |  |  |  | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0,02% | 0,11% | 0,00% | 84% | 93% | -0,48% | -3,89% | -2,25% | 104% | 90% |  |  |  |  | 
Class A2 | 0,00% | -0,06% | -0,14% | 95% | 104% | -0,02% | -2,09% | -0,91% | 101% | 87% |  |  |  |  | 
Class B | 0,04% | 0,05% | 0,10% | 83% | 89% | -0,10% | -2,15% | -2,60% | 112% | 93% | 0,03% | -0,53% | -1,34% | 89% | 87%
Class C | 0,02% | -0,22% | -0,07% | 89% | 92% | 0,10% | -1,23% | -1,40% | 105% | 90% | 0,08% | -0,35% | -0,57% | 99% | 90%
Class E | 0,01% | -0,14% | -0,24% | 74% | 82% |  |  |  |  |  | 0,01% | -0,39% | -0,10% | 88% | 89%
Overall | 0,02% | -0,05% | -0,05% | 85% | 91% | -0,11% | -2,24% | -1,87% | 106% | 90% | 0,04% | -0,43% | -0,78% | 92% | 89%
Class D | 0,14% | 0,22% | -0,14% | 85% | 89% | 0,17% | -0,52% | -0,18% | 103% | 89% | 0,05% | 0,28% | -0,19% | 93% | 86%
Class F (optional) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 23: SubCE1-3.2.2-syn (JVET-L0424)
Results are reported for CTC and for synthetic sequences that were also provided by the proponents.
The use of separate trees is dependent on a threshold signaled in the SPS.
If the number of luma samples exceeds the threshold, then separate trees are available.
If the number of samples is below the threshold, separate trees are not available.
In the remaining case there is a flag in the bit-stream that controls if separate trees are available or not.
For all slices a flag is sent at CTU level. If the flag is true, then the CTU is coded as intra CTU using separate trees. If the flag is false, then CU level separate trees are used at CU-level for intra-coded CUs in inter slices and for intra slices both, shared and separate trees are supported (cf. SubCE1-3.1.2).
 | Random Access Main 10 (Synthetic) |  |  |  |  | Low delay B Main10 (Synthetic) |  |  |  | 
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.81% | -2.89% | -1.53% | 121% | 100% |  |  |  |  | 
Class A2 | -0.48% | -1.89% | -1.00% | 129% | 98% |  |  |  |  | 
Class B | -0.74% | -4.27% | -5.16% | 122% | 93% | -0.47% | -4.10% | -5.06% | 114% | 82%
Class C |  |  |  |  |  |  |  |  |  | 
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.69% | -3.24% | -3.04% | 124% | 96% | -0.47% | -4.10% | -5.06% | 114% | 82%
Class D |  |  |  |  |  |  |  |  |  | 
Class F (optional) |  |  |  |  |  |  |  |  |  |