## Slide 1
(JVET-L0060) CE6-related: Unified matrix for transform
Kiho Choi
Samsung Electronics

## Slide 2: Motivation
Identified issues in VTM MTS
  The total number of kernel matrix for transform
  10-bit representation of coefficient
Proposed method
  Using a 64x64 matrix only that consists of coefficients based on 8-bit representation for all transform kernels
  COT structure with a 64x64 matrix based on 8-bit representation
 | MTS usage | Supported block size for Luma | Coefficient representation
DCT2 | X | 4x4 - 64x64 | 10-bit
DCT8 | O | 4x4 - 32x32 | 10-bit
DST7 | O | 4x4 - 32x32 | 10-bit

## Slide 3: Proposed method
DCT2 can be derived by sampling a subset of coefficients in the matrix as follows:
    DCT2_NxN[l, k] = matrix_64x64[l, 2(6- log2N) *k]
    where DCT2_NxN[l, k] represents the l-th element of the k-th basis vector of DCT-2 for NxN matrix and N is a size of matrix from 64 to 2.
DCT8 can be derived by sampling a subset of coefficients in the matrix as follows:
    DCT8_NxN[l, k] = matrix_64x64[l, 2(6- log2N) *k +2(5 - log2N)]
    where DCT8_NxN[l, k] represents the l-th element of the k-th basis vector of DCT-8 for NxN matrix and N is a size of matrix from 32 to 4.
DST7 can be derived by sampling a subset of coefficients in the matrix as follows:
    DST7_NxN[l, k] = (-1)^k * DCT8_NxN[N – l - 1, k]
    DST7_NxN[l, k] = (-1)^k * matrix_64x64[N – l - 1, 2(6- log2N) *k +2(5 - log2N)]
    where DST7_NxN[l, k] represents the l-th element of the k-th basis vector of DST-7 for NxN matrix and N is a size of matrix from 32 to 4.

## Slide 4: Proposed unified 64x64 matrix

## Slide 5: Memory usage
Transform size | # of elements | VTM |  |  | Proposal |  | 
 | (size^2) | # of kernels | Bits per elements | Bits amounts | # of kernels | Bits per elements | Bits amounts
2 | 4 | 1 | 10 | 40 | 0 | 8 | 0
4 | 16 | 2 | 10 | 320 | 0 | 8 | 0
8 | 64 | 2 | 10 | 1280 | 0 | 8 | 0
16 | 256 | 2 | 10 | 5120 | 0 | 8 | 0
32 | 1024 | 3 | 10 | 20480 | 0 | 8 | 0
64 | 16384 | 1 | 10 | 163840 | 1 | 8 | 131072
Total [bits] |  | 201320 |  |  | 131072 |  | 
 |  | (~25 KBytes) |  |  | (~ 16 Kbytes ) |  | 
Over VTM [%] |  | 100 |  |  | 65 |  | 
Memory usage of proposed method is reduced to 65% of VTM’s memory usage for transform

## Slide 6: Testing result
Testing result on VTM
  AI: 0.0% / -0.1% / -0.1% (E: 99%, D:100%)
  RA: 0.1% / 0.1% / 0.1% (E: 101%, D:100%)
  LD: 0.1% / 0.0% / -0.1% (E: 102%, D:100%)
Testing result on BMS
  AI: 0.0% / 0.0% / 0.0% (E: 101%, D:100%)
  RA: 0.1% / 0.1% / 0.0% (E: 101%, D:100%)
  LD: -0.1% / 0.0% / -0.4 % (E: 103%, D:100%)

## Slide 7
Thank you