## Slide 1: CE1-related: Minimum block size restriction (JVET-L0137)
Seung-Hwan Kim (seunghwan3.kim @lge.com)

## Slide 2: Summary
Propose minimum block size restriction method
  To reduce the data throughput overhead of VVC
  Method 1: chroma 2x2 block is restricted in I slice, and luma 4x4 and chroma 2x2 are restricted in P and B slice
  Method 2: luma 4x4 block and chroma 2x2 block are restricted in all slices
Experimental results
Crosscheck : MediaTek(JVET-L0482)
CTC sequences | Method 1 |  |  | Method 2 |  | 
 | Y BD-rate | EncT | DecT | Y BD-rate | EncT | DecT
AI | 0.00% | 99% | 99% | 0.46% | 88% | 95%
RA | 0.22% | 97% | 100% | 0.36% | 95% | 96%
LDB | 0.18% | 96% | 100% | 0.29% | 96% | 101%
HD and UHD sequences | Method 1 |  |  | Method 2 |  | 
 | Y BD-rate | EncT | DecT | Y BD-rate | EncT | DecT
AI | 0.00% | 99% | 100% | 0.19% | 90% | 95%
RA | 0.09% | 98% | 102% | 0.17% | 96% | 98%
LDB | 0.10% | 96% | 99% | 0.12% | 96% | 100%

## Slide 3: Introduction
A CU block in VTM2 can be split into 4x4 luma and 2x2 chroma block
  It become the cause of data throughput overhead in the hardware architecture
  Especially when the input video has high resolution (i.e., UHD video or 8K 360° video)
This contribution suggests minimum block size restriction methods to reduce the worst case complexity in aspects of memory bandwidth and throughput in hardware architecture

## Slide 4: Proposed method
Method 1: chroma 2x2 block is restricted in I slice, and luma 4x4 and chroma 2x2 are restricted in P and B slice
  The minimum chroma block size is restricted to 2x4 and 4x2 in intra slice
  The minimum luma block size is restricted to 8x4 and 4x8 for the inter slices to restrict the chroma block size over 2x2
Method 2: luma 4x4 block and chroma 2x2 block are restricted in all slices.

## Slide 5: Proposed method
The block restriction information can be inserted into high level syntax
Example : inserted into SPS(sequence parameter set)
seq_parameter_set_rbsp( ) { | Descriptor
… | 
log2_min_cu_pixel_num_luma_minus4 | ue(v)
log2_min_cu_pixel_num_chroma_minus2 | ue(v)
… | 
} | 
log2_min_cu_pixel_num_luma_minus4 : the pixel number of minimum luma CU block
log2_min_cu_pixel_num_chroma_minus2 : the pixel number of minimum chroma CU block

## Slide 6: Experimental results
Tool-on test in VTM2.0.1
The results of Test 1 ( chroma 2x2 block is restricted in I slice / luma 4x4 and chroma 2x2 are restricted in P and B slice )
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.08% | 0.04% | 99% | 100%
Class A2 | 0.00% | 0.06% | 0.07% | 99% | 100%
Class B | 0.00% | 0.04% | 0.12% | 100% | 99%
Class C | -0.01% | 0.32% | 0.57% | 98% | 99%
Class E | -0.01% | 0.00% | -0.05% | 100% | 100%
Overall | 0.00% | 0.11% | 0.17% | 99% | 99%
Class D | 0.01% | 0.64% | 0.66% | 98% | 96%
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.07% | 0.16% | 100% | 102%
Class A2 | 0.07% | 0.27% | 0.21% | 98% | 101%
Class B | 0.14% | 0.29% | 0.20% | 97% | 101%
Class C | 0.57% | 0.98% | 1.23% | 95% | 97%
Class E |  |  |  |  | 
Overall | 0.22% | 0.42% | 0.47% | 97% | 100%
Class D | 0.94% | 1.48% | 2.13% | 93% | 91%
 | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | 0.10% | 0.06% | 0.37% | 96% | 99%
Class C | 0.55% | 0.77% | 0.68% | 95% | 100%
Class E | -0.18% | 0.28% | -0.90% | 99% | 101%
Overall | 0.18% | 0.36% | 0.15% | 96% | 100%
Class D | 0.98% | 1.76% | 1.35% | 91% | 96%

## Slide 7: Experimental results
Tool-on test in VTM2.0.1
The results of Test 2 ( luma 4x4 block and chroma 2x2 block are restricted in all slices )
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.10% | 0.01% | -0.07% | 92% | 97%
Class A2 | 0.12% | 0.04% | -0.01% | 90% | 97%
Class B | 0.30% | 0.15% | 0.17% | 88% | 93%
Class C | 1.08% | 0.71% | 0.90% | 85% | 91%
Class E | 0.63% | 0.12% | 0.25% | 91% | 99%
Overall | 0.46% | 0.23% | 0.28% | 88% | 95%
Class D | 1.42% | 1.27% | 1.03% | 83% | 90%
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.06% | 0.03% | 0.17% | 98% | 99%
Class A2 | 0.15% | 0.02% | 0.04% | 94% | 97%
Class B | 0.25% | 0.34% | 0.44% | 95% | 97%
Class C | 0.89% | 1.20% | 1.37% | 94% | 92%
Class E |  |  |  |  | 
Overall | 0.36% | 0.45% | 0.55% | 95% | 96%
Class D | 1.42% | 1.58% | 2.16% | 91% | 88%
 | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | 0.12% | -0.03% | 0.26% | 96% | 100%
Class C | 0.66% | 0.73% | 0.89% | 94% | 100%
Class E | 0.08% | -0.52% | -0.24% | 98% | 102%
Overall | 0.29% | 0.10% | 0.34% | 96% | 101%
Class D | 1.07% | 1.74% | 1.88% | 91% | 99%

## Slide 8: Experimental results
Tool-on test in VTM2.0.1
The results of Test 1 with HD and UHD sequences only
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.08% | 0.04% | 99% | 100%
Class A2 | 0.00% | 0.06% | 0.07% | 99% | 100%
Class B | 0.00% | 0.04% | 0.12% | 100% | 99%
Overall | 0.00% | 0.06% | 0.08% | 99% | 100%
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.07% | 0.16% | 100% | 102%
Class A2 | 0.07% | 0.27% | 0.21% | 98% | 101%
Class B | 0.14% | 0.29% | 0.20% | 97% | 101%
Overall | 0.09% | 0.22% | 0.19% | 98% | 102%
 | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | 0.10% | 0.06% | 0.37% | 96% | 99%
Overall | 0.10% | 0.06% | 0.37% | 96% | 99%

## Slide 9: Experimental results
Tool-on test in VTM2.0.1
The results of Test 2 with HD and UHD sequences only
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.10% | 0.01% | -0.07% | 92% | 97%
Class A2 | 0.12% | 0.04% | -0.01% | 90% | 97%
Class B | 0.30% | 0.15% | 0.17% | 88% | 93%
Overall | 0.19% | 0.08% | 0.06% | 90% | 95%
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.06% | 0.03% | 0.17% | 98% | 99%
Class A2 | 0.15% | 0.02% | 0.04% | 94% | 97%
Class B | 0.25% | 0.34% | 0.44% | 95% | 97%
Overall | 0.17% | 0.17% | 0.26% | 96% | 98%
 | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | 0.12% | -0.03% | 0.26% | 96% | 100%
Overall | 0.12% | -0.03% | 0.26% | 96% | 100%

## Slide 10: Conclusion
The proposed minimum block size restriction method can reduce the maximum data throughput significantly in the worst cases with reasonable coding loss in the high resolution videos