## Slide 1: JVET-L0159 Non-CE8: Block vector predictor for IBC
Junghak Nam, Jaehyun Lim, Seung Hwan Kim

## Slide 2: Summary
Proposed schemes
  Two candidates (-2*width, 0) and (0, -2*height) are introduced to IBC instead of zero candidates
Simulation results (over VTM-2.0.1 + CPR)
  -0.11%, -0.61%, -1.18% for CTC, ClassF, and SCC in AI
  -0.11%, -0.49%, -0.79% for CTC, ClassF, and SCC in RA
  0.10%, -0.23%, -0.26% for CTC, ClassF, and SCC in LD

## Slide 3: Background
Construction of AMVP and merge candidate lists
  Fill candidates from spatial and temporal neighboring blocks
  If a number of candidate is NOT maximum number, Add zero candidates
Zero candidates are always invalid for CPR
 |  |  |  | Curr CU |  |  | 
Invalid region
BV
Valid region

## Slide 4: Proposed method
Two alternative candidates, (-2*width, 0) and (0, -2*height), are proposed
  Candidate position: before zero candidates
  For AMVP, if target reference is equal to current picture, add proposed candidates
  For merge, if current picture exists in the reference list, add proposed candidates
 |  |  |  | Cur |  |  | 
Valid region
Invalid region
(-2W, 0)
(0, -2H)

## Slide 5: Experimental results
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC | -0.19% | -0.19% | -0.11% | 108% | 104% | -0.11% | -0.10% | -0.06% | 102% | 100%
ClassF | -14.80% | -14.73% | -14.72% | 122% | 105% | -0.49% | -0.49% | -0.47% | 101% | 100%
SCC | -36.07% | -36.03% | -36.37% | 107% | 97% | -0.79% | -0.74% | -0.63% | 99% | 100%
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 + CPR |  |  |  | 
Test # | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC | 0.13% | 0.37% | -0.09% | 116% | 107% | 0.10% | 0.15% | 0.00% | 101% | 99%
ClassF | -8.61% | -8.47% | -9.25% | 118% | 108% | -0.23% | -0.08% | 0.19% | 101% | 99%
SCC | -25.58% | -26.76% | -26.77% | 113% | 103% | -0.26% | -0.42% | -0.36% | 101% | 99%
< Random access >
< Low delay B >
 | Over VTM-2.0.1 |  |  |  |  | Over VTM-2.0.1 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC | -0.49% | -0.26% | -0.21% | 156% | 104% | -0.11% | -0.06% | -0.06% | 105% | 100%
ClassF | -18.03% | -17.84% | -17.80% | 189% | 98% | -0.61% | -0.29% | -0.29% | 103% | 99%
SCC | -53.35% | -52.37% | -52.70% | 149% | 85% | -1.18% | -0.87% | -0.88% | 100% | 100%
< All intra >

## Slide 6: Conclusion
In this proposal, two alternative candidates are proposed to improve coding efficiency for CPR
  (-2*width, 0) and (0, -2*height)
  Apply both AMVP and merge mode
It is recommended to further study on CE
Thanks to Tencent for crosscheck (JVET-L0472)