## Slide 1: JVET-L0208 – Technicolor Multiple shapes prediction unit
July 2018

## Slide 2: Reminder CE10.3.1.b test
Built on top of CE10.3.1.b test
  New merge mode with triangular Prediction Unit
  Uni-prediction candidate list
  Adaptive weighting on the edges

## Slide 3: Simplified weigthing process
  CE10.3.1b: Shifting and clipping done for each uni-prediction
  Proposed: Shifting and clipping done after weighting as in bi-prediction

## Slide 4: Simplified weigthing process on top of CE10.3.1b
  Over CE10.3.1.b (VTM2.0.1)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1(vtm.cfg) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.04% | -0.04% | 101% | 97%
Class A2 | 0.01% | -0.15% | 0.08% | 94% | 96%
Class B | -0.02% | 0.04% | -0.06% | 96% | 103%
Class C | -0.03% | -0.03% | -0.03% | 102% | 114%
Class E |  |  |  |  | 
Overall | -0.02% | -0.02% | -0.02% | 98% | 103%
Class D | -0.02% | -0.03% | 0.02% | 103% | 112%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1(vtm.cfg) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.06% | -0.24% | 96% | 102%
Class C | -0.05% | 0.00% | -0.34% | 100% | 103%
Class E | -0.04% | -0.13% | -0.36% | 96% | 98%
Overall | -0.04% | -0.06% | -0.31% | 98% | 102%
Class D | 0.01% | -0.50% | -0.63% | 103% | 103%

## Slide 5: Multiple shapes prediction unit
Proposed shapes
  Syntax is modified to separate shape coding and motion vector predictors

## Slide 6: Results of simplified weighting process + multiple shapes
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1(vtm.cfg) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.47% | -0.58% | -0.90% | 141% | 105%
Class A2 | -0.72% | -1.14% | -1.07% | 167% | 100%
Class B | -0.60% | -0.78% | -0.85% | 160% | 105%
Class C | -1.25% | -1.43% | -1.70% | 165% | 106%
Class E |  |  |  |  | 
Overall | -0.77% | -0.98% | -1.13% | 159% | 104%
Class D | -0.74% | -0.88% | -0.94% | 176% | 105%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1(vtm.cfg) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -1.16% | -1.53% | -1.79% | 156% | 89%
Class C | -1.72% | -2.26% | -2.33% | 165% | 104%
Class E | -2.48% | -2.89% | -2.76% | 170% | 92%
Overall | -1.68% | -2.12% | -2.21% | 162% | 95%
Class D | -1.52% | -1.89% | -2.14% | 174% | 110%