## Slide 1: Non-CE1: Relation Between QT/BT/TT Split Constraint Syntax Elements
Han Gao
Semih Esenlik, Jianle Chen, Biao Wang, Anand Meher Kotra

## Slide 2: Motivation
Current VVC Text has 3 Split Constraint Syntax Elements: MinQtSizeY, MaxMttDepth and MaxBtSizeY
  MinQtSizeY is indicated by log2_min_qt_size_minus2 and in the SPS*
  MaxMttDepth is indicated by max_mtt_hierarchy_depth in the SPS*
  MaxBtSizeY is indicated by log2_diff_ctu_max_bt_size in the Slice Header.
  Additonally, MinCbSizeY is hardcoded as 4, MaxTtSizeY is hardcoded.
Problem
  The relations between the split constraint syntax elements is not defined, which will lead to the incomplete partitioning of picture
*separate signaled based on slice type

## Slide 3: Problem Statement
Problem 1:
  Assuming MinQtSizeY > MaxBtSizeY
   No possible to split the block completely to MinCbSizeY
Problem 2:
  Assuming MaxMttDepth < log2(MinQtSizeY) – log2 (MinCbSizY)
   No possible to split the block completely to MinCbSizeY
Problem 3:
  Assuming MaxMttDepth = 0 and MaxBtSizeY > 0
  Section 7.4.5.3 tells you to do BT split
  Section 6.4.1 tells you that BT split is not allowed.

## Slide 4: Proposed Method
Solution for problem 1:
  Signaling the MinCbSizeY indicator by log2_min_luma_coding_block_size_minus2
  Signaling the MinQtSizeY indicator relative to MinCbSizeY by log2_diff_min_qt_min_cb*
  Signaling the MaxBtSizeY indicator relative to MinQtSizeY by log2_diff_max_bt_min_qt*
Solution for problem 2:
  Signaling the MaxMttDepth indicator relative to the difference of MinQtSizeY and MinCbSizeY by diff_max_mtt_hierarchy_depth*
Solution for problem 3:
  MaxBtSizeY is signalled if MaxMttDepth is not equal to 0
  Otherwise the value of MaxBtSizeY is inferred to be equal to MinCbSizeY.
* Can be signaled separately by slice type

## Slide 5: Syntax Modifications

## Slide 6: Summary
In the solution following aspects are proposed:
  Signaling the indicator of minimum coding block size in SPS
  Signaling the indicator of MinQtSizeY relative to MinCbSizeY
  Signaling the indicator of MaxBtSizeY relative to MinQtSizeY
  Signaling the indicator of MaxMttDepth relative to the difference of MinQtSizeY and MinCbSizeY
  Signaling MaxBtSizeY (or MaxTtSizeY) only if MaxMttDepth is not equal to 0
It is asserted that the ambiguities in the VVC draft [1] are resolved with the proposed changes. It is proposed to be included in next VVC draft text.