## Slide 1: CE4-related: Improvement of BIMVP (JVET-L0301)
Byeongdoo Choi Frank Bossen
Andrew Segall

## Slide 2: What happen with linear motion
mvd1 is almost same as mvd0.
The nearest reference frame is selected, in most cases.
Bi-prediction is more frequently selected than uni-prediction.
In most cases, mvp_flag1 is identical to mvp_flag1, because paired MVs are selected.

## Slide 3: Syntax design and derivation process
In BIMVP mode,
mvd1 is inferred to be equal to mvd0
ref0 and ref1 are inferred to be equal to 0
inter_pred_idc is inferred to be equal to 3
mvp1 is inferred to be equal to mvp0
bimvp_flag is signaled before inter_pred_idc, because this mode is a kind of skip mode for AMVP.

## Slide 4: Test results (vs VTM 2.0.1) - RA

## Slide 5: Conclusion
The proposed method shows 0.69% gain with 104% encoding complexity on average, and with increasing gains for higher resolution sequences.
The cross-check is reported by LG.
We propose the adoption in the next VVC.