## Slide 1: CE15-related: Palette mode when dual-tree is enabled (JVET-L0308)
J. Ye, X. Li, S. Liu, and X. Xu
2018/10

## Slide 2: Introduction
In CE15.2/CE15.1, when dual tree is enabled, separate palette coding for luma and chroma is used.
  Luma has its own palette table, index map, and palette predictor list
  Chroma has its own palette table, index map, and palette predictor list
The proposed method provide an alternative way to do palette coding when dual tree is enabled

## Slide 3: Proposed method (1)
When dual tree is enable for I slice:
  Luma: apply palette coding, one flag to indicate whether palette mode is chosen or not
  Chroma: not apply palette coding, other available mode are tested.
When dual tree is disabled for P/B slice, the same to CE15.2/CE15.1

## Slide 4: Proposed method (2)
When dual tree is enable for I slice:
  Luma: apply palette coding, one flag to indicate whether palette mode is chosen or not
  Chroma: checking the collocated luma block
    If it is all coded by palette mode, the current chroma block can be palette mode
    If it is not all coded by palette mode, the current block cannot apply palette coding, other available mode are tested.
When dual tree is disabled for P/B slice, the same to CE15.2/CE15.1

## Slide 5: Performance (1)
Method 1: anchor 1 is VTM 2.0.1, anchor 2 is CE15.2

## Slide 6: Performance (2)
Method 2: anchor 1 is VTM 2.0.1, anchor 2 is CE15.2

## Slide 7: Conclusion
The proposed methods, especially method 2 shows 0.1%/0.15% luma coding gain on class F and class SCC with AI configuration.
It is suggested to further study in CE
Thanks Sharp for crosscheck!

## Slide 8: Thank you!