## Slide 1: JVET-K0353 CE6-related: MTS using DST-4 and transposed DCT-2
Yongbing Lin, Jianhua Zheng, Quanhe Yu,
Na Zhang(HiSilicon), Ce Zhu (UESTC)

## Slide 2: Introduction
MTS in VTM 2
  use DST-7 and DCT-8 as transform cores
Proposal
  use DST-4 and transposed DCT-2
Benefits of proposal
  reusing circuit implementation of existing DCT-2 transform
  reusing transform coefficients of existing DCT-2 transform
  enabling partial butterfly implementation for the proposed transpose of DCT-2

## Slide 3: Derivation of the proposed 4-point transforms from 8-point DCT-2 transform
Figure. Derivation of the proposed 4-point transforms (i.e., A and B) from 8-point DCT-2 transform

## Slide 4: Test results for the proposal
Test condition |  | BDR-Y | BDR-U | BDR-V | EncTime | DecTime
CTC | AI | 0.06% | 0.06% | 0.10% | 97% | 99%
 | RA | 0.06% | 0.22% | 0.11% | 99% | 100%
 | LB | -0.04% | 0.13% | -0.09% | 99% | 99%
 | LP | 0.03% | 0.23% | 0.37% | 99% | 100%
CTC + interMTS | RA | 0.12% | 0.12% | 0.11% | 98% | 99%
 | LB | 0.00% | 0.12% | 0.34% | 98% | 99%
CTC + interMTS + signaling_align | RA | 0.12% | 0.13% | 0.13% | 98% | 96%
 | LB | -0.01% | 0.04% | 0.18% | 98% | 99%
Coding performance compared to BMS-2.0.1 with VTM configuration

## Slide 5: Conclusion
MTS using DST-4 and transposed DCT-2
  Reuse of hardware design
  No additional storage for the proposed transforms
  Fast algorithm - partial butterfly implementation
  Negligible performance change to VTM2
Recommend to inclusion of the proposals in next test model

## Slide 6
Thank You
www.hisilicon.com