## Slide 1: CE1-related: Context modeling of CU split modes
Yin Zhao, Haitao Yang, and Jianle Chen
Huawei Technologies
JVET-L0361

## Slide 2: Introduction
In Ljubljana meeting, JVET-K0134 and JVET-K0362 proposed to modify the context modeling of cu split modes to increase coding efficiency
This contribution combines the methods in the two proposals to achieve coding gain
In VVC, cu split modes are coded with four flags
  qt_split_cu_flag (5 ctx based on qt depth of four neighbors)
  mtt_split_cu_flag (3 ctx based on qt depth and mtt depth of two neighbors)
  mtt_split_cu_horizontal_flag (3 ctx based on width and height of the current node)
  mtt_split_cu_binary_flag (6 ctx based on split direction and width and height of the current node)
JVET-L0361

## Slide 3: Proposed method
qt_split_cu_flag (JVET-K0362)
  four neighbors context to two neighbors, conditioned on the depth of the current CU
  ctxInc = ( (qtDepthC < qtDepthA) ? 1:0 ) + ( (qtDepthC < qtDepthL) ? 1:0 )
  ctxInc += qtDepthC < 2? 0 : 3
mtt_split_cu_flag (JVET-K0134)
  Based on width and height of the current node and those of two neighbors
  Further based on the coding tree type, three ctx for chroma tree (new aspect)
  ctxInc = ( (widthC > widthA)? 1:0 ) + ( (heightC > heightL)? 1:0 )
  ctxInc += isChromaTree? 9 : ( sizeC > th2? 0 : (sizeC > th1? 3 : 6) )
  where sizeC = widthC * heightC,
  th2 = 1024 / 512 / 256 and th1 = 128 / 64 / 64 for maxBTSize 128 / 64 / 32 (and below)
mtt_split_cu_horizontal_flag (no change)
mtt_split_cu_binary_flag (reduce from 6 to 1, JVET-K0134, JVET-K0362)
JVET-L0361

## Slide 4: Simulation results
JVET-L0361
Num Ctx | VVC2 | Test 1 (w/o separate ctx for chroma tree) |  |  | Test 2 (w/ separate ctx for chroma tree) |  | 
qt_split_cu_flag | 5 | 6 |  |  | 6 |  | 
mtt_split_cu_flag | 3 | 9 |  |  | 12 |  | 
mtt_split_cu_vertical_flag | 3 | 3 |  |  | 3 |  | 
mtt_split_cu_binary_flag | 6 | 1 |  |  | 1 |  | 
Total | 17 | 19 |  |  | 22 |  | 
BD-rate |  | PSNR-Y | PSNR-U | PSNR-V | PSNR-Y | PSNR-U | PSNR-V
AI |  | 0.00% | -0.30% | -0.31% | -0.06% | -0.28% | -0.30%
RA |  | -0.10% | -0.16% | -0.11% | -0.12% | -0.23% | -0.25%
LD |  | -0.16% | -0.46% | -0.36% | -0.20% | -0.16% | -0.45%

## Slide 5: Conclusion
The proposed method (test 2) brings -0.1%, -0.1%, -0.2% gain in AI, RA, LB.
It is recommended to include the proposed context modeling method in VVC.
Thanks Samsung for cross-checking the proposal (JVET-L0487).
JVET-L0361