## Slide 1: JVET-L0409 Filtering Coefficients Simplification for filtering complexity reduction in ALF
S. Sethuraman
Ittiam Systems
5 October 2018

## Slide 2: Reducing multiplications in ALF
BMS-ALF requires 13 multiplications per output sample due to the non-separable 2-D filtering
  Summarized as a key complexity aspect for ALF at the last meeting
    ALF multiplication is 10-bit x 10-bit
JVET-K0215 proposed to make 6 of these coefficients to be powers of 2 so as to replace 6 multiplications with simple left shifts
  Less than half the multiplications are removed
  Rest of the coefficients are re-computed after making the 6 coefficients a power of 2 on the encoding side
  Proposed coefficient coding changes

## Slide 3: Proposed method
Normatively constrain the absolute value of all the coefficients other than the center coefficient (which is derived implicitly on the decoding side) such that it has only 2 or 3 bits set (to 1)
  For the constraint of N bits set (to 1), N shifts and (N-1) additions only are required
No changes to how the coefficients are signaled
Non-normative method of constraining:
  Identify the position in the coefficient value for a filter where the Nth set bit occurs from the most-significant bit position
  Add a value equal to (1 << (N-1)) to the coefficient value to create a rounded value
  Constrain the original coefficient value and the rounded coefficient value to retain only the first N set bits.
  Select the option with the least difference from the original value from these 2 options as the final normative coefficient value to be signaled in the bitstream

## Slide 4: Benefits of the proposed method
Replacing 10-bit x 10-bit with just 2 (or 3) shifts and 1 (or 2) adds
  In hardware, substantial reduction in gate-count for ALF
  In software, lower latency vector shift instructions instead of longer latency multiplication instructions
    Better throughput due to decreased register pressure
  SIMD processing is not affected
    Most processors support a variable shift for each lane of a vector instruction
    For a 4x4 block, the center coefficient multiplication for the 16-output samples can be done in a vector form

## Slide 5: Combination with JVET-K0215
6 coefficients use 1 shift as in JVET-K0215
6 coefficients use the N set-bits constraint
Experiments were done with and without re-computation of coefficients
No changes to how the coefficients are signaled

## Slide 6: Test Conditions
The tests were performed in VTM-1.0 with the ALF from CE2.4.1.4 from last meeting (that uses adaptive max 7x7 luma filter with 4x4 block size for classification) by enabling ALF on top of VTM-1.0
Fixed filters were disabled except in the anchor
  Fixed filters were found to offer ~-0.05% BDRATE gain
  Test (a): N = 3
  Test (b): N = 2
  Test (c): N = 1
  Test (d): N =3 in combination with JVET-K0215 w/o coefficient re-computation
  Test (e): N=3 in combination with JVET-K0215 with coefficient re-computation

## Slide 7: Test Results
Observations:
  Minimal BDRATE drop with the proposed normative constraint for N=3 and 2
  Even without re-computation on the encoding side, the ALF BD-RATE gains are mostly retained for N=3 and 2
  Going to 1-shift requires re-computations to restrict the BDRATE drops
Test-cases | ALF Tool-ON BD-RATE in VTM-1.0 for RA |  | 
 | Y | U | V
CE2.4.1.4 from last meeting | -4.98% | -3.14% | -2.66%
(a) 3-shifts for 12-coeffs | -4.84% | -3.08% | -2.50%
(b) 2-shifts for 12 coeffs | -4.72% | -2.96% | -2.42%
(c) 1 shift for 12 coeffs | -4.27% | -2.70% | -2.26%
(d) 6 with 1-shift + 6 with 3-shifts (without re-computation between groups) | -4.59% | -2.83% | -2.16%
(e) 6 with 1-shift + 6 with 3-shifts (with re-computation between groups) | -4.83% | -3.05% | -2.50%

## Slide 8: Partial Test Results in VTM2.0.1
Partial results in VTM2.0.1 show slightly lower BDRATE drops, as ALF in VTM2.0.1 does not have fixed filter and has a lower tool-OFF drop (4.66% against the 4.98% shows earlier in VTM1.0)
It was also confirmed that the 3-shift and 2-shift drops stay low even when the constraint is applied post-merge on the encoding side
 | 2-shift - Over VTM 2.0.1 in RA |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.28% | 0.04% | 0.04% | 102% | 99%
Class A2 |  |  |  |  | 
Class B | 0.32% | -0.01% | -0.07% | 103% | 101%
Class C | 0.17% | 0.07% | 0.07% | 103% | 104%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.12% | 0.08% | -0.13% | 102% | 105%

## Slide 9: Conclusions
Proposed normative constraint on the number of set bits in the absolute value of the filter coefficients of all filter sets signaled (except the derived center coefficient)
Reduces the need for ALF to just 1 multiplication per output sample and 12*N shifts and 12*(N-1) additions
The BDRATE impact is minimal and a method exists without any need to re-compute the coefficients on the encoding side
It is requested that this method be studied in an ALF related core experiment.