## Slide 1: JVET-L0427 CE15-related: Separate Palette Coding for Luma and Chroma components
Roman Chernyak
Sergey Ikonin
Jianle Chen

## Slide 2: Background
VVC2.x includes Dual Tree for I slices
CE15 Palettes’ Implementations are harmonized with Dual Tree in following way:
Sps.DT?
Tree type
Single CU
Luma CU
Chroma CU
Single CU
Dual
Single
Yes
No
Palette Coding Y
Palette Coding Cb-Cr
Palette Coding Y
Palette Coding Cb-Cr
Palette Coding Y-Cb-Cr

## Slide 3: Proposal
Unify Palette Coding for both Dual Tree on and off cases:
Sps.DT?
Tree type
Single CU
Luma CU
Chroma CU
Single CU
Dual
Single
Yes
No
Palette Coding Y
Palette Coding Cb-Cr
Palette Coding Y
Palette Coding Cb-Cr
Palette Coding Y
Palette Coding Cb-Cr

## Slide 4: Simulation results
Test2(Y & Cb-Cr)
Test1 (Y-Cb-Cr)
Anchor:
VTM2.0.1 no DT
Test1:
Anchor + Palette SCC (CE15.2)
Test2 (Proposed):
Test1 + Y and Cb-Cr always independent

## Slide 5: Conclusion
Proposed Palette Coding design unifies Single CU processing for Dual Tree on and off cases
Proposed Palette Coding design demonstrates 9.0% / 3.9% / 1.3% (AI / RA / LDB) on class TGM and 4.0% / 3.3% / 2.4% (AI / RA / LDB) on class F of Luma BD-rate saving on top of CE15.2 (HEVC SCC Palette Coding), if Dual Tree is disabled.