## Slide 1: On Picture Order Count Signaling for VVC (JVET-L0449)
S. Deshpande, B. Choi (Sharp)

## Slide 2: Organization
Proposal
Conclusion

## Slide 3: Proposal (1/5)
VVC WD does not include picture order count (POC) signaling and decoding
POC is used by various coding tools
POC signaling and decoding is proposed with following characteristics:
  Signaling of POC LSB values for all picture types
  Signaling and operation of POC without signaling of MSB values
  Optional signaling of MSB value information for one or more pictures
Proposal is based on HEVC POC signaling and decoding and has a few modifications described in next slides.

## Slide 4: Proposal (2/5)
Proposal aspect 1: Signal POC LSB for all pictures (including IDR pictures)

## Slide 5: Proposal (3/5)
Proposal aspect 2: Signaling in SPS that allows a “LSB only” mode which results in simpler PicOrderCntMSB derivation:
  Signal log2_max_pic_order_cnt_msb_cycle equal to 0
  No extra signaling at slice level (i.e. only signal slice_pic_order_cnt_lsb in slice).
  Simplifies POC derivation: Does not need derivation of PicOrderCntMsb
The variable PicOrderCntMsb of the current picture is derived as follows:
If the current picture is an IRAP picture with NoRaslOutputFlag equal to 1 IDR picture or if log2_max_pic_order_cnt_msb_cycle for the active SPS for this slice is present and is equal to 0 the variable PicOrderCntMsb is set equal to 0.

## Slide 6: Proposal (4/5)
Proposal aspect 3: Optional signaling of MSB information for one or more pictures
    Provides robustness
    Provides future extensibility
The variable PicOrderCntMsb of the current picture is derived as follows:
If the current picture is an IRAP picture with NoRaslOutputFlag equal to 1 IDR picture or if log2_max_pic_order_cnt_msb_cycle for the active SPS for this slice is present and is equal to 0 the variable PicOrderCntMsb is set equal to 0.
Otherwise if the slice of the current picture has slice_pic_order_cnt_msb_cycle signalled, the variable PicOrderCntMSB is set equal to slice_pic_order_cnt_msb_cycle multiplied by MaxPicOrderCntLsb.
Otherwise, PicOrderCntMsb is derived as follows:
<HEVC POC derivation…>

## Slide 7: Proposal (5/5)
Proposal aspect 4: PicOrderCntVal range is modified
If slice_pic_order_cnt_msb_signaling_present is equal to 1 the value of PicOrderCntVal shall be in the range of −2( log2_max_pic_order_cnt_lsb_minus4 + log2_max_pic_order_cnt_msb_cycle + 3 ) to 2(log2_max_pic_order_cnt_lsb_minus4 + log2_max_pic_order_cnt_msb_cycle + 3 ) − 1, inclusive
Otherwise the value of PicOrderCntVal shall be in the range of −231 to 231 − 1, inclusive.

## Slide 8: Conclusion
POC signaling and decoding is proposed for VVC
It is proposed to adopt the proposed syntax and semantics in VVC WD

## Slide 9
Thank You