## Slide 1: JVET-L0515: CE3-related: Non-zero reference lines padding method on the top-line of CTU
Po-Han Lin, Chi-Chang Kuo, Ching-Chieh Lin and Chun-Lung Lin
Macau, CN
Oct. 2018

## Slide 2: Outline
Introduction
Proposed method
Results
Conclusions

## Slide 3: Introduction
MRL (Multiple Reference Line) is able to use extended reference line to predict a CU.
MRL was adopted in this meeting (CE3-1.1.4, MPM only, disabling on the top-line of CTU).

## Slide 4: Introduction
Due to the hardware issue, MRL is disabled when the current CU is on the top-line of a CTU.
But the restriction reduce the gain of MRL by 0.06% in AI and 0.02% in RA.

## Slide 5: Proposed method
Use the reference line 0 to pad the reference line 1 and 3.
With the proposed padding method, parsing of the MRL syntax no more depends on the CU position. And it could retrieve some gains.
There are two padding methods proposed in this contribution.

## Slide 6: Proposed syntax modification

## Slide 7: Proposed method 1 for line 1
Pad the samples in the segment D, E and F from the sample right below it.
Fa = (X1 + L1 + 1) >> 1

## Slide 8: Proposed method 1 for line 3
Pad the samples in the segment D, E and F from the sample right below it.
Fb = (3 * X3 + L3 + 2) >> 2 Fc = (X3 + L3 + 1) >> 1 Fd = (X3 + 3 * L3 + 2) >> 2

## Slide 9: Proposed method 2
For method 2, it’s similar to method 1, but pads the sample in segment C from segment B.
This method is simpler than the method 1 because there is no interpolation filter applied.

## Slide 10: Results of method 1
Compared to VTM2.0.1
  0.44% / 0.19% gain in AI / RA condition

## Slide 11: Results over CE3-1.1.4
Compared to the adopted MRL
  0.04% / 0.01% gain in AI / RA condition
  Same complexity as the adopted method

## Slide 12: Results of method 2
Compared to VTM2.0.1
  0.44% / 0.21% gain in AI / RA condition
  The results are not cross-checked yet

## Slide 13: Results over CE3-1.1.4
Compared to the adopted MRL
  0.04% / 0.02% gain in AI / RA condition
  Same complexity as the adopted method
  Thanks Huawei for cross-checking

## Slide 14: Conclusions
A simple modification which makes the parsing process be unified and retrieves some gain.
Method 2 results over the CE3-1.1.4
  0.04% gain in AI condition with the same complexity.
It is suggested to adopt method 2 in the VTM software based on CE3-1.1.4.

## Slide 15: Thank you!