## Slide 1
JVET-M0085
CE6-related: Fast algorithm for DCT-4/DST-4 as alternative transforms for MTS
T. Toma, K. Abe Panasonic Corporation
M. Ikeda, T. Tsukuba SONY Corporation

## Slide 2
2
Introduction
A new set of MTS transforms, i.e. replacing DST-7 / DCT-8 by DST-4 / DCT-4, was proposed in JVET-L0262 in Macao meeting.
It was discussed if fast algorithm is also available for non-DCT-2 transform basis functions that are used in MTS.
 This contribution proposes fast algorithm for DST-4 and DCT-4
Also, additional combination tests are conducted mainly to see how DST-4 / DCT-4 work with maximum MTS size restricted to 16..
  Combination with CE6-3.2b and CE6-3.2c
  Combination with CE6-4.1d
  Combination with JVET-M0046

## Slide 3
3
Proposed fast algorithm for DST-4 and DCT-4
Utilize symmetric property of matrix coefficients
Same algorithm can be used for both DST-4 and DCT-4
  DST-4 can be derived by flipping and sign changing of DCT-4

## Slide 4
4
Fast algorithm in detail
DCT4 matrix can be decomposed using the following 2x2 matrices.
Type 1
Type 2
Type 3
Type 4
Type 5
Type 6
Type 7
Type 8
The number of multiplications is reduced from 4 to 3 as follows
[Ex. Type 1]
3 times
4 times

## Slide 5
Number of multiplication and adding operations
The number of multiplication operations is reduced to 75%
 | Matrix multiplication |  | Fast algorithm | 
N-points | Mul | Add | Mul | Add
4 | 16 | 12 | 12 | 14
8 | 64 | 56 | 48 | 60
16 | 256 | 240 | 192 | 248
32 | 1024 | 992 | 768 | 1008

## Slide 6
6
Simulation results 1
Anchor: modified VTM 3.0 replacing MTS transform to DST-4 / DCT-4
Test: anchor with the fast algorithm
DecT is reduced by 5 % in AI, 2 % in RA and 3 % in LDB
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 96% | 92%
Class A2 | 0.00% | 0.00% | 0.00% | 97% | 94%
Class B | 0.00% | 0.00% | 0.00% | 97% | 97%
Class C | 0.00% | 0.00% | 0.00% | 98% | 95%
Class E | 0.00% | 0.00% | 0.00% | 97% | 95%
Overall | 0.00% | 0.00% | 0.00% | 97% | 95%
Class D | 0.00% | 0.00% | 0.00% | 97% | 91%
Class F | 0.00% | 0.00% | 0.00% | 97% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 98% | 97%
Class C | 0.00% | 0.00% | 0.00% | 98% | 97%
Class E | 0.00% | 0.00% | 0.00% | 99% | 97%
Overall | 0.00% | 0.00% | 0.00% | 98% | 97%
Class D | 0.00% | 0.00% | 0.00% | 98% | 97%
Class F | 0.00% | 0.00% | 0.00% | 99% | 102%
 | Random access Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 98% | 98%
Class A2 | 0.00% | 0.00% | 0.00% | 98% | 99%
Class B | 0.00% | 0.00% | 0.00% | 98% | 99%
Class C | 0.00% | 0.00% | 0.00% | 98% | 97%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 98% | 98%
Class D | 0.00% | 0.00% | 0.00% | 98% | 96%
Class F | 0.00% | 0.00% | 0.00% | 98% | 99%

## Slide 7
7
Simulation results 2
Anchor: VTM 3.0
Test: modified VTM 3.0 with the fast algorithm
DecT is reduced by 7 % in AI, 2 % in RA and 3 % in LDB
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.66% | 0.55% | 0.71% | 101% | 89%
Class A2 | 0.50% | 0.23% | 0.21% | 99% | 91%
Class B | 0.33% | -0.01% | 0.04% | 100% | 95%
Class C | -0.24% | -0.27% | -0.32% | 100% | 95%
Class E | -0.01% | -0.24% | -0.17% | 100% | 94%
Overall | 0.23% | 0.03% | 0.07% | 100% | 93%
Class D | -0.27% | -0.42% | -0.35% | 100% | 95%
Class F | -0.12% | -0.21% | -0.04% | 100% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.06% | -0.02% | -0.49% | 100% | 97%
Class C | -0.29% | -0.45% | -0.09% | 100% | 97%
Class E | -0.14% | -0.19% | -1.03% | 100% | 99%
Overall | -0.16% | -0.20% | -0.49% | 100% | 97%
Class D | -0.29% | -0.68% | -1.02% | 100% | 97%
Class F | -0.39% | -0.13% | -0.78% | 100% | 101%
 | Random access Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.32% | 0.27% | 0.44% | 101% | 98%
Class A2 | 0.29% | 0.24% | 0.16% | 100% | 99%
Class B | 0.18% | 0.14% | 0.01% | 100% | 98%
Class C | -0.18% | 0.01% | -0.05% | 100% | 98%
Class E |  |  |  |  | 
Overall | 0.13% | 0.15% | 0.11% | 100% | 98%
Class D | -0.24% | -0.48% | -0.36% | 100% | 96%
Class F | -0.03% | -0.12% | -0.05% | 100% | 99%

## Slide 8
8
Summary of additional combination tests (with inter MTS enabled)
It is generally observed that BD-rate loss of DST-4 / DCT-4 approach compared to DST-7 / DCT-8 gets smaller if the maximum MTS size is restricted to 16.
  [Example]
  No MTS size restriction: 0.23%, 0.13% loss for AI, RA, and 0.16% gain for LDB
  With CE6-3.2.b (max. MTS size: 16): 0.11%, 0.07% loss for AI, RA, and 0.18% gain for LDB
 |  | AI, w/ InterMTS |  |  | RA, w/ InterMTS |  |  | LDB, w/ InterMTS |  | 
No. | Test | Y | U | V | Y | U | V | Y | U | V
1 | DST4 / DCT4: w/o combination | 0.23% | 0.03% | 0.07% | 0.13% | 0.15% | 0.11% | -0.16% | -0.20% | -0.49%
2 | With CE6-3.2.b (max. MTS = 16) - Nx32 and 32xN for N < 32 | 0.44% | 0.37% | 0.42% | 0.35% | 0.40% | 0.34% | 0.08% | 0.01% | -0.54%
3 | With CE6-3.2.c (max. MTS = 16) - Nx16 and 16xN for N <= 16 | 0.64% | 0.54% | 0.57% | 0.49% | 0.43% | 0.48% | 0.20% | 0.12% | -0.22%
4 | With CE6-4.1.d + max MTS = 16 - SBT with max MTS =16 |  |  |  | 0.13% | 0.27% | 0.49% | -0.46% | -0.82% | -0.23%
5 | With JVET-M0046 | 0.31% | 0.04% | 0.12% | 0.18% | 0.07% | 0.16% | -0.17% | -0.18% | -0.33%
6 | CE6-3.2b | 0.33% | 0.40% | 0.38% | 0.28% | 0.30% | 0.38% | 0.26% | 0.20% | -0.01%
7 | CE6-3.2c | 0.55% | 0.62% | 0.63% | 0.45% | 0.43% | 0.43% | 0.35% | 0.15% | -0.10%
8 | CE6-4.1d |  |  |  | -0.29% | -0.14% | 0.03% | -0.47% | -0.64% | -0.06%
9 | JVET-M0046 (Test 5) | 0.12% | 0.05% | 0.02% | 0.05% | 0.01% | 0.10% | 0.14% | 0.10% | -0.05%

## Slide 9
9
Conclusion
This contribution proposes fast algorithm for DST-4 and DCT-4.
By utilizing symmetric property of matrix coefficient, the number of multiplication operations is reduced to 75 % as compared to matrix multiplication.
Several combination tests with DST-4 / DCT-4 method related to restricting maximum MTS size to 16 are conducted.
It is generally observed that BD-rate loss of DST-4 / DCT-4 approach compared to DST-7 / DCT-8 gets smaller if the maximum MTS size is restricted.

## Slide 10
10
Thank Technicolor for cross-checking this proposal !