## Slide 1: CE2-related: Alignment of affine control-point motion vector and subblock motion vector
Han Huang, Wei-Jung Chien, Vadim Seregin, Hongtao Wang and Marta Karczewicz (Qualcomm)

## Slide 2: Summary
Proposed:
  Use subblock MVs for affine inheritance
    To remove affine CPMV buffer and unification of inherit from current CTU row and above CTU row.
  Use subblock MVs as the control-point MV of affine motion
    Alignment.
  Directly predict subblock MVs in affine merge instead of affine CPMVs
    Remove additional rounding process to reduce complexity.
Test results:
  -0.01%, 0.01%, 0.00% in RA, 0.03%, -0.17%, -0.03% in LDB
  Combined with CE2 test 2.4.7: 0.01%, 0.00%, 0.01% in RA, 0.06%, 0.22%, -0.08%

## Slide 3: Introduction
Affine inheritance in VTM-3.0
  From current and left CTU: use CPMVs of the neighboring affine coded block
  From above and above left CTU: use the bottom-left and bottom-right subblock MVs of the neighboring affine coded block
  Need additional buffer to store the affine CPMVs
Affine inherited merge candidate in VTM-3.0
  Derive the predicted CPMVs (1st rounding process is applied for each CPMV)
  Derive the subblock MVs from predicted CPMVs (2nd rounding process is applied for each subblock)

## Slide 4: Proposed
Inheritance from current and left CTU: Use the subblock MVs locate at the bottom-right, bottom-middle and right-middle.
Inheritance from above and above left CTU: use the bottom-right and bottom-middle subblock MVs
Features:
  Division in affine inheritance process remains power of 2 (W/2 and H/2), implemented by right shifting.
  Only need to be stored for affine inheritance from left and above left CTU. Total number of MVs: (128/8+1)*2=34

## Slide 5: Proposed
Use subblock MVs as the control-point MV of affine motion

## Slide 6: Proposed
Directly predict subblock MVs in inherited affine merge candidate
  Remove one unnecessary rounding process for predicting affine CPMVs

## Slide 7: Test results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.03% | -0.02% | 98% | 98%
Class A2 | -0.02% | 0.04% | 0.09% | 99% | 96%
Class B | -0.02% | 0.03% | -0.05% | 96% | 95%
Class C | 0.01% | 0.00% | 0.02% | 96% | 93%
Class E |  |  |  |  | 
Overall | -0.01% | 0.01% | 0.00% | 97% | 95%
Class D | 0.02% | -0.02% | 0.11% | 96% | 92%
Class F | -0.04% | -0.03% | 0.02% | 95% | 94%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | -0.47% | -0.04% | 99% | 96%
Class C | 0.03% | 0.20% | 0.15% | 100% | 100%
Class E | 0.04% | -0.15% | -0.28% | 96% | 91%
Overall | 0.03% | -0.17% | -0.03% | 98% | 96%
Class D | 0.03% | 0.01% | 0.12% | 97% | 93%
Class F | -0.13% | -0.18% | 0.07% | 97% | 93%

## Slide 8: Combined test with CE2: test 2.4.7
Affine inheritance only available if width >=16 and height >= 16
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.06% | -0.01% | 98% | 98%
Class A2 | 0.03% | -0.02% | 0.12% | 97% | 98%
Class B | 0.00% | 0.01% | -0.09% | 95% | 94%
Class C | 0.01% | 0.04% | 0.08% | 95% | 94%
Class E |  |  |  |  | 
Overall | 0.01% | 0.00% | 0.01% | 96% | 96%
Class D | 0.06% | 0.04% | 0.03% | 96% | 92%
Class F (optional) | -0.02% | -0.03% | -0.02% | 95% | 93%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.04% | -0.05% | -0.10% | 99% | 97%
Class C | 0.08% | 0.39% | 0.33% | 96% | 90%
Class E | 0.07% | 0.44% | -0.60% | 95% | 90%
Overall | 0.06% | 0.22% | -0.08% | 97% | 93%
Class D | 0.07% | 0.40% | -0.26% | 96% | 92%
Class F (optional) | -0.04% | 0.20% | 0.35% | 97% | 93%
  Total number of additional MVs to be stored:
  (128/16+1)*2=18