## Slide 1: CE7-related QP offset based on block size
JVET-M0114

## Slide 2: Contents
  Introduction: local QP control should be fine-grained
  Expected correlation between QP and block size
  Proposal: QP offset based on block size
  QP offset table and block size-based index
  CTU-level control

## Slide 3: Local QP control: should be fine-grained
Large Quantization Groups = same QP for mixed simple-complex content
  QP too high for fine texture: loss of detail, ripple/mosquito from neighboring contours, lower quality compared to neighboring uniform areas
  QP too low for high-contrast contours: high bit cost
Small Quantization Groups = better adaptation
  Sweet point 16x16 or even 8x8
  But delta-QP bit cost can be too high (e.g. for low bitrate B-pictures)
Example problems with large QGs

## Slide 4: Correlation between block size and QP
  QP mostly based of luma variance  higher on high-contrast areas (contours)
    Also higher on complex motion
  Block size often smaller to follow contours (or motion)
  Probably higher QPs on smaller blocks
Example picture split
Example variance-based QP (yellow = higher)

## Slide 5: Implicit QP offset based on block size
  Table of QP offsets, e.g. at picture level
  Index related to block size (derived from split depth or subdiv)
  Implicit offset for CU = offset_table[size_index]
    But does not impact QP prediction (not the same granularity)
  Can enable larger QGs with finer QPs (better adaptation with lower bit cost)
Example implicit offset based on split depth
Example implicit offset based on subdiv

## Slide 6: Offset table and size index
Table: small blocks first; repeat last
  Offset clearly variable for small blocks, but gets stable for large blocks
Index: maxSubdiv - cbSubdiv
  maxSubdiv = 2*(log2_ctu_size_minus2 - log2_min_luma_coding_block_size_minus2)
PPS syntax example
Size index | 0 | 1 | 2 | 3 | 4 | ≥5
QP offset | 3 | 2 | 1 | 0 | -2 | -3
QP-offset table example
num_block_size_qp_offset | ue(v)
for (i=0; i < num_block_size_qp_offset; i++) { | 
pps_block_size_qp_offset[ i ] | se(v)
} | 

## Slide 7: CTU-level control
Encoders can have specific rules for specific areas (logos, banners, skin, grass)
  Could need disabling or varying implicit QP offset at sub-picture level
  Classic technique = control QP dynamic range with a scaling factor.
  Can add a scaling index in CTU (fewer bits for often-used values)
Scale index | 0 | 1 | 2 | 3 | 4 | …
QP-offset scale | 1 | 0 | 1/2 | 1/4 | 3/4 | etc
Scaling table example (can be hard-coded in the standard)

## Slide 8
Thank you