## Slide 1: JVET-M0138 Intra Reference Sample Deblocking
Zhi Zhang
Ericsson
2019-01-08
Notes: 2018-02-21
1

## Slide 2: Blocking artifacts along intra prediction direction
Blocking artifacts in previously decoded CUs introduce discontinuity of reference samples
The current [1 2 1] / 4 low pass filter or 4-tap interpolation filter can not eliminate the discontinuity
Example:
FoodMarket
VTM3.0, RA, QP34
ALF disabled
512x512 block
at position (1408, 384)
POC11, slice QP is 43
64x64 CU
Intra mode 34

## Slide 3: Proposed method Intra Reference Sample Deblocking (IRSDB)
IRSDB is applied to:
  Luma block
  Block width is larger than or equal to 32
  Block height is larger than or equal to 32
  Unfiltered intra reference samples
IRSDB fitlered reference sample is further filtered by:
    [1 2 1] / 4 low-pass filter
    or 4-tap interpolation filter
Intra prediction mode | Reference sample filter
HOR_IDX or VER_IDX | IRSDB
2, DIA_IDX or VDIA_IDX | IRSDB + [1 2 1] / 4 low-pass filter
Remaining directional modes | IRSDB + 4-tap interpolation filter

## Slide 4: Checkpoint positions potential positions to apply IRSDB
A set of checkpoint positions are defined that includes the following positions:
  at the sample to the top-left of the current block
  at each position (X, Y) above the current block that X is divisible by 32
  at each position (X, Y) to the left of the current block that is Y divisible by 32
Current CU size | Max number of checkpoint positions
32x32 | 3
32x64 | 5
64x32 | 5
64x64 | 7

## Slide 5: IRSDB filtering decision Checkpoint position at top-left of current CU
At least the 32 reference samples for the block P to the left of the current block have been decoded
At least 32 reference samples for the block Q above the current block have been decoded
abs(p0,i-q0,i) < 2.5*tc
abs(p0,i-p3,i-p4,i+p7,i) + abs(q0,i-q3,i-q4,i+q7,i) < (3 * beta / 32)
where tc and beta value depends on the slice QP similar to HEVC deblocking.
where i = multiple reference line index

## Slide 6: IRSDB filtering decision Checkpoint positions at above of current CU
The block P to the above of the current block have been decoded and block P width >= 32
The block Q to the above of the current block have been decoded and block Q width >= 32
Block Q and block P belong to two different PUs or Tus
abs(p0,i-q0,i) < 2.5*tc
abs(p0,i-p3,i-p4,i+p7,i) + abs(q0,i-q3,i-q4,i+q7,i) < (3 * beta / 32)

## Slide 7: IRSDB filtering decision Checkpoint positions at left of current CU
The block P to the left of the current block have been decoded and block P height >= 32
The block Q to the left of the current block have been decoded and block Q height >=32
Block Q and block P belong to two different PUs or TUs
abs(p0,i-q0,i) < 2.5*tc
abs(p0,i-p3,i-p4,i+p7,i) + abs(q0,i-q3,i-q4,i+q7,i) < (3 * beta / 32)

## Slide 8: IRSDB filtering operation For reference sample pn,i and qn,i
where,
  where,
    n ranges from 0 to 6
    i = multiple reference line index

## Slide 9: IRSDB filtering operation For reference samples at top-left of current CU
where,
  where,
    m ranges from -i to i
    i = multiple reference line index

## Slide 10: Subjective result 1
Anchor:
      FoodMarket RA coding QP 34, ALF disabled
      POC 11, slice QP 43
      512x512 block at position (1408, 384)
IRSDB:
      Prediction mode same as anchor
      Coding tree same as anchor
      Applying IRSDB on a 64x64 CU

## Slide 11: Subjective result 2
Anchor:
      RedKayak RA coding QP 39
      ALF enabled
      POC 20, slice QP 46
      1152x696 block at position (768, 384)
Encode / decode the entire video sequence with IRSDB enabled

## Slide 12: Objective result
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,06% | -0,06% | 0,01% | 100% | 101%
Class A2 | -0,01% | 0,01% | 0,00% | 100% | 102%
Class B | 0,00% | -0,06% | -0,02% | 100% | 99%
Class C | 0,00% | -0,02% | -0,07% | 100% | 99%
Class E | -0,03% | -0,03% | 0,05% | 100% | 100%
Overall | -0,02% | -0,03% | -0,01% | 100% | 100%
Class D | 0,01% | -0,02% | -0,01% | 100% | 99%
Class F | 0,01% | 0,03% | 0,19% | 100% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,03% | -0,06% | -0,01% | 101% | 98%
Class A2 | -0,02% | -0,03% | 0,12% | 100% | 98%
Class B | -0,02% | 0,07% | -0,12% | 99% | 98%
Class C | -0,01% | 0,05% | 0,01% | 100% | 102%
Class E |  |  |  |  | 
Overall | -0,02% | 0,02% | -0,02% | 100% | 99%
Class D | 0,01% | 0,02% | 0,02% | 100% | 98%
Class F | -0,03% | 0,02% | -0,07% | 100% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,01% | -0,18% | -0,46% | 101% | 98%
Class C | 0,03% | 0,13% | 0,21% | 100% | 100%
Class E | -0,02% | 0,88% | -0,32% | 99% | 98%
Overall | 0,01% | 0,19% | -0,20% | 100% | 99%
Class D | 0,05% | -0,07% | 0,19% | 100% | 98%
Class F | -0,12% | -0,23% | 0,08% | 100% | 102%

## Slide 13
Notes: 2018-02-21
13