## Slide 1: JVET-M0148 Non-CE9: Simplifications to DMVR search pattern and interpolation for refinement
S. Sethuraman
Ittiam Systems
9 January 2019

## Slide 2: Search Pattern in CE9.2
Square shaped integer distance refinement positions with refinement range of +/-2
  Best timing for hardware requires evaluating 25 costs concurrently
    Higher gate count need
    For cost-functions such as SAD/PR-MR-SAD, 2x5 line buffers of interpolated samples are sufficient; full block need not be buffered
  2-stage evaluation requires evaluating 5 in stage-1 and 8 more in stage-2
    Increased timing and more internal memory as all interpolated samples used for refinement need to be stored
  Software implementations perform only 9 cost evaluations in 4-stages to keep average decoding time increase low
A new search pattern that allows concurrent evaluation of all costs at a reduced gate count and with minimal impact on coding efficiency is desired

## Slide 3: Proposed Search Pattern
Rhombus shaped integer distance refinement positions with refinement range of +/-2 is proposed
  25 positions in refinement range is reduced to 13 positions
A 2-stage normative cost evaluation process is proposed to keep average decoding time on software implementations close to the 9 costs evaluated earlier
  Requires 5 costs to be evaluated in each stage
An extension to the 2-D parametric error surface for sub-pixel offset estimation based on integer distance costs called 1-D parametric error surface is introduced
  First stage positions get 2-D error surface; the 4 diagonal positions get 1-D diagonal error surface based sub-pixel offsets.
0
1
2

## Slide 4: Benefits of the proposed search pattern
Cost at a given integer distance refinement position is evaluated on alternate rows of the block
  (1 + 5 + 1) = 7 even row positions access one set of alternate interpolated rows
  (3 + 3) = 6 odd row positions access the other set of alternate interpolated rows
  Thus, for every new interpolated row of samples produced, either 7 costs or 6 costs need to be updated at a row-level
    Implies that just 7 row-level cost evaluation units suffice
Concurrent evaluation of all positions with just 7 row-level cost evaluation units
  Offers the best timing at a significantly reduced gate count
As mentioned earlier, for cost functions such as SAD or PR-MR-SAD, a row-level pipeline can be set up with minimal (200 sample) internal memory requirement for 2 x 5 rows of interpolated samples
1-D parametric error surface allows coding efficiency drop due to reduced refinement positions to be kept minimal

## Slide 5: CE9.2.1 – Study items
Primary requirement for DMVR from last meeting
  Restrict internal memory requirements for refinement
    Refinement block size limited to 1024 samples
    Calculate internal memory to avoid accessing pre-fetch cache again for MC
Base method was constrained to not have refinement for CUs with luma sample count greater than 1024 in CE9.2.6 from L-meeting (JVET-L0173)
CE9.2.1 studies the following:
  Impact of the type of interpolation used for refinement
    Nearest rounded integer grid samples (Integer-DMVR)
    Bilinear MC at 1/16th of a pel accuracy with 10-bit accuracy (BiMC-DMVR)
  Impact of cost function
    SAD vs. Block mean removed SAD (B-MR-SAD)
  Impact of using refined MVs for purposes other than current CU’s MC
    CTU-level pipeline
    VPDU-level pipeline
  Impact of force splitting a CU into sub-Pus
    32 width, 32 height vs. 16 width, 16 height

## Slide 6: Results
Simulation results are presented in CE9.2.1g that uses 16x16 sub-PU size with the earlier search pattern replaced by the proposed search pattern
The proposed 13-position refinement has only a 0.08% BDRATE drop when compared to the 25-position refinement
  Performing evaluation at all 13 positions as compared to only 5+5=10 has only a 0.06% BDRATE drop

## Slide 7: Interpolation for refinement
Bilinear interpolation was proposed in JVET-K0041 and JVET-K0359
  1/16th of a pel accurate interpolation requires 10-bit x 4-bit multiplications
Earlier version was using 14-bit intermediate bit-depth after both the horizontal and vertical interpolations implying that vertical interpolations require 14-bit x 4-bit multiplication
In CE9.2.1d, the bilinear interpolation was changed to happen with 10-bit intermediate bit depth after both stages of interpolation
  40% additional multiplications and additions when compared to bi-pred 8x8 MC
Integer DMVR as proposed in JVET-K0275 uses only nearest integer grid samples to avoid the interpolation complexity, but loses ~0.15% when DMVR is employed without BIO and ~0.12% when DMVR is employed with BIO
A simpler interpolation for refinement that eliminates any need for multiplications while retaining most of the compression gains of bilinear MC at 1/16th of a pel precision is desired

## Slide 8: Proposed Multiplication-free Interpolation
Quarter pel accuracy is used when 1-D interpolation only is required
  (3*a + b + 1)>>1 can be computed as ((a<<1) + a + b + 1)>>1
Half-pel accuracy in both H and V is used when 2-D interpolation is required
  > 4/16 AND <12/16 in both H and V sub-pixel positions
  Interpolation is computed as (a + b + c + d + 2)>>2
The multiplications are thus eliminated and even the additions are slightly reduced as rounding after horizontal interpolation is eliminated.
motion
vector
Integer sample coordinate
Half sample coordinate
Rounded motion vector
Horizontal Quarter-pel sample coordinate
Vertical Quarter-pel sample coordinate
motion vector
Integer sample coordinate
Half sample coordinate
Rounded motion vector
Horizontal Quarter-pel sample coordinate
Vertical Quarter-pel sample coordinate

## Slide 9: Results
Results are presented when the bilinear interpolation with 1/16th of a pel accuracy in CE9.2.1g is replaced with the proposed interpolation
Compared to the 0.12% BDRATE drop that integer DMVR incurs, the proposed interpolation has only a 0.04% BDRATE drop.

## Slide 10: Supplemental Result
Using the proposed interpolation along with SAD as the cost function to facilitate a row-level pipeline, the results are as follows:
Compared to using B-MR-SAD, using SAD as the cost function in this case, has a 0.07% additional BD-RATE drop. However, SAD simplifies the cost evaluation unit and facilitates row level pipeline that reduces internal memory requirement.

## Slide 11: Results with both proposed elements
The two elements together have an overall 0.11% BDRATE drop over CE9.2.1g results

## Slide 12: Complexity Analysis
To avoid access of data accessed by DMVR from pre-fetch cache from being accessed again, the internal memory requirement is:
  2 x (sub-PU-w + 4 + 7) x (sub-PU-h + 5) 10-bit samples
    For sub-PU-w=16, sub-PU-h=16, this becomes 2 x 27 x 21 10-bit samples
When using SAD or PR-MR-SAD, DMVR requires only 2 x 5 x (sub-PU-w + 4) 10-bit interpolated sample buffers for cost evaluations
Proposed 13-point rhombus with alternate row cost reduces the number of concurrent row-level cost evaluation units to 7 (from 25)
Proposed interpolation for refinement eliminates the need for multiplications and the additions required in the worst-case are around 28% of the additions required for 8x8 bi-pred MC using DCTIF

## Slide 13: Conclusions
2 simplifications to DMVR are proposed
  First simplification relates to restricting the number of integer distance refinement positions to 13 (from 25)
    Enables reduced gate count (7 row-level cost evaluation units) and reduced internal memory
    Has only a 0.08% BDRATE drop when compared to the square shaped 25 refinement positions
    Software average decoding time advantage is retained with a 2-stage normative cost evaluation
  Second simplification relates to making the interpolation performed for refinement multiplication-free
    Achieved by using half-pel 2-D or quarter-pel 1-D interpolation
    Has only a 0.04% BDRATE drop (as opposed to 0.12% drop that integer DMVR has)
  Combined result of both simplifications shows 0.11% BDRATE drop
It is requested that DMVR with these simplifications be adopted into the next VTM as they significantly reduce the hardware complexity of DMVR

## Slide 14: THANKS TO HISILICON FOR CROSS-CHECKING THE RESULTS!