## Slide 1
CE7-related:
Unified rice parameter derivation
for bypass level coding
Samsung Research
Yinji Piao
JVET-M0198

## Slide 2: Coefficient coding in VTM3.0
Binarization and Sub-block coding order
  for( k … ) { // 1st pass, max 28 bins
    sig_flag[ k ]
    if( sig_flag[ k ] ) {
    gt1_flag[k]
    if( gt1_flag[ k ] )
    par_flag[ k ]
    }}
    for( k … ) { // 2nd pass, max 4 bins
    if( gt1_flag[ k ] )
    gt3_flag[ k ]
    }
    for( k …k1 ) { // 3rd pass (EP bins)
    if(gt2_flag[k])
    remainder[ k ] // baseLevel = 4
    }
    for( k1-1 … k2) { // 4th pass (EP bins)
    if(gt1_flag[k])
    remainder[ k ] // baseLevel = 2
    }
    for( k2-1 … 0) { // 5th pass (EP bins)
    Abs_level[ k ] // baseLevel = 0
    }
if( ricePar < 3 && rem > (3<<ricePar)-1 )
{
ricePar++;
}
if( ricePar < 3 && rem > (3<<ricePar)-1 )
{
ricePar++;
}
ricePar = riceParTable[sumAbsLevel]
where sumAbsLevel = sum of absolute neighboring
5 coeffs.
HEVC-like
JEM-like
Rice Para derivation
HEVC-like

## Slide 3: Proposed method
Unified solution for rice parameter derivation
    for( k …k1 ) { // 3rd pass
    if(gt3_flag[k])
    remainder[ k ]
    }
    for( k1-1 … k2) { // 4th pass
    if(gt1_flag[k])
    remainder[ k ]
    }
    for( k2-1 … 0) { // 5th pass
    Abs_level[ k ]
    }
ricePar = riceParTable[sumAbsLevel]
where sumAbsLevel = relative sum of AbsLevel (neighboring 5 coeffs)
, baseLevel = 0
Rice Para derivation
ricePar = riceParTable[sumAbsLevel]
where sumAbsLevel = relative sum of AbsLevel (neighboring 5 coeffs)
, baseLevel = 2
ricePar = riceParTable[sumAbsLevel]
where sumAbsLevel = relative sum of AbsLevel (neighboring 5 coeffs)
, baseLevel = 4
Current: sumAbsLevel = min (sum, 31)
Proposed: sumAbsLevel = max(min(sum – 5 x baseLevel, 31), 0)

## Slide 4: Proposed method
Unified solution for rice parameter derivation
  More robust for parallel processing
    Enables parallel derivation of rice parameters for the positions locate on the same diagonal line for each 4x4 subblock
Current position
Neighboring positions for sumAbsLevel
Positions for parallel derivation of rice para

## Slide 5: Experimental result
Unified solution with JEM-like vs HEVC-like scheme
HEVC-like (prev)
JEM-like (template)
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.16% | 0.08% | 0.22% | 100% | 96% | 0.70% | 0.60% | 0.77% | 102% | 104%
Class A2 | 0.31% | 0.38% | 0.32% | 99% | 95% | 0.62% | 0.63% | 0.65% | 101% | 101%
Class B | 0.24% | 0.28% | 0.25% | 100% | 98% | 0.64% | 0.63% | 0.60% | 101% | 103%
Class C | 0.18% | 0.21% | 0.14% | 101% | 99% | 0.47% | 0.54% | 0.38% | 100% | 102%
Class E | 0.15% | 0.12% | 0.20% | 100% | 99% | 0.55% | 0.50% | 0.64% | 100% | 104%
Overall | 0.21% | 0.22% | 0.23% | 100% | 98% | 0.60% | 0.58% | 0.59% | 101% | 103%
Class D | 0.21% | 0.29% | 0.19% | 101% | 99% | 0.55% | 0.63% | 0.67% | 100% | 102%
Class F (optional) | 0.37% | 0.35% | 0.38% | 100% | 99% | 0.37% | 0.42% | 0.43% | 100% | 103%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.09% | 0.12% | 0.18% | 96% | 92% | 0.42% | 0.56% | 0.51% | 101% | 101%
Class A2 | 0.12% | 0.22% | 0.21% | 96% | 92% | 0.27% | 0.53% | 0.49% | 101% | 103%
Class B | 0.13% | 0.13% | 0.17% | 99% | 97% | 0.37% | 0.64% | 0.39% | 101% | 102%
Class C | 0.11% | 0.20% | 0.21% | 100% | 99% | 0.30% | 0.36% | 0.38% | 102% | 105%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.12% | 0.16% | 0.19% | 98% | 96% | 0.34% | 0.53% | 0.43% | 101% | 103%
Class D | 0.08% | -0.26% | -0.07% | 99% | 98% | 0.27% | 0.08% | 0.16% | 101% | 102%
Class F (optional) | 0.23% | 0.27% | 0.21% | 100% | 99% | 0.30% | 0.39% | 0.36% | 101% | 103%

## Slide 6: Experimental result
Proposed unified solution
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0_lowQP |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.06% | 0.06% | 101% | 100% | -0.02% | -0.05% | 0.01% | 108% | 112%
Class A2 | 0.01% | 0.02% | 0.00% | 102% | 100% | -0.01% | -0.01% | -0.01% | 109% | 110%
Class B | 0.00% | -0.01% | 0.01% | 102% | 101% | -0.02% | -0.01% | -0.04% | 104% | 110%
Class C | 0.00% | -0.04% | -0.05% | 102% | 102% | 0.00% | -0.01% | -0.03% | 102% | 102%
Class E | 0.00% | 0.03% | 0.05% | 101% | 101% | -0.05% | -0.02% | -0.03% | 101% | 100%
Overall | 0.00% | -0.01% | 0.01% | 102% | 101% | -0.02% | -0.02% | -0.02% | 105% | 107%
Class D | -0.02% | 0.02% | 0.02% | 102% | 101% | -0.03% | 0.03% | -0.01% | 101% | 101%
Class F (optional) | 0.10% | 0.23% | 0.25% | 102% | 102% | 0.20% | 0.19% | 0.28% | 102% | 100%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3.0_lowQP |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.05% | 0.10% | 100% | 100% | -0.01% | 0.03% | 0.07% | 110% | 114%
Class A2 | -0.01% | 0.01% | 0.10% | 101% | 102% | 0.00% | 0.01% | 0.06% | 109% | 113%
Class B | -0.02% | 0.12% | -0.04% | 101% | 101% | 0.00% | 0.08% | 0.00% | 102% | 107%
Class C | 0.00% | -0.09% | 0.05% | 102% | 103% | -0.01% | -0.04% | -0.01% | 100% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.01% | 0.03% | 0.04% | 101% | 101% | -0.01% | 0.02% | 0.02% | 104% | 107%
Class D | -0.02% | -0.25% | -0.17% | 101% | 101% | -0.01% | 0.03% | 0.11% | 101% | 101%
Class F (optional) | 0.17% | 0.20% | 0.12% | 100% | 100% | 0.11% | 0.14% | 0.17% | 101% | 100%
Proposed @ lowQP
Proposed @ CTC

## Slide 7: Comparison
Bypass coded level | Current Rice parameter derivation | Unified rice parameter derivation
Third pass (bypass coding of remainder, base_level=4) for(k=startScanIdx; k<startIdx2; k++) { if( gt2_flag[ k ] != 0 ) { decode remainder[k] coeff[k] = coeff[k] + 2 * remainder[k] } } | if(ricePar < 3 && rem > (3<<ricePar)-1) { ricePar++; } | riceParTable[ max(min( 31, sumAbs – base_level*5 ), 0) ] , where base_level = 4
Third pass (bypass coding of remainder, base_level=2) for(k=startIdx2; k<startIdxBypass; k++) { if( gt1_flag[ k ] != 0 ) { decode remainder[k] coeff[k] = coeff[k] + 2 * remainder[k] } } | if(ricePar < 3 && rem > (3<<ricePar)-1) { ricePar++; } | riceParTable[ max(min( 31, sumAbs – base_level*5 ), 0) ] , where base_level = 2
Fourth pass (bypass coding of complete coefficients) for(k=startIdxBypass; k<=endScanIdx; k++) { decode absLevel[k] coeff[k] = absLevel[k] } | riceParTable[ min( 31, sumAbs ) ] | riceParTable[ max(min( 31, sumAbs – base_level*5 ), 0) ] where base_level = 0

## Slide 8: Conclusion
Unified solution for remaining level and fully bypass-coded level coding
No performance decrease
More robust for parallel processing