## Slide 1: CE4-related: MMVD improvements (JVET-M0206)
Jan., 2019
Seungsoo Jeong, Min Woo Park and Kiho Choi (Samsung)
JVET 13th Meeting

## Slide 2: Introduction
Motivation
  MMVD’s distance list index is signalled using truncated unary coding method.
  Current distance list index’s binarization method has an advantage in small distance index.
Table 1. Distance list index binarization
Distance list index | binarization
0 | 0
1 | 10
2 | 110
3 | 1110
4 | 11110
5 | 111110
6 | 1111110
7 | 1111111

## Slide 3: Proposed method 1
Method 1: only binarization method change
  Proposed binarization method has an advantage at small and large distance.
  There is no additional syntax and CTX model.
Table 2. The result of method 1
Distance list index | binarization
0 | 00
1 | 01
2 | 10
3 | 110
4 | 1110
5 | 11110
6 | 111110
7 | 111111

## Slide 4: Proposed method 2
Method 2: one more CTX model with Method 1
  In this method, one more context model is used on top of Method 1
  If first bin is ‘1’, second bin uses context model for better performance.
Table 3. The result of method 2
Distance list index | binarization
0 | 00
1 | 01
2 | 10
3 | 110
4 | 1110
5 | 11110
6 | 111110
7 | 111111

## Slide 5: Proposed method 3
Method 3: CTX initial value change with Method 1
  In this method, the context initial value of Method 1 is changed to 154.
Table 4. The result of method 3
Distance list index | binarization
0 | 00
1 | 01
2 | 10
3 | 110
4 | 1110
5 | 11110
6 | 111110
7 | 111111

## Slide 6: Result
RA | Y | U | V | Enc. | Dec. | LD | Y | U | V | Enc. | Dec.
Test 1 | -0.08% | -0.09% | -0.12% | 102% | 103% | Test 1 | 0.01% | -0.14% | 0.00% | 100% | 101%
Test 2 | -0.10% | -0.13% | -0.14% | 100% | 99% | Test 2 | 0.01% | 0.05% | -0.05% | 99% | 98%
Test 3 | -0.08% | -0.06% | -0.11% | 100% | 99% | Test 3 | 0.02% | -0.13% | -0.19% | 98% | 98%

## Slide 7: Conclusion
Proposed binarization method in distance list index has an advantage at small and large distance.
0.08% gain in RA from only binarization change.
The adoption of this binarization method change (Test 1) on VVC software is requested.
We thank SHARP for cross-checking.

## Slide 8
Thank you

## Slide 9: Result
Method 1 : only binarization method change

## Slide 10: Result
Method 2 : one more CTX model with Method 1

## Slide 11: Result
Method 3 : CTX initial value change with Method 1