## Slide 1: CE3-related: Partial reference sample range for MDLM (JVET_M0212)
Reporter： Junyan Huo, Shuai Wan

## Slide 2: Introduction
JVET_M0212
The current VVC adopts the multi-directional LM (MDLM) mode, including LM_A and LM_L modes.
Figure 1: LM_A mode
Figure 2: LM_L mode
Figure 2: LM_L mode

## Slide 3: The proposed method
JVET_M0212
Partial reference sample range is used for MDLM:
Figure 3: LM_A mode with 3/4 reference samples range
Figure 4: LM_L mode with 3/4 reference samples range

## Slide 4: Results of the proposed method
JVET_M0212
Test1:
Anchor: VTM3.0
Tested: The proposed method in MDLM
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.14% | -0.33% |  | 99%
Class A2 | -0.01% | -0.05% | -0.04% |  | 99%
Class B | -0.01% | -0.17% | -0.21% |  | 99%
Class C | -0.03% | -0.11% | -0.27% |  | 100%
Class E | -0.01% | -0.02% | 0.01% |  | 100%
Overall | -0.02% | -0.11% | -0.18% |  | 99%
Class D | -0.01% | -0.06% | -0.12% |  | 100%
Class F | 0.00% | 0.03% | -0.09% |  | 100%

## Slide 5: Results of the proposed method
JVET_M0212
Test2:
Anchor: VTM3.0
Tested: The proposed method combined with JVET_M0211
 | All Intra Main10 |  |  |  | 
 | Over VTM 3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.12% | -0.51% | -0.54% |  | 99%
Class A2 | -0.03% | -0.21% | -0.11% |  | 100%
Class B | -0.04% | -0.36% | -0.59% |  | 100%
Class C | -0.08% | -0.23% | -0.43% |  | 99%
Class E | -0.03% | -0.07% | -0.13% |  | 99%
Overall | -0.06% | -0.28% | -0.39% |  | 99%
Class D | -0.04% | -0.21% | -0.14% |  | 98%
Class F | -0.05% | -0.11% | -0.21% |  | 100%

## Slide 6
Thank you.