## Slide 1: JVET-M0224 CE10-related: Local Illumination Compensation simplifications
Saurav Bandyopadhyay, Xiaoyu Xiu, Yuwen He
InterDigital Inc.
January, 2019

## Slide 2: Introduction
The LIC design in the CE10.5.2/JEM
  Is used to compensate for illumination changes at motion compensation stage that exists in between the temporal reference blocks and current block based on a linear model
  LIC parameter e.g. scaling factor and the offset are separately estimated for each individual reference list L0 and L1 for each of the two prediction blocks
  Bi-predictive weighted average (BPWA) weights provided for each of the two illumination compensated prediction blocks for the bi-prediction are used to combine the prediction templates
  BPWA is applied after LIC: applying weighted averaging on the prediction generated by LIC
  The complexity of LIC for bi-prediction is high: LIC parameters and application for two times
  Simplified LIC for bi-prediction
  BPWA applied first followed by LIC on bi-directional prediction signal
    First performs the BPWA to the template samples from two prediction lists to produce the bi-prediction template reference samples
    LIC parameters are estimated using the BPWA based bi-prediction template reference samples and the template samples of current CU
  Disable LIC for ATMVP sub-block merge mode

## Slide 3: Proposed LIC simplification for bi-prediction
LIC is applied after BPWA
Benefit: One time LIC parameter estimation and application for bi-prediction

## Slide 4: Experimental results
4
© 2018 InterDigital, Inc. All Rights Reserved.
Anchor: VTM-3.0
 | RA: Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.12% | -0.67% | -1.03% | 146% | 99%
Class A2 | -0.41% | -0.18% | -0.28% | 124% | 101%
Class B | -0.65% | -0.23% | -0.32% | 130% | 99%
Class C | -0.39% | -0.40% | -0.31% | 137% | 101%
Class E |  |  |  |  | 
Overall | -0.63% | -0.35% | -0.45% | 134% | 100%
Class D | -0.08% | -0.14% | -0.03% | 133% | 102%
Class F (optional) | -1.08% | -0.76% | -0.71% | 130% | 101%
LB: Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.83% | -0.83% | -0.89% | 144% | 98%
-0.56% | -0.56% | -0.74% | 157% | 99%
-0.07% | -0.21% | -0.03% | 105% | 101%
-0.55% | -0.58% | -0.62% | 137% | 99%
-0.19% | -0.37% | -0.50% | 147% | 103%
-2.93% | -1.70% | -2.20% | 146% | 99%

## Slide 5: Experimental results (cont.)
5
© 2018 InterDigital, Inc. All Rights Reserved.
Anchor: CE-10.5.2
 | RA: Over CE-10.5.2 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.16% | -0.07% | -0.13% | 99% | 99%
Class A2 | -0.03% | -0.04% | -0.06% | 99% | 100%
Class B | -0.05% | -0.01% | -0.07% | 100% | 100%
Class C | -0.04% | -0.06% | -0.08% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.07% | -0.04% | -0.09% | 99% | 100%
Class D | -0.03% | -0.10% | 0.11% | 100% | 100%
Class F (optional) | -1.08% | -0.76% | -0.71% | 130% | 101%
LB: Over CE-10.5.2 |  |  |  | 
Y | U | V | EncT | DecT
-0.06% | 0.02% | -0.09% | 100% | 97%
-0.07% | -0.34% | -0.21% | 100% | 97%
0.01% | -0.16% | 0.24% | 100% | 98%
-0.04% | -0.15% | -0.04% | 100% | 97%
-0.08% | 0.07% | -0.10% | 100% | 101%
-2.93% | -1.70% | -2.20% | 146% | 99%

## Slide 6: Summary
Proposal simplified LIC method to reduce complexity of LIC for the bi-prediction
  Parameter estimation: generates bi-prediction reference samples of the template samples for current block and estimate the LIC parameters once
  LIC application process: only applied LIC once
LIC is not effective for ATMVP sub-block mode, and it is proposed to be disabled
Thanks to Technicolor for cross-checking (JVET-M0714)